## Slide 1: Use of [Ramp] in IBIS 4.1
Lynne Green

## Slide 2: Topics
History of [Ramp]
[Ramp] use in EDA tools
[Ramp] with differential models
[Ramp] with external models
[Ramp] in IBIS 4.1

## Slide 3: History of [Ramp]
[Ramp] dates back to IBIS 1.0
[Ramp] use and derivation
  Linear V-t
  Rload to Vcc or Gnd
  ECL: Rload is 50 Ohms to -2V
IBIS added V-t tables later
  Real transitions are not linear (or even monotonic)
  Still a required keyword (back compatibility)

## Slide 4: [Ramp] use in EDA tools
[Ramp] used in simulation only if no V-t tables
[Ramp] is still used by EDA tools
  Used in pre-simulation algorithms
  Initial simulation time step (dt)
  Estimating crosstalk (dt, Vcc or dV)
Valid dV and dt are needed in models!
  Rload is not a critical parameter
  As long as Rload is a typical load

## Slide 5: [Ramp] use in EDA tools
EDA tools do not require full-swing I/O
Any “normal” loading is OK for most EDA tools
  Use 20% to 80% voltage swing into “normal” load
  Load under the actual expected operating conditions
  Example: standard for LVDS gives normal loading
EDA tools have robust code for [Ramp]
  Ideal solution uses existing code

## Slide 6: [Ramp] with differential models
“Normal” load is differential
  Rload to Vcc or Gnd might not make sense
Signals usually not rail-to-rail
  Still use 20% to 80% voltage swing
  Works for both current- and voltage-mode drivers
Helpful to add comments in model about the actual load
  | Rload of 100ohms between the LVDS output pins.

## Slide 7: [Ramp] with external models
More complex driver circuit designs
  Programmable or time-varying slew rate
  Pre-emphasis, multi-level logic, etc.
More complex terminations
  Programmable termination
  Termination not purely resistive (RC network)
SPICE and AMS models in external files
  No information in the external files on dt

## Slide 8: [Ramp] with external models
EDA tools use dt to estimate time step
  [Ramp] is already (mis-)applied as needed today
  Sometimes with a comment on the actual load
Logistics: Where to put the information in IBIS 4.1?
  SI tool simulates to get dV and dt
    What load and time-step?
    Where to store dV and dt?
  New keyword or subparameter
    [Ramp] already contains all of the needed information
  [Ramp] with broader definition of load

## Slide 9: [Ramp] in IBIS 4.1
Why keep it as a required keyword?
  EDA tools need dt, could use dV
  Could make Rload optional
Is this data readily available?
  On the datasheet for the I/O buffer
  From the transistor-level simulation results
  From measured test-bench data

## Slide 10: [Ramp] in IBIS 4.1
BIRD 85: Slew Time Estimate Clarifications
*| Note that when using [External Model], the [Ramp] keyword is
*| intended to provide EDA tools with a quick first-order
*| estimate of driver slew characteristics. Therefore, data for
*| [Ramp] may be measured using a load that conforms to the
*| driver's intended operation, rather than the load recommended
*| in Section 9: Notes on Data Derivation Method.

## Slide 11
[Model] ExBufferSPICE
Model_type I/O
Vinh = 2.0
Vinl = 0.8
[Voltage Range] 3.3 3.0 3.6
[Ramp]
dV/dt_r 1.57/0.36n 1.44/0.57n 1.73/0.28n
dV/dt_f 1.57/0.35n 1.46/0.44n 1.68/0.28n
|
[External Model]
Language SPICE
Corner Typ buffer_typ.spi buffer_io_typ
...

## Slide 12
Thanks to all who contributed to the discussion:
John Angulo, Bob Ross, Michael Mirmak, Stephen Peters, and all of the other IBIS Open Forum participants.