## Slide 1
An ICM Example Using a Semiconductor Device Package
By
Michael Mirmak
Intel Corporation
IBIS Summit at PCB East 2003
October 21, 2003
Thanks to Kelly Green for data testing assistance

## Slide 2: Agenda
ICM Status
BGA Package Structure
Package Modeling in IBIS 4.x
A 4.x Package Example
An ICM 1.0 Example Using a BGA Design
ICM Advantages
Areas for Improvement
Data Issues
Questions and Free Discussion

## Slide 3: ICM Status
ICM = IBIS Interconnect Modeling Specification
Version 1.0 approved September 12, 2003
Final documents posted October 1, 2003:
http://www.eda.org/pub/ibis/icm_ver1.0/
Development of a parser in progress
  Code about 25% completed
  Alpha test version expected early November

## Slide 4
Package modeling: a direct application of ICM…
BGA (Ball Grid Array) Package structure
  Five-part path
    Bond wire (usually gold) – connects die pad to substrate
    Package trace – routing path in substrate
    Via – connects trace to solder ball
    Solder ball – attach point for device to PCB
    Plating par – stub left from separation of packages during manufacturing
die pad
bond wire
package trace
plating bar
solder ball
via
BGA Package Structure
drawing courtesy A. Muranyi
Notes: <number>
<footer>
<header>
07/29/26

## Slide 5
Package modeling in IBIS 4.x
[Package] keyword
  Required for each component
  Contains typical (optionally minimum and maximum) values for
  R_pkg, L_pkg and C_pkg
[Pin] keyword
  Each pin can have a distinct R_pin, L_pin or C_pin value
  Overrides the values under the [Package] keyword
  Only a single value can be used (no corners)
[Package Model] keyword
  Can reference an external file or [Define Package Model] within the same .IBS file
  Overrides the values under the [Package] keyword
  Two methods possible currently
    coupled, single-lump RLC matrix description
    (full, banded, and sparse matrix formats available)
    uncoupled multi-section description using RLC, length
[Alternate Package Model] keyword
Adapted from A. Muranyi, “Introduction to IBIS Models and IBIS Model Making”

## Slide 6
die pad
bond wire
package trace
plating bar
solder ball
via
|********************************************
|
[Define Package Model] BGA example
[Manufacturer] Noname Corp.
[OEM] Noname Corp.
[Description] BGA
[Number Of Sections] 5
[Number Of Pins] 3
[Pin Numbers]
|
A1 Len=0 R=0.160 L=5.0n / | bond wire
Len=4.00 L=0.170n C=0.250p / | package trace
Fork
Len=0.80 L=0.200n C=0.100p / | plating bar
Endfork
Len=0.010 L=0.010n C=0.020p / | via
Len=0 C=2.0p / | Ball 1
|
A2 Len=0 R=0.160 L=5.0n / | bond wire
Len=2.50 L=0.170n C=0.250p / | package trace
Fork
Len=0.80 L=0.200n C=0.100p / | plating bar
Endfork
Len=0.010 L=0.010n C=0.020p / | via
Len=0 C=2.0p / | Ball 2
|
A3 Len=0 R=0.160 L=5.0n / | bond wire
Len=4.00 L=0.170n C=0.250p / | package trace
Fork
Len=0.80 L=0.200n C=0.100p / | plating bar
Endfork
Len=0.010 L=0.010n C=0.020p / | via
Len=0 C=2.0p / | Ball 3
| The resistance matrix for this package has
| no coupling
|
[Resistance Matrix] Banded_matrix
[Bandwidth] 0
[Row] 1
10.0
[Row] 2
15.0
[Row] 3
15.0
|
[Inductance Matrix] Full_matrix
[Row] 1
3.04859e-07 4.73185e-08 1.3428e-08
[Row] 2
3.04859e-07 4.73185e-08
[Row] 3
3.04859e-07
|
|
[Capacitance Matrix] Sparse_matrix
[Row] 1
A 4.x Package Example
Notes: <number>
<footer>
<header>
07/29/26

## Slide 7: An ICM 1.0 Example
Assumptions:
  BGA device package, five-part path
  Differential interface, 90 Ω diff. impedance
  RLGC nodal structure
Other details
  Package designed using Cadence* tools (MCM format)
  Electrical data extracted using Ansoft* tools into lumped matrix and distributed HSPICE* W-element format (not tabular frequency)
  Sections extracted as pairs or pair-of-pairs

## Slide 8: An ICM 1.0 Example
  |**************************************************************************
  | The following example corresponds to a BGA wirebond package
  |**************************************************************************
  [Begin Header]
  [ICM Ver] 1.0
  [File Rev] 1.1
  [File Name] bga_example.icm
  [Date] 10/15/2003
  [Source] From SPICE model data
  [Notes] This is an example wirebond BGA package model.
  [Disclaimer] This model is provided as an example only.
  [Copyright] ---
  [Support] http://www.yourcompanyhere.com
  [Redistribution] Yes
  [End Header]
  |
  |**************************************************************************
  |
  [Begin ICM Family] Wirebond_Package
  [Manufacturer] Noname
  [ICM Family Description] A wirebond BGA package design
  |
  |**************************************************************************
  |
  [ICM Model List]
  | Name Mating Min_Slew_Time Image
  |----------------------------------------------------------------------------
  diff-two-pair-short-TRL Mated 1000ps
  diff-two-pair-mid-TRL Mated 1000ps
  diff-two-pair-long-TRL Mated 1000ps
  |
  | wirebond TRL via ball
  |Die_side >--------< >---< >---< >--------< Ball_side
  | |
  | |platingbar

## Slide 9: An ICM 1.0 Example
  |**************************************************************************
  |Units below assumed to be meters
  |
  [Begin ICM Model] diff-two-pair-short-TRL
  ICM_model_type MLM
  [Nodal Path Description]
  Model_nodemap Die_side
  N_section (A1 A2 A3 A4 11 12 13 14 ) Mult=1 wirebond
  N_section (11 12 13 14 21 22 23 24 ) Len=1.0e-3 TRL
  N_section (21 22 31 32 ) Mult=1 via
  N_section ( 23 24 33 34 ) Mult=1 via
  N_section (31 32 x1 x2 ) Len=1.0e-3 platingbar
  N_section ( 33 34 x3 x4 ) Len=1.0e-3 platingbar
  N_section (31 32 B1 B2 ) Mult=1 ball
  N_section ( 33 34 B3 B4 ) Mult=1 ball
  Model_nodemap Ball_side
  [End ICM Model]
  |
  [Begin ICM Model] diff-two-pair-mid-TRL
  ICM_model_type MLM
  [Nodal Path Description]
  Model_nodemap Die_side
  N_section (A1 A2 A3 A4 11 12 13 14 ) Mult=1 wirebond
  N_section (11 12 13 14 21 22 23 24 ) Len=2.5e-3 TRL
  N_section (21 22 31 32 ) Mult=1 via
  N_section ( 23 24 33 34 ) Mult=1 via
  N_section (31 32 x1 x2 ) Len=1.0e-3 platingbar
  N_section ( 33 34 x3 x4 ) Len=1.0e-3 platingbar
  N_section (31 32 B1 B2 ) Mult=1 ball
  N_section ( 33 34 B3 B4 ) Mult=1 ball
  Model_nodemap Ball_side
  [End ICM Model]
  |

## Slide 10: An ICM 1.0 Example
  [Begin ICM Model] diff-two-pair-long-TRL
  ICM_model_type MLM
  [Nodal Path Description]
  Model_nodemap Die_side
  N_section (A1 A2 A3 A4 11 12 13 14 ) Mult=1 wirebond
  N_section (11 12 13 14 21 22 23 24 ) Len=4.0e-3 TRL
  N_section (21 22 31 32 ) Mult=1 via
  N_section ( 23 24 33 34 ) Mult=1 via
  N_section (31 32 x1 x2 ) Len=1.0e-3 platingbar
  N_section ( 33 34 x3 x4 ) Len=1.0e-3 platingbar
  N_section (31 32 B1 B2 ) Mult=1 ball
  N_section ( 33 34 B3 B4 ) Mult=1 ball
  Model_nodemap Ball_side
  [End ICM Model]
  |
  |**************************************************************************
  |
  [ICM Node Map] Die_side
  | pin node name
  1 A1 Die_Pair1_P
  2 A2 Die_Pair1_N
  3 A3 Die_Pair2_P
  4 A4 Die_Pair2_N
  [ICM Node Map] Ball_side
  | pin node name
  1 B1 Ball_Pair1_P
  2 B2 Ball_Pair1_N
  3 B3 Ball_Pair2_P
  4 B4 Ball_Pair2_N
  [End ICM Family]
  |

## Slide 11: An ICM 1.0 Example
  |**************************************************************************
  [Begin ICM Section] TRL
  [Derivation Method] Distributed
  | Note - resistance and conductance data taken at DC
  [Resistance Matrix] Full_matrix
  [Row] 1
  12.88360411759953 0.1122120358629589 0.1122120358629535 0.1122120358629596
  [Row] 2
  12.88360411759959 0.1122120358629578 0.1122120358629697
  [Row] 3
  12.88360411759938 0.1122120358630265
  [Row] 4
  12.88360411759949
  [Inductance Matrix] Full_matrix
  [Row] 1
  4.762471117800315e-007 1.574556825167307e-007 4.166419413304077e-008 2.533102103479589e-008
  [Row] 2
  4.746270568634125e-007 7.829217743956544e-008 4.167732136295897e-008
  [Row] 3
  4.74695722999582e-007 1.575422041099422e-007
  [Row] 4
  4.764080626393532e-007
  [Capacitance Matrix] Full_matrix
  [Row] 1
  1.13724568263412e-010 -3.699327364720182e-011 -3.195922952611326e-012 -1.703330485507162e-012
  [Row] 2
  1.161253452991748e-010 -1.420237001727346e-011 -3.194945464961537e-012
  [Row] 3
  1.160998680089507e-010 -3.698488552069936e-011
  [Row] 4
  1.135869774794572e-010
  [Conductance Matrix] Diagonal_matrix
  0
  0
  0
  0
  [End ICM Section] TRL

## Slide 12: An ICM 1.0 Example
  |**************************************************************************
  [Begin ICM Section] platingbar
  [Derivation Method] Distributed
  | Note - resistance and conductance data taken at DC
  [Resistance Matrix] Full_matrix
  [Row] 1
  6.447272395548234 0.06157635467979937
  [Row] 2
  6.447272395547882
  [Inductance Matrix] Full_matrix
  [Row] 1
  3.875774956956585e-007 1.453875900301228e-007
  [Row] 2
  3.876372566358464e-007
  [Capacitance Matrix] Full_matrix
  [Row] 1
  1.228751177567252e-010 -4.55112340759e-011
  [Row] 2
  1.228294743230235e-010
  [Conductance Matrix] Diagonal_matrix
  0
  0
  [End ICM Section] platingbar

## Slide 13: An ICM 1.0 Example
  |**************************************************************************
  [Begin ICM Section] ball
  [Derivation Method] Lumped
  | Note - resistance and conductance data taken at DC
  [Resistance Matrix] Full_matrix
  [Row] 1
  0.00122974 5.92605e-005
  [Row] 2
  0.00121302
  [Inductance Matrix] Full_matrix
  [Row] 1
  3.91849e-011 4.81629e-012
  [Row] 2
  4.0174e-011
  [Capacitance Matrix] Full_matrix
  [Row] 1
  3.99986e-014 -5.64816e-015
  [Row] 2
  3.84177e-014
  [Conductance Matrix] Diagonal_matrix
  0
  0
  [End ICM Section] ball

## Slide 14: An ICM 1.0 Example
  |**************************************************************************
  [Begin ICM Section] wirebond
  [Derivation Method] Lumped
  | Note - resistance and conductance data taken at DC
  [Resistance Matrix] Full_matrix
  [Row] 1
  0.357348 0.0153167 0.000203431 0.0
  [Row] 2
  0.360486 0.00520121 0.000603478
  [Row] 3
  0.358009 0.0157098
  [Row] 4
  0.356194
  [Inductance Matrix] Full_matrix
  [Row] 1
  3.12277e-009 1.01577e-009 3.05886e-010 2.22836e-010
  [Row] 2
  3.02065e-009 4.47214e-010 2.93897e-010
  [Row] 3
  2.99636e-009 9.45824e-010
  [Row] 4
  3.01787e-009
  [Capacitance Matrix] Full_matrix
  [Row] 1
  4.03601e-013 -1.28769e-013 -1.50353e-014 -8.75617e-015
  [Row] 2
  4.19554e-013 -3.78802e-014 -1.42581e-014
  [Row] 3
  4.16062e-013 -1.22606e-013
  [Row] 4
  4.06634e-013
  [Conductance Matrix] Diagonal_matrix
  0
  0
  0
  0
  [End ICM Section] wirebond

## Slide 15: An ICM 1.0 Example
  |**************************************************************************
  [Begin ICM Section] via
  [Derivation Method] Lumped
  | Note - resistance and conductance data taken at DC
  [Resistance Matrix] Full_matrix
  [Row] 1
  0.00301846 0.000640491
  [Row] 2
  0.00304867
  [Inductance Matrix] Full_matrix
  [Row] 1
  6.42506e-011 2.56352e-011
  [Row] 2
  5.96354e-011
  [Capacitance Matrix] Full_matrix
  [Row] 1
  4.81705e-013 -8.01111e-014
  [Row] 2
  4.89624e-013
  [Conductance Matrix] Diagonal_matrix
  0
  0
  [End ICM Section] via
  |**************************************************************************
  |
  [End]

## Slide 16: ICM 1.0 Advantages
Each section can be independently modeled
  If nodal scheme used, the number of paths in each section does not need to match that of any other section
Coupling can be represented directly per section
  Per-section coupling missing in IBIS PKG
  ICM is a major enhancement
Conductance is added as a parameter
  IBIS PKG RLC -> ICM RLGC
ICM data format very cleanly converts other matrix data formats
  Conversion can be scripted
  Lower- vs. upper-half matrix format the only irritant

## Slide 17: Areas for Improvement
Frequency Dependence
  At present, all values taken at DC conditions
  Additional values and equations can only be included using comments
Frequency dependence using an additional subparameter would enable ICM to use tabular-frequency data
  Example: Matrix parameters for 1 MHz, 100 MHz, etc.
Using ICM with IBIS models
  Assumed now that ICM<->IBIS link handled by tool
  BIRD to [Alternate Package Model] and/or [Package Model] keywords could add link to ICM
  Requires additional subparameters to map ICM node/pin maps to IBIS [Pin] keyword data

## Slide 18: Data Issues
ICM cookbook has been proposed
  Data format, scripting, extraction advice
Cookbook may also need data checking recommendations
  “Optimum” frequency for data extraction appropriate to the interface?
  S-parameters: appropriate bandwidth for extracted data?
  S-parameters: passivity may be an issue for data being used for transient simulations
These checks are inappropriate to the golden syntax parser

## Slide 19
Questions and
Free Discussion