## Slide 1: Multi-Element C_comp Modeling
Michael Mirmak
Intel Corporation
IBIS Summit
PCB East 2004
October 4, 2004

## Slide 2: Agenda
Background
  Recall C_comp “Back Out” Experiments
  Transient Matching
  AC Differential- and Common-mode Behaviors
Creating a Better AC Model for C_comp
  Simulation Data in AC Domain
  The Giacotto-Muranyi Model
  Improvements on the G-M Model
  Analytic vs. EDA Tool Solutions
  Results
  Applying G-M Models to the Differential Case
  Next Steps
Note: many slides in this presentation are animated

## Slide 3: How is C_comp data collected?
Common method for single-ended buffer C_comp
  Use Vsource with known edge rate, dV/dt
  Measure the input current
  Calculate capacitance (may have to take an average)
Driver
I
Vsource
dV/dt
What about for the differential case?
How about pre-emphasis (wired-or structures)?
from April ’04 Summit

## Slide 4: IBIS for SerDes Pre-Emphasis
A
B
C
D
TX+
TX-
Pre-Emphasis
A = P C = P
B = P D = P
De-Emphasis
A = P C = P
B = P D = P
Main
Boost
Pullup – Main (+ & -)
Pullup – Boost (+ & -)
Ground Clamps
Main + & -
from April ’04 Summit
1) Extract C_comp
for entire buffer
2) Split C_comp
across Main, Boost

## Slide 5: Results of First Attempt
from April ’04 Summit
Transistor vs. Combination IBIS into Rload
C_comp = 8pF

## Slide 6: Proposed Fix
Method 2: Adjust all V-t curves for the total C_comp value before using the models for simulation
  Each V-t curve reflects total C_comp load
  Adjust each curve (Main, Boost) for total C_comp
  Set IBIS C_comp for Main, Boost to 0 pF
  Add external cap equal to original total C_comp
images and equations from A. Muranyi
Vwfm_pu (V-t)
Vfx_pu
fixture
Current through fixture
is function of current
through pullup AND
through die cap
from April ’04 Summit

## Slide 7: Results of Using New Method
Matches only when c_comp set = 14pF ?
from April ’04 Summit

## Slide 8: A Further Complication
Transistor model capacitance behaviors are not simple
  Capacitance varies with frequency and bias V
  Frequency-based measurement result is not a constant
Recall A. Muranyi’s
analyses:
“Details on
True Differential Buffer
Characterization Revisited”
October, 2003
V
Hz
F
from April ’04 Summit
Single-ended capacitance
of our “8 pF” buffer
vs. V & F

## Slide 9: A Further Complication
Differential view of transistor model capacitance
  Differential capacitance not included in adjusted model
  Note that finding of femto-farad differential capacitances described in previous summits may not always apply!
Recall A. Muranyi’s
analyses:
“Details on
True Differential Buffer
Characterization Revisited”
October, 2003
V
Hz
F
from April ’04 Summit
Differential capacitance
of our “8 pF” buffer
vs. V & F

## Slide 10: Another New Approach
First C_comp adjustment attempt made two assumptions
  Differential buffers can be “split” in two
  Each can be modeled adequately with a single C_comp
Additional data calls at least one assumption into question
  Single C_comp does not permit frequency dependence
  A differential component appears at some frequencies
Proposal: Stay in AC Domain for C_comp Measurement
  Attempt to match AC behavior of simulation model
  Once model correlates in frequency of interest, add data into IBIS model
    This may stretch IBIS 3.2/4.0 beyond available keywords

## Slide 11: Our Target Behavior
V
Hz
F
from April ’04 Summit
~ 14-15 pF
~ 5-7 pF
A Low
Pass
Filter!

## Slide 12: Recall L. Giacotto’s Slides…
2002: Luca Giacotto presented twice on buffer impedance starting with observations by A. Muranyi
Two caps,
two resistors

## Slide 13: Original Giacotto-Muranyi C_comp Model
Pad
CComp = 7pF
C1 = 8.3pF
45 Ω
R1
Linearized
I-V Curve
One side of our differential
buffer (built-in pulldown,
current source is AC high-Z)
Near DC, only 45 Ω;
At low AC, caps look more
like ~ 14 pF
Value of R1 depends on
frequency of drop in
capacitance to ~ 7 pF

## Slide 14: Model vs. AC Analysis of Buffer
transistor model
Ignoring voltage…

## Slide 15: Modified G-M Model
Pad
CComp = 3p
C2 = 8.3p
45 Ω
R1
R2
C3 = 4p
Linearized
I-V Curves
Near DC, only 45 Ω;
At low AC, caps still add to ~ 14 pF
Adding new elements
to cause new “break”
in frequency

## Slide 16: Modified Model AC Analysis
transistor model
Ignoring voltage…

## Slide 17: Model Assessment
Model is a fair match up to ~ 2 GHz
Problems arise
  A single C_comp value is no longer adequate
  No IBIS keywords support this structure
  Still need to “back out” these elements from V-t curves
Pad
CComp = 3p
C2 = 8.3p
45 Ω
R1= 5 kΩ
R2
= 20 Ω
C3 = 4p
Linearized
I-V Curves

## Slide 18: Original C_comp Adjustment
Pad
CComp
Rfixture
Diff.
Driver
Idriver
Icap
Ifixture
Idriver(t) = Icap(t) + Ifixture(t)
Icap = C_comp * dV/dt where dV/dt is instantaneous V-t slope
Ifixture = V-t/Rfixture, taken at every time point
“Cap-less” V-t curve = Idriver(t) * Rfixture
  Driver is pullup curve set with internal pulldowns
  Vfixture = 0, since there is no active, driving pulldown

## Slide 19: Modified Approach
Idriver(t) = Icap(t) + Ifixture(t) + I1 + I2
Icap = C_comp * dV/dt where dV/dt is instant. slope of V-t
Ifixture = V-t/Rfixture, taken at every time point
“Cap-less” V-t curve = Idriver(t) * Rfixture
I1(t) = C1* dV1/dt
I1(t) = {V-t – V1(t)}/R1
I2(t) = C2* dV2/dt
I2(t) = {V-t – V2(t)}/R1
Pad (V-t curves)
CComp
Rfixture
Diff.
Driver
Idriver
Icap
Ifixture
C1
C2
R1
R2
I1
I2
V1
V2
But
we don’t know V or I!!!

## Slide 20: Modified Approach (2)
Yes, we do know…
RC charge equation is V1 = Vi + Ae-t/RC
  see Horowitz and Hill, The Art of Electronics, Chapter 1
For arbitrary Vi (t), this becomes
If I1(t) = C1*dV1/dt…
Pad (V-t curves)
CComp
Rfixture
Diff.
Driver
Idriver
Icap
Ifixture
C1
C2
R1
R2
I1
I2
V1
V2

## Slide 21: Modified Approach (3)
Pad (V-t curves)
CComp
Rfixture
Diff.
Driver
Idriver
Icap
Ifixture
Very tricky differential equation…
Easier solution – use EDA tool to generate data!
  Create netlist as shown
  Drive PWL source with original V-t data set(s), at pad
  CCCS into load = Rfixture provides “adjusted” V-t curves
C1
C2
R1
R2
I1
I2
V1
V2

## Slide 22: New “Cap-less” Main V-t Table
Rising Only

## Slide 23: Original V-t and First Adjust…
Rising Only

## Slide 24: Assessment
We can now adjust V-t curves for AC C_comp
  Enabling each portion of differential buffer…
  Take a separate V-t curve (Main Only, Boost only)
  Take AC domain frequency response for entire buffer
    Single-ended response only analyzed so far
  Match AC domain with model & extract adjusted V-t curve
Can we repeat the process for differential behavior?
V
Hz
F
A High
Pass
Filter!

## Slide 25: What about differential C_comp?
Pad
CCompP = 3p
C2P = 8.3p
45 Ω
R1P
R2P
C3P = 4p
CCompN = 3p
45 Ω
R1N
R2N
C2N = 8.3p
Pad
C3N = 4p
To match our
target…
CD ~ 4.5p
at high Hz
(do
C2P and
C2N add
up, acting
differentially?)
Where should Cdiff go?

## Slide 26: What about differential C_comp?
Pad
CCompP = 3p
C2P = 8.3p
45 Ω
R1P
= 5k
R2P
= 20
C3P = 4p
CCompN = 3p
45 Ω
R1N
= 5k
R2N
= 20
C2N = 8.3p
Pad
C3N = 4p
To match our
target…
RD ~ 2 Ω
At high Hz,
C2P and
C2N add
up, acting
differentially
Bias = 0V
We need Rdiff, not Cdiff!

## Slide 27: Differential C_comp (Bias = 0 V)
Diff. C_comp resembles a pass-band
filter (BW ~ 1/Rd)

## Slide 28: What about differential C_comp?
Pad
CCompP = 3p
C2P = 8.3 p
45 Ω
R1P
= 5k
R2P
= 20
C3P
= 2.33 p
CCompN = 3p
45 Ω
R1N
= 5k
R2N
= 20
C2N = 8.3 p
Pad
C3N
= 2.33 p
To match our
target…
RD ~ 2 Ω
At high Hz,
C2P and
C2N add
up, acting
differentially
Bias = 0.75 V

## Slide 29: Diff. C_comp (Bias = 0.75 V)

## Slide 30: What about differential C_comp?
Pad
CCompP = 2.6 p
C2P = 4.86 p
45 Ω
R1P
= 5k
R2P
= 800
C3P
= 1.63 p
CCompN = 2.6 p
45 Ω
R1N
= 5k
R2N
= 800
C2N = 4.86 p
Pad
C3N
= 1.63 p
To match our
target…
RD ~ 2 Ω
At high Hz,
C2P and
C2N add
up, acting
differentially
Bias = 1.5 V

## Slide 31: Diff. C_comp (Bias = 1.5 V)

## Slide 32: Summary and Next Steps
A new method for adjusting V-t curves is shown
  Based on frequency-domain capacitance profile
  Fit to a circuit expanded from Giacotto-Muranyi model
  Covers both differential and single-ended AC behavior
Comments and Next Steps
  Method is untested in system simulation!
    EDA tool method (CCCS) does not generate clean V-t data
    Local IBIS creation tools will choke on “noise” in V-t data
  Need analytic method of model value fit
    Values here determined using trial-and-error; fit isn’t great
    Giacotto proposed pole-zero analysis
    No luck in getting PZ to generate matching RC values
    Will all models have the same RC model profile?
  Need to incorporate more voltage bias data
  Need a recommendation for model bandwidth

## Slide 33: BACKUP

## Slide 34: Single-ended C_comp – Alternate View