## Slide 1
Statistical Eye Simulation Requirements
Huang Chunxing
huangchunxing@huawei.com
Asian IBIS Summit, Shanghai China
October 27, 2006

## Slide 2: Statistical Eye Simulation Flow
Simulation flow:
Time domain simulation
Statistical post-processing
The data source could be signal source or real serdes model.

## Slide 3: Simulation Requirements
Simulation platform should support IBIS or Hspice serdes model.
Simulation platform should simulate channel responses by using convolution method.
Simulation platform should easily realize jitter modulation, equalizer and emphasis.
Simulation platform should support equalizers, such as LFE, DFE and CTE.
Powerful post-processing ability.
Simulation platform may further support co-simulating with Matlab for user defined statistical processing.

## Slide 4: Jitter Modulation
Using Voltage Controlled Delay to add jitter
Jitter at transmitter includes PJ, DCD
RJ will be consider in statistical post-processing

## Slide 5: Emphasis
Emphasis technique includes pre-emphasis and de-emphasis
Both pre-emphasis and de-emphasis could be expressed as FIR filter

## Slide 6: Channel Models
Channel models, including fwrd and xtlks, could be expressed in S-parameter
Supporting transient simulation with touchstone files
pulse response
Impulse response

## Slide 7: Equalizer-LFE
LFE is linear feed-forward equalizer
discrete – usually just one tap per bit
finite – not long enough to completely correct the impulse response
May result in noise gain

## Slide 8: Equalizer-DFE
DFE is decision feed-back equalizer
DFE uses a feedback loop of the desired signal which is decoded from the output of a slicer
DFE can further correct the residual ISI

## Slide 9: Equalizer-CTE
CTE is continuous time equalizer
CTE model is an ideal circuit with the desired pole, zero response.
p0 and z0 are programmable

## Slide 10: Equalizer-Algorithm
Calculating the optimal sampling point and equalizer coefficients
LMS adaptive algorithm
Zero Forcing algorithm

## Slide 11: Statistical Post-processing
Calculating Forward channel PDF
1.Overlapping each bit at one UI range.
2. At each UI sampling point, computing
PDF of Overlapping data.

## Slide 12: Statistical Post-processing
Xtlk Convolution Method
1.Interpolating each Xtlk channel responses to small enough time interval
2. Overlapping each bit in one UI range
3. Computing PDF of Overlapping data at each UI sampling point
4. Averaging PDFs through whole UI sampling points to get the average PDF.
5. Repeating 1-4 for each aggressors.
6. Convolving average PDFs of all aggressors to get the whole crosstalk PDF.
Charles Moore presented convolution method in his paper “Computing effect of cross talk using Convolution” at 802.3ap.
http://grouper.ieee.org/groups/802/3/ap/public/channel_adhoc/moore_c1_0305.pdf

## Slide 13: Statistical Post-processing
Random Jitter
Random Jitter distribution
Overall PDF

## Slide 14: Statistical Post-processing
Statistical Eye
Statistical eye is set of probability contours
Horizontal axis is with respect to sampling point
Vertical axis is with respect to signal amplitude
Different colored lines represent BER

## Slide 15: Statistical Post-processing
Bathtub
Intercept through statistical eye along horizontal axis to get horizontal Bathtub at definite voltage
Intercept through statistical eye along vertical axis to get vertical Bathtub at definite sampling time
Horizontal
Vertical

## Slide 16: Overall Simulation Eye Flow
Channel
Eye after Equalizer
Transmitter Eye
Eye after Jitter Modulation
Eye after Emphasis
Eye after Channel

## Slide 17: Example - Channel pre-simulation
Assumed conditions:
10Gbps NRZ, PRBS 23, 100000 bits, amplitude 800mvpp, Tr(f) = 24ps
0.15UIpp DJ = 0.05UI DCD+0.1UI PJ, 0.15UIpp RJ @10-12BER
BER = 1e-12 (2*Q=14.069)
3tap de-emphasis, 5tap DFE
Slice voltage: 10mV
Forward Channel Eight crosstalk channels

## Slide 18: Example - Channel pre-simulation
Simulation result:
28mv eye-height
0.222UI eye-width
It shows that the channel could undertake 10Gbps data transmission

## Slide 19: Conclusion
Basic method of statistical eye simulation has been presented here
An ideal platform to realize statistical eye simulation:
  Jitter Modulation at transmitter
  Pre-emphasis or de-emphasis
  Supporting Forward channel, Xtlk channel models
  Equalizer
  Statistical post-processing