## Slide 1: IBIS4.2 and VHDL-AMS for SERDES and DDR2 Analysis
Ian Dodd
Architect, High Speed Tools
Ian_dodd@mentor.com
Gary Pratt
Manager, High Speed Partnerships
gary_pratt@mentor.com
© Mentor Graphics Corp., 2006,
Reuse by written permission only. All rights reserved.
31st October 2006

## Slide 2: IBIS 4.2 Multi-lingual Extensions
Traditional IBIS lacks the ability to adequately model the behavior of devices used in state of the art communication channels:
  Drivers with pre-compensation
  Receivers with input slew rate sensitivity.
  Phase locked loop clock and data recovery
  Simple and adaptive equalization
  Multi-level signaling
Traditional IBIS also lacks the ability to adequately specify new measurements:
  Differential overshoot
  Eye masks
IBIS 4.2 Multi-lingual Extensions can address both of these limitations

## Slide 3: SPICE as an IBIS 4.2 Multi-lingual option
Good supply of transistor level models for older devices
  May be encrypted and therefore not portable between tools
Poor standardization
  Lots of proprietary primitives
Extremely slow simulation
  Particularly when using transistor level models
Missing a high level view
  Needed to effectively model complex digital logic
  Needed to make complex measurements.

## Slide 4: AMS as an IBIS 4.2 Multi-lingual option
VHDL-AMS and Verilog-AMS International standards
  IEEE and Accellera
Fast.
  Models are compiled to machine code just like built in primitives.
  Digital content is handled in event driven kernel
Flexible
  Can provide both behavior and measurement.
Accurate
  Uses the same analog non-linear solver as SPICE

## Slide 5: IBIS 4.2 Multi-lingual Case Studies
The model maker and user can best decide whether it is best to create models using the IBIS 4.2 multi-lingual extensions utilizing SPICE or AMS
The best solution for the SI Engineer may well be a tool that supports the mixing of both
AMS provides some unique features so this presentation is going to provide two case studies that highlight these features.

## Slide 6: AMS Case Study One Full non-linear analysis of a SERDES channel
Simulate to 10 million data bits
Custom data pattern
VHDL-AMS Driver with non-linear drive characteristics and pre-compensation
Realistic S-Parameter model for packages, two connectors and backplane*
VHDL-AMS receiver model with built in envelope recorder
Simulations to be done on an average single processor notebook computer running Microsoft Windows
Appropriate simulation time-step for accurate results
As with previous examples used in presentations, this S-parameter model was provided by an independent third party and not optimized for simulation speed
*

## Slide 7
AMS PRBS Generator
AMS SERDES TX
S-Parameter TX Package, Stub, Connector, Backplane, Connector, Stub, RX Package
AMS RX and Envelope Generator

## Slide 8: The VHDL-AMS SERDES Transmitter Model
begin
-- output the proper current based on the state of signal din,
-- and values of constants Ipe and Imain
if domain = quiescent_domain use – if DC then
itxp == Ipe/2.0; itxn == Ipe/2.0; -- set both outputs to half
elsif din='1' and din'delayed(bit) = '0' use
itxp == Ipe; itxn == 0.0; -- first pulse (txp positive)
elsif din='1' and din'delayed(bit) = '1' use
itxp == Imain; itxn == Ipe-Imain; -- normal pulse (txp positive)
elsif din='0' and din'delayed(bit) = '1' use
itxp == 0.0; itxn == Ipe; -- first pulse (txn positive)
elsif din='0' and din'delayed(bit) = '0' use
itxp == Ipe-Imain; itxn == Imain; -- normal pulse (txn positive)
end use;
break on din, din'delayed(bit) ; -- deal with the discontinuities
-- P and N-side C_comp, R_term, Vdd
i_r_term_p == (vtxp - Vdd)/R_term; i_c_comp_p == c_comp * vtxp'dot;
i_r_term_n == (vtxn - Vdd)/R_term; i_c_comp_n == c_comp * vtxn'dot;
end architecture;

## Slide 9: Results: Simulation to 10 Million Data Cycles (All simulations completed overnight)
10 Cycles
100 Cycles
1,000 Cycles
10,0000 Cycles
100,000 Cycles
1,000,00 Cycles
10,000,000 Cycles

## Slide 10: AMS Case Study Two Automated DDR2 Measurements
Implement all measurements specified in the DDR2 datasheet in a VHDL-AMS model
Utilize standard IBIS 3.2 driver and receiver models

## Slide 11
overshoot area
absolute overshoot
slew rate
monotonicity
crossing zone
runt pulse
undershoot area
min pulse width
absolute undershoot
overshoot area
absolute overshoot
pos set runt pulse
undershoot area
pos setup tangent
absolute undershoot
pos hold tangent
neg setup tangent
neg hold tangent
neg hld runt pulse
pos derated setup
pos derated hold
neg derated setup
neg derated hold
Delta TF
pos hld runt pulse
neg set runt pulse
DDR2 Electrical and Timing Constraints
Notes: While certainly not meant to summarize the entire JEDEC DDR2 specification, this diagram does quickly convey the complexity and difficulty of thoroughly testing a typical CPU to DDR2 memory interface. Add to this the fact that these tests must be made on each data line individually and the task quickly becomes overwhelming. Required tests include absolute over/undershoot which tests for the never-to-exceed voltage limits, and the over/undershoot area which limits the power dissipated by clamp diodes. Slew rate is measured on both DQS and DQ which is then applied to the derating table to determine the required setup and hold time based on the rise and fall characteristics. Measuring the DQ slew rate is complicated by the requirement that the slew be based on the line with the maximum slope that originates at the AC crossing and is tangent to the measured signal. Additional tests include the crossing of the differential DQS signal within a certain voltage zone, and the requirement that DQS be monotonic within another voltage zone. Both DQS and DQ must be monitored for runt pulses, where the signal crosses the threshold but fails to reach a certain voltage before crossing back through the threshold. Finally, DQS must be checked for minimum pulse width, and the DQ must be checked for setup and hold requirements based on the slew-rate derated calculations.

## Slide 12: IBIS 4.2 Measurement Model
IBIS 3.2 Model
IBIS 3.2 Model
Printed Circuit Board
…
DDR2 Measurement Model
IBIS 3.2 Model
IBIS 3.2 Model
DQS
DQ0
Results
Notes: The measurement model can be used stand-alone as a distinct device in the pre-layout editor …
The model monitors the clock and data pins, and performs the measurements as outlined on the previous slide. If a violation occurs, an appropriate message is generated. Unfortunately, the IBIS standard does not deal with standard message formats, or how to transfer the message out of the model and into the underlying tool for a consistent display to the user. This is an issue the IBIS committee may want to address.

## Slide 13: Pre-layout analysis using the IBIS 4.2 Measurement Model
Notes: Which will look like this in a pre-layout tool …

## Slide 14
TANGENT MEASUREMENT
Wait for vref crossing
Store data points
Wait for vix_ac cross
Calculate the slope from each point to the vix_ac crossing point
Return the maximum slope
Wait for vix_dc crossing
Calculate the slope from each subsequent point back to the vix_dc crossing
Wait for vref crossing
Return the max slope
(error and exception handling removed for clarity)
Notes: This code demonstrates how the maximum tangent line is determined. The calculation of the setup tangent line is complicated by the fact that we do not know the tangent line pivot point (the AC crossing point) until after the datapoints for the free-end of the tangent line have passed. For this reason, the free-end data points must be stored until the AC crossing occurs.
The process begins by waiting for a reference crossing. At that point, the module then stores all the analog solution points (ASPs, also known as “time-points”), until the signal crosses the AC threshold. Instantaneously after the AC crossing, the slopes of the lines from each stored point to the AC crossing point is calculated, and the maximum of these is stored. The “nominal” slope line is the line drawn directly between the reference and AC crossing. If the slope of the signal curves left of the nominal line, the nominal line will end up having the greatest slope and thus its slope will be used as the entry to the derating table. If the signal curves to the right of the nominal line, the resulting tangent line with the greatest slope will be used as the entry to the derating table.
The “Hold” tangent measurement is slightly easier, as we know the pivot point of the tangent line first, so we do not need to store any data points. This section of the process waits until the DC crossing, then calculates the slope from that crossing point to each analog solution point until the reference crossing is detected. The line with the largest slope is used as the tangent line, and used as the index into the hold derating lookup table.
Unfortunately, IEEE 1076.1 does not define a signal for analog solution points. This is left up to the simulator vendors to provide, and might not be a universally supported extension. A work-around to this is to use some fixed period sampling instead of ASPs, but this requires some knowledge of the expected time-step so that an appropriate sampling period can be chosen. Unnecessary sampling could also slightly increase the simulation time for this model. The addition of an ASP signal would be a valuable enhancement for the IEEE 1076.1 committee to provide in their next revision of the standard.

## Slide 15
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 2337
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 4790
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 7290
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 9815
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 12294
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 14816
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 17293
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 19816
U2 pin 2 Violation - DQS exceeded VIXACMIN at Differential Crossing at time: 1275
U2 pin 2 Violation - DSQ exceeded VINDCMAX or VINDCMIN at time: 5914
U2 pin 2 Violation - DSQ exceeded VINDCMAX or VINDCMIN at time: 5955
U2 pin 1 Setup Check PASSED. Expected: 0.275 ns. Actual: 1.55 ns at time: 4536
U2 pin 2 Warning: dqs slew value out of range of table.
dqs_slew= 4.33e+9. Max table index value= 4.00e+009 at time: 5799
U2 pin 2 Warning: dq slew value out of range of table.
dq_slew= 3.566e+9. Max table index value= 2.00e+009 at time: 5799
U2 pin 1 Hold Check PASSED, Expected: 0.32 ns. Actual: 1.177 ns. at time: 5799
Notes: The Orange signal DQ, the purple is subtracted differential DQS, and the light blue is the a plot of the calculated tangent line. The model automatically applies the tangent line slope to the de-rating tables and determines if the de-rated timing constraints have been met, so The tangent line is for visualization purposes only.
The model automatically performs the 25 electrical and timing tests as outlined earlier, and outputs the results. The model can be configured to output any combination of violations, passes, measurements, and margins.

## Slide 16: Model for the Full DDR2 Channel Integrating both Behavior and Measurement *
IBIS 3.2 Model
DDR2 Memory Digital HLD Model
(responds to read cycles)
IBIS 3.2 Model
CPU Digital HLD Model
(generates real write/read cycles)
Printed Circuit Board
…
DDR2 Measurement Model
IBIS 3.2 Model
IBIS 3.2 Model
IBIS 4.1 Chipset Model
IBIS 4.1 Memory Model
DQS
DQ0
DQ[63:1], A[18:0], etc[26:0]
…
Msgs
Chipset Measurement Model
Msgs
… (108)
… (108)
…
* Note: This model is not in strictly IBIS 4.2 compliant because it uses an external circuit that references an IBIS 3.1 model
Notes: As mentioned earlier, the measurement model can be incorporated into the post-layout IBIS 4.1 device model to allow a complete post-layout analysis. This diagram shows the model being incorporated into the DDR2 Functional SI analysis (See DesignCon 2006 IBIS Summit for more details).
Once in IBIS 4.1 format, all that is left to the model user is to import the IBIS 4.1 model into their IBIS 4.1 compatible tool, assign the model to the memory part, and invoke the simulator. The IBIS 4.1 models take care of providing stimulus to the PCB, and measuring the resulting signals at the memory pins. All the user need do is review the resulting messages to see if there has been a violation … infinitely simpler than previous alternatives of manual inspection and interpretation.

## Slide 17: Special thanks to
Randy Wolff and his associates at Micron for assistance in developing DDR2 simulation and measurement models.