## Slide 1
IBIS Evolution and Adoption
Will Hobbs
Intel Corporation

## Slide 2
IBIS Evolution and Adoption
Surprise! Technology growth isn’t slowing down
New challenges cause subtler effects to be significant
  Higher speeds. Picoseconds count.
  Lower voltages. Millivolts add up.
Models and simulators must keep up
  Low noise and timing budgets demand better simulations
  Models need to be comprehensive, include subtle effects
  See case study, next foils
Accuracy work and commitment to future growth need publicity
  Quell fears of high speed I/O architects
IBIS 3.x must be implemented and deployed ASAP
  Speculative implementation of 3.0 would have helped, as would:
  Faster parser development - 1 year is too long
Future enhancements must be deployed more quickly

## Slide 3
Case Study
Problem: Glitch on strobe during SSO in particular systems caused false state machine clocking
Data
Strobe
Deep Glitch, eroded margin. Multiple contributors:
SSO of data affected strobe, but only with specific data patterns
Reflection coincident with SSO
Noise margin eroded by path problems:
  termination plane noise
  routing topology
  package routing
  Vcc bypassing
  connector inductance
  sub-optimal ground return path
Effects subtle, simulators and models inadequate, decomposition into contributing elements exceedingly difficult in-system.

## Slide 4
Signal (over plane)
Return
Connector pin inductance not properly modeled.
Subtle but measurable difference, significant
with eroded margin
High L, Low L
Signal return-path coupling can be a significant source of noise
Ground Path
Signal Paths
Hole in plane
Subtle Effects Accumulate
Contributed 50-90 mV
These are not all IBIS issues, but illustrate the need for ever finer precision and good models.

## Slide 5
Recent Modeling Approach
Flight time measurement taken from input of output buffer to output of input buffer
  Easier to spec logic level transition times
  Incompatible with IBIS
  Necessary? Not sure. But if so, limits EDA vendor choices
Behavioral input model required to model in IBIS
Board traces, interconnect
Driver
Receiver
IBIS Domain
Span of this method

## Slide 6
To Ponder
Has behavioral simulation reached its limit?
  Some think so (present company excluded)
  If not, we need to address their concerns
  If so, we need to identify the limits of behavioral simulation, and ...
  Find a happy coexistence between structural and behavioral (API?), without losing:
    IP protection
    Vendor neutrality
    Speed advantage of behavioral simulation
  More models, better models
  And, we need to keep pushing IBIS to meet emerging needs
    More sophisticated input models
    Improved package models (include coupling, e.g.)
    Equation-based models?
    Feedback?