## Slide 1
IBIS Test Board
Peter LaFlamme
Fairchild Semiconductor
333 Western Ave.
So. Portland, ME 04106
207-775-8000

## Slide 2
Purpose:
Test board offers a means for testing and verifying IBIS Accuracy methodologies through experiment.
Test board was designed for measuring
    DC IV Curves
    Test Loads (AC Waveforms)
    Capacitance (Input and Output)
An IBIS model can be created from sample silicon

## Slide 3
IBIS Test Board
Respun and Ready for Testing!
Schematics and Layout available to all
Will be part of our demo at
DesignCon99

## Slide 4
Board Specifications:
Layout Accommodates a 16244 function in 48-lead
TSSOP package
Test board is a simple 4 layer stackup
Only requires device power, all other signals are
generated on-board
2 Devices (U1 and U2)
  U1 is set up for standard IBIS I/V data collection
and input/output Capacitance measurement
  U2 is set up for all AC measurements
Test strips for measuring T-line characteristics of board traces
Test strips for measuring the load characteristics of board Vias
and 3 types of probe connections.

## Slide 5
IBIS Model Structure
INPUT MODEL
OUTPUT MODEL
Package RLC
Package RLC
Package RLC
Vcc
Gnd
Clamp
PWR
clamp
Input
Package RLC
Package RLC
Package RLC
Vcc
Gnd
Clamp
PWR
Clamp
Output
Pull-up
Pull-Down

## Slide 6
IBIS DC Data: IV Curves
I/V Curves:
  INPUT and TRI-STATE: Clamp Structures
  OUTPUT: Pull-Down and/or Pull-up
Schematic:
Input and Output DC Sweep
Vcc= Max, Typ, Min (+/- 10%)
Temp = -40C, 25C, 85C
DUT
Vcc
V
+
-
A
V
+
-
A

## Slide 7
Output IV Curves Pull-up and Pull-down
ACT244 Output Pull-Down
0
0.1
0.2
0.3
0.4
0.5
0.6
0
0.5
1
1.5
2
2.5
3
3.5
4
4.5
5
5.5
Vout (V)
Iout (A)
ACT244 Output Pull-Up
-0.6
-0.5
-0.4
-0.3
-0.2
-0.1
0
0
0.5
1
1.5
2
2.5
3
3.5
4
4.5
5
5.5
Vtsble = Vcc-Vout (V)
Iout (A)
Vcc
V
+
-
A

## Slide 8
Input and Tri-State IV Curves Gnd Clamp and Pwr Clamp
ACT244 Input GND Clamp
-30
-25
-20
-15
-10
-5
0
-5
-4
-3
-2
-1
0
1
Vout (V)
Iout (A)
ACT244 Input PWR Clamp
0
2
4
6
8
10
12
14
16
18
-5
-4.5
-4
-3.5
-3
-2.5
-2
-1.5
-1
-0.5
0
Vtable = (Vcc - Vout) (V)
Iout (A)
Vcc
V
+
-
A

## Slide 9
AC Test Load Waveforms
Tline terminated to Zo (IBIS Load)
Standard Lumped “Datasheet” Load
Lightly Loaded Tline (Un-terminated)
Driver Driving Receiver of Same Family
(Un-terminated)
Importance of properly modeling environment

## Slide 10
Test Load Waveforms (Ideal Transmission Line, T-line terminated to Zo)
Schematic:
Rise
Fall
Waveforms:
Fall
Rise
50 Ohms
DUT
Vcc
Probe
Parasitics
50 Ohms
DUT
Vcc
Probe
Parasitics

## Slide 11
Test Load Waveforms (Standard “Datasheet” Load)
Schematic
ACT244 Driving Lumped Load (50pF/500)
IBIS Simulation
-2
0
2
4
6
5
10
15
20
25
Time (nS)
Vout (V)
Waveform:
50pF
500 Ohms
DUT
Vcc
Probe
Parasitics

## Slide 12
Test Load Waveforms (Transmission Line, Un-terminated)
Schematic:
Waveform:
Zo, To
DUT
Vcc
Probe
Parasitics

## Slide 13
Test Load Waveforms (Driver and Receiver, Un-terminated)
Schematic:
Waveform:
Zo, To
Drv
Vcc
Rcv
Vcc
Probe
Parasitics

## Slide 14
Additional Measurements Capacitance
Frequency Domain
  LRC meter
  Capacitance Bridge
Time Domain
  TDR
  Pulse Technique
Note: Capacitance measured is the sum of Input, Output or I/O capacitance and package capacitance
Pkg

## Slide 15
Parameters Not Measured
Package Resistance
  Resistance typically < 0.1 Ohm
Package Inductance
  Accuracy can be inferred from test load waveforms
  Not easily measured in package parts

## Slide 16
IBIS Test board (Summary)
Test Case to Verify Specification
  Still work to be done to “characterize” board and test loads
Set of Test Structures
  Measure AC and DC Parameters
  Specification Companion
Board Design is FREE
  Schematics
  Gerbers
  Parts List
  Study, Improve and Share