## Slide 2: Tips and Tricks for Creating IBIS Models
Samples from a case study on the creation and QA of IBIS models from SPICE simulation models
Jon Powell - Viewlogic Consulting Services
Notes: Presented by:
Jon Powell
Ibis Librarian
Director of High Speed Design Consulting Services, Viewlogic

## Slide 3: OverView (sorry)
Some Important IBIS features
Setting up test circuits
Running QA
Some common problems
Some difficulties in IBIS
Example Model Simulation Comparisons
Notes: The purpose of this presentation is to share some of the tricks and pitfalls that I have run across in the generation of various IBIS models.
I use SPICE models from IC manufacturers as my input data and XNS as my IBIS QA simulator. I use an internal proprietary SPICE to IBIS translator called VML (Virtual Modeling Lab).
We will start with basic setup and run through some of the issues in extracting data, building IBIS models, and full model Quality Assurance (QA).

## Slide 4: Important IBIS features
VT Curves
Test Fixture Description
Properly chosen point distribution
Notes: I believe that a full and proper set of Voltage/Time waveforms are critical for most highspeed new devices. Of the models I have seen, many employ Rise Time Control (or Slew Rate Control) and these VT curves are necessary for complete transition description.
For most CMOS models, a 50ohm to GND and 50ohm to VCC load is appropriate for the model generation but this may vary with actual output device strength.
I also think that generating IBIS data with a fixed timestep or voltage step is often not appropriate. The 100 point limit of IBIS makes the selection of a fixed step not compatible with the desire for maximum accuracy in the data. This can be especially seen in RTC models with risetimes in the 30-40ns range (a la those from Altera).

## Slide 5: Setting up Test Circuits
Get rid of package (and die) parasitics.
Measure to a high accuracy
Set SPICE options to allow for exact voltage measurement
Make QA measurements with Cdie present.
Be sure to measure long enough
Be sure input signal does not effect output.
Notes: For maximum accuracy in describing the transition, you should remove all of the stray capacitance that is possible and put this capacitance into the appropriate location in the IBIS models.
Be careful that your data is correct coming out of SPICE. SPICE has many options to explore that set voltage, time, and current print or plot accuracy.
I usually make another measurement (for QA only, not inclusion in the IBIS model) that contains the Cdie.
Be careful that you are modeling enough of the output stage that your input stimulus has little or no effect on the final output.

## Slide 6: Running QA
QA against original SPICE VT data.
Use a well chosen mid-voltage point for time synchronization on rising and falling edges.
Compare both with Cdie and without
Add additonal test cases
  Test Fixture (ie. 50pf)
  Transmission line.
  Full package test.
Notes: If you aren’t going to run QA comparisons, DON”T WRITE THE IBIS MODEL.
You aren’t doing anyone any favors by releasing a model that probably won’t work. IBIS models are hard to write and need QA.
Compare IBIS simulator results to original SPICE waveform data. They should match pretty well.
Feel free to generate other SPICE simulations that you can compare to the IBIS simulator results. You can’t do too much QA, but it can be quite time consuming.
You also have to decide what is a “good” model comparison and what is unacceptable.
Different simulators have different strengths that you will have to take into account in your comparisons.

## Slide 7: Some Common Problems
Simulation Time Doesn’t allow waveform to reach full high or low.
SPICE model doesn’t behave well without Cdie
SPICE model needs special control options to converge.
SPICE diode model creates unlikely amounts of current.
QA Simulation doesn’t reproduce some SPICE features.
Notes: I have seen RTC models with risetimes in the 40ns or greater range (even though a majority of the transition occurs in the first 1ns). These can be challenge to properly model and fit the data into IBIS.
Some SPICE models just won’t behave well if you remove the Cdie. Try adding just enough Cdie back to make the model behave. Be sure to remove the same amount from the IBIS internal model.
I haven’t figured out what to do about the 0ohm diode models in SPICE. Adding some static resistance seems to be an acceptable solution.

## Slide 8: Some Difficulties in IBIS
100 point limit can create difficulties in fitting large MIN MAX TYP IV and VT curves. May require careful linearization.
MIN MAX and TYP may not describe full range of corners desired.
LC may not be enough information for package description (look to 3.1)
Transition Time not very useful for RTC or many highspeed advanced drivers.
Notes: Linearization of 3 curves into 1 100point table is not trivial. Be careful.
I think that if I had to a chance to re-write IBIS I would remove the 100 point limit and get rid of the MIN TYP MAX definition in favor of user definable unlimited corners. We were just to specific and unnecessarily limiting. Mea Culpa.
Some new package are impedance matched. This might not translate well into the LC package parameters. You may find it necessary to use the new TLINE package definitions.
The transition time definitions have little or no use when simulating RTC components (see upcoming example)

## Slide 9: Example Model QA Simulations
Notes: This example has a very strong and defined RTC on the falling edge. This is a 10ka model from Altera.
This simulation shows an overlay of the original SPICE input data (which is the same as the data that goes into the FALLING WAVEFORM portion of the IBIS model) and an XNS simulation of the translated IBIS file. This uses VT curves exclusively for the definition of FALLTIME and transition shape.

## Slide 10: Without VT waveforms
Notes: This is the same models minus the VT curves and using the FALLTIME numbers to define the transition. I think this shows the importance of well chosen VT curves for RTC models.