## Slide 1: IBIS Training
I/O Buffer Information Specification
IBIS East Summit
October 15,1998
Joseph Socha

## Slide 2: IBIS training
This is targeted to be a half day introductory class with Hands-On lab exercises
Today presentation is to show the direction
Gather IBIS community feedback
Notes: Most of the presentations at technical conferences and IBIS meeting deals with the technical aspects of the model, its description or performance good or bad.
This class doesn't contain any profound data revelations, it attempts to bring first time and novice users up to speed with the language. A device physicist may be able to read this IBIS spec and have an intuitive feel for creating a model. Most engineers might use the spec. as a cure for insomnia.
After completing the class I hope an average engineer could use an IBIS model with some confidence, refine a model to suit your accuracy needs, and be confident he will get a reasonable result in the lab when comparing simulation to his scope.
Today's presentation is only a partial view of the IBIS class. I intend to include labs that will have the student prepare several versions of IBIS models to allow the student to learn the syntax as well as use a simulator to complete the exercises.
I would also like to get feed back from the audience.

## Slide 3: Introduction
In order to enable an industry standard method to electronically transport
IBIS Modeling Data between silicon vendors, simulation software vendors, and
end customers, this template is proposed. The intention of this template is
to specify a consistent format that can be parsed by software, allowing each
simulation vendor to derive models compatible with their own product.
IBIS 1.0 Specification
The examples included here are based on a couple of the currently available simulators. They are used here to help illustrate points that will help the students develop a better understanding to modeling devices and putting them to the IBIS format.
Notes: From the v 1.0 spec

## Slide 4: Target Audience
Engineers who do SI simulation
Engineers who develop IBIS models
Silicon vendors
CAE software developers
Notes: Here are some of the users who will benefit from this class.
Device physicists need not apply.

## Slide 5: What is this IBIS stuff anyway ?
IBIS(Input Output Buffer Information Specification) is a format for describing digital device (input and output) behavior. IBIS models include many of the devices characteristics such as pin parasitic’s and rise/fall data as well as the Voltage vs. Current behavioral data. IBIS is not a stamp of approval.
Notes: Excerpt from the IBIS FAQ
What is this IBIS stuff anyhow ?
IBIS(Input Output Buffer Information Specification) is a method of providing the Input/Output device characteristics through V/I data without disclosing any
circuit/process information. It can be thought of as a behavioral modeling
specification suitable for transmission line simulation of Digital Systems and
applicable to most digital components.

## Slide 6: Abstract
IBIS models can be very useful for discovering signal integrity issues after layout. They can also help to create design strategies as well as design rules for layout that improve your chances for first turn success
Notes: “Behavioral I/O buffer models such as those supported by the emerging IBIS (I/O Buffer Information Specification) standard can be extremely useful in uncovering signal integrity problems after the board has been routed. Like all circuit models, which attempt to capture the behavior of a complex physical system using a less complex mathematical model, behavioral I/O buffer models are susceptible to discrepancies between simulation and actual hardware. Semiconductor vendors and users should not under estimate the care and effort required to build accurate models.”
Robert J Haller and Greg Edlund
Constructing Accurate Behavioral Models of I/O buffers DesignCon98

## Slide 7: Empirical Method Example
Notes: This is what we hope to prevent from our products.

## Slide 8: History of IBIS
Originally started by Intel. Presently driven by the IBIS open forum consisting of EDA vendors, Computer Manufacturers, Semiconductor vendors and Universities.
IBIS versions:
        V1.0 - Original First release April 1993
        V1.1 - Released June 1993 at DAC, Dallas.
        V2.0 - Ratified June 1994 at DAC, San Diego
        V2.1 - Released Dec 1994
        ANSI/EIA-656 approved Dec 1995
        V3.0 - Ratified June 1997
        IEC 62014-1 - Sep 1997
Notes: <number>
<footer>
<header>
<date/time>
IBISv1.1 is meant for CMOS/TTL type of I/O’s and maintains the core set of IBIS keywords.
IBISv2.1 was expanded from v1.1 to support additional types of I/O’s particularly ECL, PECL, Differential etc. Waveform tables(V/T) and pin mapping features were also added along with many other extensions. IBISv2.1 is an approved ANSI/EIA-656 standard.
IBISv3.0 has been ratified at DAC97. The next step for the committee is to create a parser that supports v3.0 features. IBISv3.0 has various advanced features. Some of the added features are Driver selection, Diode stored charge, Package Model extension, Electrical board description, Multi-stage Drivers, Series elements and more.
The EIG(Electronic Information Group)within EIA has been actively working towards making IBIS part of the IEC(European) standard. IBIS has been accepted as IEC-62014-1 recently(Sep’97)at the Tokyo International Standards meeting.
There has been other proposals made from the International committees to extend IBIS to cover EMC simulation.
DIE, EDIF 4 0 0 are some of the other standards that references IBIS.
From: High level Electronic System Design Conference(HESDC) ‘97 Syed B. Huq

## Slide 9: Lets relate syntax to real world
We will cover a simple driver example and build a simple IBIS model

## Slide 10: Simple Transmission Line Symbols
Driver = Output or I/O
Receiver = Input
Notes: Driver on the left, transmission line in the middle and receiver on the right.

## Slide 11: Decompose and look at DC
Notes: Steady state condition.

## Slide 12: Now the AC Picture
Notes: On the incident wave. Driver drives the t-line. The t-line drives the load.

## Slide 13: Discontinuities Cause Reflections: An Example with no Discontinuities
50ohms
50ohms
50ohms
Notes: Perfect 50 system.

## Slide 14: Impedance Mismatch Example
Driver
Receiver
Both
Notes: Why we need to simulate.

## Slide 15: Representation of a Driver
Notes: Simplistic view generally used in hand calculations.
Piece wise linear approximation using Voh/Ioh and Vol/Iol curves.

## Slide 16: CMOS VI Curve
Notes: VI curve plotted from spice simulation.

## Slide 17: Representations of a Driver
Rise time is assumed to be linear !
Notes: Adding more detail

## Slide 18: IBIS 1.1 Driver
L_pin
C_pin
Simulator
switching
Pullup
Pulldown
POWER clamp
GND clamp
Notes: Now present some IBIS syntax.

## Slide 19: Increasing Model Complexity
More accurate simulations
Still not handled
  Connector models
  Simultaneous switching ( Vcc starvation)
  ...
Notes: The model of today can not handle all possible situations.
Use the right tool for the right job.

## Slide 20: Lets move on to the syntax

## Slide 21: Key Words Ver 1.0
[IBIBS Ver]
[Comment char]
[File name]
[File Rev]
[Date]
[Source]
[Notes]
[Disclaimer]
[Component]
[Manufacturer]
[Package]
R_pkg,L_pkg, C_pkg
[Pin]
Signal_name, model_ name
R_pin, L_pin, C_pin
[Model]
Model_type, Polarity,Enable
Vinl, Vinh, C_comp
[Voltage Range]
[Pulldown]
[Pullup]
[GND Clamp]
[POWER Clamp]
[Ramp]
[Rising Waveform]
[Falling Waveform]
[End]
Notes: This is a list of the key words as extracted from the v1.0 spec

## Slide 22: Key WordsVer 2.1
[IBIBS Ver]
[Comment char]
[File name]
[File Rev]
[Date] [Source] [Notes] [Disclaimer] [Copyright]
[Component]
[Manufacturer]
[Package]
[Pin]
[Package Model]
[Pin Mapping]
[Diff Pin]
[Model]
[Temperature Range]
[Voltage Range]
[Pullup Reference]
[Pulldown Reference]
[POWER Clamp Reference]
[GND Clamp Reference]
[Pulldown]
[Pullup]
[GND Clamp]
[POWER Clamp]
[Rgnd]
[Rpower]
[Rac]
[Cac]
[Ramp]
[Rising Waveform]
[Falling Waveform]
[Package Model]
[Define Package Model]
[Manufacturer]
[OEM]
[Description]
[Number of Pins]
[Pin Numbers]
[Model Data]
[Resistance Matrix]
[Inductance Matrix]
[Capacitance Matrix]
[Bandwidth]
[Row]
[End Model Data]
|[End Package Model]
Notes: The version 2.1 spec has increased the key words dramatically in order to increase the accuracy of the models.

## Slide 23: Header
[IBIBS Ver] Required [IBIBS Ver] 1.0
[Comment char] Optional [Comment char] |_char
Notes: |==============================================================================|
| Keyword: [IBIS Ver] |
| Required: Yes |
| Description: Used to specify the IBIS ASCII template version. This will be |
| used to inform an electronic parser of the kinds of data types |
| that will be present in the file. |
| Usage Rules: [IBIS Ver] must be the first keyword in any IBIS file. It is |
| normally on the first line of the file, but can be preceded |
| by comment lines (that must begin with a "|"). |
|------------------------------------------------------------------------------|
[IBIS Ver] 1.1 | Used for template variations
|==============================================================================|
| Keyword: [Comment char] |
| Required: Optional |
| Description: Used to define a new comment character to replace the default |
| "|" (pipe), if desired. |
| Usage Rules: The new comment character which is to be defined must be |
| followed by the underscore character and the letters "char". |
| For example: "|_char" redundantly redefines the comment |
| character to be the pipe character. The new comment character |
| will be in effect only following the [Comment char] keyword. |
| The following characters can NOT be used: A B C D E F G H I J |
| K L M N O P Q R S T U V W X Y Z a b c d e f g h i j k l m n o |
| p q r s t u v w x y z 0 1 2 3 4 5 6 7 8 9 [ ] . _ / = |
| Other Notes: The [Comment char] keyword can be used throughout the file, as |
| desired. |
|------------------------------------------------------------------------------|
[Comment char] |_char
|==============================================================================|

## Slide 24: Header
[File name] Required [File name] filename.ibs
[File Rev] required [File Rev] 1.0
Notes: |==============================================================================|
| Keyword: [File name] |
| Required: Yes |
| Description: Used to specify the name of the IBIS file, "filename.ibs". |
| Usage Rules: The file name must comply with normal DOS rules (8 char. max. |
| and no characters that are illegal in DOS). In addition, it |
| must be all lower case, and use the extension ".ibs". |
|------------------------------------------------------------------------------|
[File name] ver1_1.ibs
|==============================================================================|
| Keyword: [File Rev] |
| Required: Yes |
| Description: Used to track the revision level of a particular .ibs file. |
| Usage Rules: Revision level can be set at the discretion of the engineer |
| defining the file. The following guidelines are recommended: |
| 0.x silicon and file in development |
| 1.x pre-silicon file data from silicon model only |
| 2.x file correlated to actual silicon measurements |
| 3.x mature product, no more changes likely |
|------------------------------------------------------------------------------|
[File Rev] 1.0 | Used for .ibs file variations
|==============================================================================|

## Slide 25: Header
[Date] Optional [Date] 04/19/93
[Source] Optional [Source] Lab measurement
[Notes] Optional [Notes] Great part but …
[Disclaimer] Optional
[Disclaimer] This information is for modeling purposes only, and is not guaranteed.
Notes: |==============================================================================|
| Keywords: [Date] [Source] [Notes] [Disclaimer] |
| Required: Optional |
| Description: Optionally used for further file clarifications. |
| Usage Rules: The [Date] information is allowed to contain blanks, and be of |
| any format up to 40 characters. |
|------------------------------------------------------------------------------|
[Date] 04/19/93 | Latest file revision date
[Source] Put originator and source of information here. For example:
From silicon level SPICE model at Intel,
From lab measurement at IEI,
Compiled from manufacturer's data book at Quad Design, etc...
[Notes] This section can be used for any special notes related
to the file.
[Disclaimer] This information is for modeling purposes only, and
is not guaranteed. | May vary by component
|==============================================================================|

## Slide 26: Body
[Component] Required [Component] Foo321
[Manufacturer] Required [Manufacturer] ACME Corp.
Notes: |==============================================================================|
| Keyword: [Component] |
| Required: Yes |
| Description: Used to mark the beginning of the IBIS description of the |
| integrated circuit named after the keyword. |
| Usage Rules: If the .ibs file contains data for more than one component, |
| each section must begin with a new [Component] keyword. The |
| length of the Component Name must not exceed 40 characters, |
| and blank characters are allowed. |
|------------------------------------------------------------------------------|
[Component] Component Name
|==============================================================================|
| Keyword: [Manufacturer] |
| Required: Yes |
| Description: Used to clarify the component's manufacturer. |
| Usage Rules: The length of the Manufacturer's Name must not exceed 40 |
| characters (blank characters are allowed, e.g., Texas |
| Instruments). In addition, each manufacturer must use a |
| consistent name in all .ibs files. |
|------------------------------------------------------------------------------|
[Manufacturer] Manufacturer's Name | e.g., Intel
|==============================================================================|

## Slide 27: Body
[Package] Required
[Package]
| variable typ min max
R_pkg 250.0m 225.0m 275.0m
L_pkg 15.0nH 12.0nH 18.0nH
C_pkg 18.0pF 15.0pF 20.0pF
Notes: |==============================================================================|
| Keyword: [Package] |
| Required: Yes |
| Description: Used to define a range of values for the default packaging |
| resistance, inductance, and capacitance of the component pins. |
| Sub-Params: R_pkg, L_pkg, C_pkg |
| Usage Rules: Typical column must be specified. If data for the other |
| columns are not available, they must be noted with "NA". |
| Other Notes: If RLC parameters are available for individual pins, they can |
| be listed in columns 4-6 under keyword [Pin]. The values |
| listed in the [Pin] description section override the default |
| values defined here. |
|------------------------------------------------------------------------------|
[Package]
| variable typ min max
R_pkg 250.0m 225.0m 275.0m
L_pkg 15.0nH 12.0nH 18.0nH
C_pkg 18.0pF 15.0pF 20.0pF
|==============================================================================|

## Slide 28: Body
[Pin] Required
[Pin] signal_name model_name R_pin L_pin C_pin |
1 RAS0# Buffer1 200.0m 5.0nH 2.0pF
2 RAS1# Buffer2 209.0m NA 2.5pF
3 EN1# Input1 NA 6.3nH NA
4 A0 3-state
5 D0 I/O1
6 RD# Input2 310.0m 3.0nH 2.0pF
7 WR# Input2
8 A1 I/O2
9 D1 I/O2
10 GND GND 297.0m 6.7nH 3.4pF
11 RDY# Input2
12 GND GND 270.0m 5.3nH 4.0pF
| .
| .
| .
18 VCC3 POWER
19 NC NC
20 Vcc5 POWER 226.0m NA 1.0pF
Notes: |==============================================================================|
| Keyword: [Pin] |
| Required: Yes |
| Description: Used to associate the component's I/O models to its various |
| external pins and signal names. |
| Sub-Params: signal_name, model_name, R_pin, L_pin, C_pin |
| Usage Rules: All pins on a component must be specified. The first column |
| must contain the pin name. The second column, signal_name, |
| gives the data book name for the signal on that pin. The |
| third column, model_name, associates the I/O model for that |
| pin. Each model_name must have a [Model] keyword below, |
| unless it is a reserved model name (POWER, GND, or NC). |
| |
| Each line must contain either three or six columns. A pin |
| line with three columns only associates the pin's signal and |
| model. Six columns can be used to override the default |
| package values (specified under [Package]) FOR THAT PIN ONLY. |
| When using six columns, the headers R_pin, L_pin, and C_pin |
| must be listed. If "NA" is in columns 4 through 6, the |
| default packaging values must be used. |
| |
| Column length limits are: |
| [Pin] 5 characters max |
| model_name 20 characters max |
| signal_name 20 characters max |
| R_pin 9 characters max |
| L_pin 9 characters max |
| C_pin 9 characters max |
|------------------------------------------------------------------------------|

## Slide 29: Model Key Word Examples
[Model] my_driver
Model_type Output
Polarity Non-inverting
[Model] my_reciever
Model_type Input
Vinl = 0.75V
Vinh = 2.0V
[Model] my_bi_dir_bus
Model_type I/O
Polarity Inverting
Enable Active-Low
Vinl = 0.75V
Vinh = 2.0V
Notes: |==============================================================================|
| Keyword: [Model] |
| Required: Yes |
| Description: Used to define a model, and its attributes. |
| Sub-Params: Model_type, Polarity, Enable, Vinl, Vinh, C_comp |
| Usage Rules: Each Input, Output, I/O, 3-state, or Open-drain model must |
| begin with the keyword [Model]. The model_name must match |
| the one that is listed under the [Pin] keyword and must not |
| contain more than 20 characters. An .ibs file must contain |
| enough [Model] keywords to cover all of the model_names |
| specified under the [Pin] keyword, except for those |
| model_names which use reserved words (POWER, GND and NC). |
| Model_names with reserved words are an exception and |
| they do not have to have a corresponding [Model] keyword. |
| C_comp is allowed to use "NA" for the min and max values only. |
| Other Notes: A complete [Model] description normally contains the following |
| keywords: [Voltage range], [Pullup], [Pulldown], [GND_clamp], |
| [POWER_clamp], and [Ramp]. However, some models may have only |
| a subset these keywords. For example, an input structure |
| normally only needs the [Voltage range], [GND_clamp], and |
| possibly the [POWER_clamp] keywords. |
| Note that C_comp defines the silicon die capacitance. This |
| value should not include the capacitance of the package. |
| |
|------------------------------------------------------------------------------|
[Model] model_name
Model_type Input, Output, I/O, 3-state, Open_drain | List one only
Polarity Non-Inverting, Inverting | List one only, if any
Enable Active-High, Active-Low | List one only, if any
| Signals RAS, CAS, A(0-64), D(0-128),... | Local list, if desired
Vinl = 0.8V | input logic "low" DC voltage, if any
Vinh = 2.0V | input logic "high" DC voltage, if any
| variable typ min max
C_comp 12.0pF 10.0pF 15.0pF
|==============================================================================|

## Slide 30: Body
[Voltage range] required
[Voltage range] 5.0V 4.5V 5.5V
Notes: |==============================================================================|
| Keyword: [Voltage range] |
| Required: Yes |
| Description: Used to define the power supply voltage tolerance over which |
| the model is intended to operate. |
| Usage Rules: Actual voltages (not percentages) are to be presented in the |
| usual typ, min, max format. "NA" is allowed for the min and |
| values only. |
| Other Notes: [Voltage range] also describes the voltage range over which |
| the various V/I curves and ramp rates were derived. |
|------------------------------------------------------------------------------|
| variable typ min max
[Voltage range] 5.0V 4.5V 5.5V
|==============================================================================|

## Slide 31: Converting a part to IBIS
With the Keywords covered thus far
  examine a data sheet
  identify some important parameters
  start building a model
Notes: How do we take readily available data and create a model. What questions should we ask

## Slide 32: Describing the driver
Overly simplistic view
  A driver has a single output impedance
Simplistic view
  A driver’s high state has a single impedance
  A driver’s low state has a single impedance
Behavioral view
  Driver has a single high and low curve

## Slide 33: Real ASIC Example
Lets look at a data sheet for a real part
  Create an overly simplistic view
  Create a simple view
  Look at the real curves
This example illustrates Good syntax but flawed analysis and data gathering. Don’t fall into this trap !
Notes: Readily available data may not be what you want.

## Slide 34
8 ma Buffer

## Slide 35
8ma Buffer

## Slide 36: Overly Simplistic Driver
The example 5 volt driver has a max current of 8 ma.
Using Ohms law V=IR you would expect the driver to have and output impedance of 625 ohms
Notes: Overly simplistic view

## Slide 37: Simplistic View
Closer inspection reviles that the lowest output voltage in the high state( Voh) is 2.4 volts. The 2.4 is measured with respect to ground so the delta voltage is 2.6 volts. If we use ohms law again and use this voltage we get 2.6v=(8ma)(325ohm)
On the Low output side we see Vol is .4v so 0.4v = (8ma)(50ohm)
This indicates that the high drive and low drive are very different.
Lets build a driver and simulate it to test this theory.
Notes: Is it getting any better ?

## Slide 38: End Points
Most simulators will take the two data points and extend them linearly in the active region during the simulation. Lets calculate the endpoints incase we need them.
If the low out put is 50 ohms what will be the V/I point at the rails.
0V = 0ma and 5V = 100 ma
For the high output 5V = 0ma and 0V = 15.3ma
Notes: Extrapolate some data.

## Slide 39: Flawed Data Gathering
We calculated to points thus far.
They won’t match the data points from the VI curves in the data sheets.
We used DC Max. operating data.
We really want data from normal operating region.
Lets use this data first then use normal data
Notes: We collected data from a corner case in the data sheet . We really want data from the operational region of the data sheet. The typical data will give us a feel for the performance of the device and best (fast process) and worst (slow process) case data will help us margin our design using the device.

## Slide 40: Building the Model
[IBIS Ver] 1.0
[File name] simple.ibs
[File Rev] 0.1
[Component] Simple_test
[Manufacturer] NONE
[Package]
| typ min max
R_pkg 10.0000m NA NA
L_pkg 2.0000nH NA NA
C_pkg 0.8000pF NA NA
Notes: Start by adding the IBIS version, add the file name and the revision. The component name used here “simple_test”. This name by be used by a simulator in a post rout simulation to match the components on the board to your models. The Manufacturer in the case is “NONE” because we are using suspect data to highlight the methodology.
The package characteristics were no included in the scanned in data sheets.

## Slide 41: Building the model
[Pin] signal_name model_name
1 D0 CMOS_I/O
[Model] CMOS_I/O
Model_type Output
| typ min max
C_comp 2.6000pF NA NA
[Voltage Range] 5.0000V NA NA
Notes: We only want to build a single pin device who’s pin number is 1. We want to assign it an name “CMOS_I/O”
The Model keyword will allow a simulator to connect pin 1 to the behavioral description of the pin.
We need to include the capacitance of the die and the operating voltage of the device.

## Slide 42: The Model is Taking Shape
We need to add the output behavior
  start with the simplistic view
but first the syntax

## Slide 43: [Pulldown] and [Pullup]
[Pulldown]
| Voltage I(typ) I(min) I(max)
|
-5.0V -40.0m -34.0m -45.0m
-4.0V -39.0m -33.0m -43.0m
| .
| .
0.0V 0.0m 0.0m 0.0m
| .
| .
5.0V 40.0m 34.0m 45.0m
10.0V 45.0m 40.0m 49.0m
|
[Pullup]
|
| Voltage I(typ) I(min) I(max)
|
-5.0V 32.0m 30.0m 35.0m
-4.0V 31.0m 29.0m 33.0m
| .
| .
0.0V 0.0m 0.0m 0.0m
| .
| .
5.0V -32.0m -30.0m -35.0m
10.0V -38.0m -35.0m -40.0m
|
[GND_clamp]
|
| Voltage I(typ) I(min) I(max)
|
-5.0V -3900.0m -3800.0m -4000.0m
-0.7V -80.0m -75.0m -85.0m
-0.6V -22.0m -20.0m -25.0m
-0.5V -2.4m -2.0m -2.9m
-0.4V 0.0m 0.0m 0.0m
5.0V 0.0m 0.0m 0.0m
|
[POWER_clamp]
|
| Voltage I(typ) I(min) I(max)
|
-5.0V 4450.0m NA NA
-0.7V 95.0m NA NA
-0.6V 23.0m NA NA
-0.5V 2.4m NA NA
-0.4V 0.0m NA NA
0.0V 0.0m NA NA
Notes: |==============================================================================|
| Keywords: [Pulldown], [Pullup], [GND_clamp], [POWER_clamp] |
| Required: Yes, if they exist in the device |
| Description: The data points under these keywords define the V/I curves of |
| the pulldown and pullup structures of an output buffer and the |
| V/I curves of the clamping diodes connected to the GND and the |
| POWER pins, respectively. |
| Usage Rules: In each of these sections the first column contains the |
| voltage value, and the three remaining columns hold the |
| typical, minimum, and maximum current values. The four |
| entries, Voltage, I(typ), I(min), and I(max) must be placed on |
| a single line and must be separated by at least one white |
| space or tab character. |
| All four columns are required under these keywords, however |
| data is only required in the typical column. If minimum |
| and/or maximum current values are not available, the reserved |
| word "NA" must be used. "NA" can be used for currents in the |
| typical column, but numeric values MUST be specified for the |
| first and last voltage points on any V/I curve. Each V/I |
| curve must have at least 2, but not more than 100, voltage |
| points. |
| Other Notes: It should be noted that the V/I curve of the [Pullup] and the |
| [POWER_clamp] structures are 'Vcc relative', meaning that the |
| voltage values are referenced to the Vcc pin. The voltages in |
| the data tables are derived from the equation: |
| Vtable = Vcc - Voutput |
| Therefore, for a 5V component, -5 V in the table actually |
| means 5 V above Vcc, which is +10 V with respect to ground; |
| and 10 V means 10 V below Vcc, which is -5 V with respect to |
| ground. Vcc-relative data is necessary to model a pullup |
| structure properly, since the output current of a pullup |
| structure depends on the voltage between the output and Vcc |
| pins and not the voltage between the output and ground pins. |
| Note that the [GND_clamp] V/I curve can include quiescent |
| input currents, or the currents of a 3-stated output if so |
| desired. |
|------------------------------------------------------------------------------|

## Slide 44: Ramp and End
[Ramp] Required
[Ramp]
| variable typ min max
dV/dt_r 4.2/1.8n 3.5/2.5n 5.0/1.1n
dV/dt_f 2.5/1.5n 2.0/2.3n 3.0/0.8n
[End]

## Slide 45: Adding Voh/Ioh and Vol/Iol
The Low state data (Vol/Iol) is “Pulldown”
High state data (Voh/Ioh) is “Pullup”
  The pullup data is referenced to Vcc not Gnd

## Slide 46
[Pulldown]
| Voltage I(typ) I(min) I(max)
0.0000V 0.0pA NA NA
0.4000V 8.0mA NA NA
[Pullup]
| The voltages in this table are referenced to Vcc and were generated such
| that Vtable = Vcc - Voutput.
| Voltage I(typ) I(min) I(max)
0.0000V 0.0pA NA NA
2.4000V -8.0mA NA NA
[Ramp]
| typ min max
dV/dt_r 2.5V/1ns NA NA
dV/dt_f 2.5V/1ns NA NA
[END]
Notes: We picked out two points and entered the data.
We want a 5ns rise time to 5volts which 2.5v/ns ramp rate.

## Slide 47: Look at the curves
Notes: The curve viewer show the linear section in-between our two defined points.

## Slide 48: Simulation Setup
Notes: We will use a our model (driver) to drive a 50 ohm transmission line with a 1ns delay (6 inches with 2.0ns/Ft)

## Slide 49: Simulation Results
Notes: Even though we told the model we wanted 2.5v/ns rise time you can see the rise time looks like it is about 30ns. The impedance is so high it takes lots and lots of reflections to to produce this wave form.
The second wave form is zoomed in on the leading edge and the length is doubled to show the reflections.
This is obviously a poor model for device but it is syntactically correct and simulates just fine.

## Slide 50: Extrapolated End Points
Notes: Change the model to use the zero and 5v data points.

## Slide 51: Pick some VI points
New data points from the data sheet
Pullup
Voltage Current
1.0 -73ma
2.0 -68ma
3.0 -55ma
4.0 -32ma
5.0 0.0
Pulldown
Voltage Current
0.0 0.0
1.0 41ma
2.0 72ma
3.0 92
4.0 96
Notes: Look back at the data sheet and pick off some points.

## Slide 52: Change the Pulldown
[Pulldown]
| Voltage I(typ) I(min) I(max)
0.0000V 0.0pA NA NA
0.4000V 8.0mA NA NA
[Pulldown]
| Voltage I(typ) I(min) I(max)
0.0 0.0 NA NA
1.0 41mA NA NA
2.0 72mA NA NA
3.0 92mA NA NA
4.0 96mA NA NA
Before
After
Notes: Add them to the model.

## Slide 53: Change the Pullup
[Pullup]
| The voltages in this table are referenced to Vcc and were generated such
| that Vtable = Vcc - Voutput.
| Voltage I(typ) I(min) I(max)
0.0000V 0.0pA NA NA
2.4000V -8.0mA NA NA
Before
1.0 -73ma
2.0 -68ma
3.0 -55ma
4.0 -32ma
5.0 0.0
5.0 0.0
4.0 -32ma
3.0 -55ma
2.0 -68ma
1.0 -73ma
[Pullup]
| The voltages in this table are referenced to Vcc and were generated such
| that Vtable = Vcc - Voutput.
| Voltage I(typ) I(min) I(max)
0.0 0.0 NA NA
1.0 -32mA NA NA
2.0 -55mA NA NA
3.0 -68mA NA NA
4.0 -72mA NA NA
After
Notes: The pullup section may be counter intuitive.

## Slide 54: New Curves
Notes: The curves with the new data points

## Slide 55: New Simulation Results
Notes: A dramatic difference in the simulation results

## Slide 56: Adjust the Time Scale
Notes: Adjust the time scale to get better resolution.

## Slide 57: Checking Syntax
IBIS Golden parser
HyperLynx visual IBIS editor
Model translators
  Viewlogic ibis2xtk
Others
Notes: When creating you own models you need a syntax checker.

## Slide 58: HyperLynx Visual IBIS Editor
Notes: Example

## Slide 59: More Data Points
Notes: Lets use a lot of data points and see the simulation difference.

## Slide 60: Lab1
Use a text editor to build a the two models from the previous slides. Check your syntax. Change the line length to examine the reflections
This process will vary by tool selection.

## Slide 61: Items To Add
Protection diodes
Rise / Fall data
  next simulation lab

## Slide 62: Other Topics
ftp/web sites for tools
IBIS cookbook
3rd party measured data
Correlation to measured data
  IBIS East Test Board
IBIS FAQ’s

## Slide 63: Feedback
Please e-mail feedback to joe@trilogic.com
Thank you for your time.