## Slide 1: Model Extraction based on Differential TDR
Dr. Steven Corey
TDA Systems, Inc.
steve@tdasystems.com

## Slide 2: TDR Block Diagram
(TDR source may actually be implemented as a Norton
equivalent current source)
Notes: Time Domain Reflectometry measurements have always been the measurement approach of choice for board characterization work. Based on TDR measurements, a circuit board designer can determine characteristic impedances of board traces, compute accurate models for board components, and predict board performance more accurately.
In a simple TDR setup, shown on this slide, incident waveform amplitude at the Device Under Test (DUT) is typically half the original stimulus amplitude V at the TDR source. The smaller DUT incident waveform amplitude is due to the resistive divider effect between the 50  resistance of the source and 50  impedance of the coaxial cables connecting the TDR sampling head and the DUT. The impedance of the board trace can be determined from the waveform measured by the TDR oscilloscope, Vmeasured, which is the superposition of the incident waveform at the DUT and the reflected one, offset by 2 electrical lengths of the cable interconnecting the oscilloscope TDR sampling head to the DUT.
Please note that in reality TDR source is a more of current source. This fine point can make it more obvious the effects that DC loading of the termination may have on the incident step amplitude.

## Slide 3: Differential TDR
Virtual ground plane
Even and odd mode measurements
Notes: Differential TDR measurements can come in handy when it is difficult to achieve good reference to a ground plane, or when a differential line analysis must be performed. Virtual ground plan, created by two TDR source of different polarity, arriving simultaneously at a device under test with clear symmetry, helps achieve the desired measurement results.

## Slide 4: Even and Odd Impedance Profile Example
Zeven>Zself>Zodd
teven>tself>todd
Note: - odd mode = differential measurement (two TDR sources of opposite polarity) - even mode = common mode measurement (two TDR sources of the same polarity)
Notes: Even and odd analysis, based on even and odd impedance profiles is an extremely useful TDR analysis tool for symmetric line systems, such as cables, connectors etc. Odd impedance profile is obtained from a differential TDR measurement with two TDR source of opposite polarity, and even impedance profile is obtained through a measurement with two TDR source of the same polarity. Differential reference short is used for computing the impedance profile

## Slide 5: Symmetric Coupled Line Model
Zodd, Zeven, todd, teven:
directly obtained from odd and even impedance profiles

Notes: This is a simple and accurate symmetric coupled lines model obtained from even and odd mode analysis. This model is accurate and rigorous; the only disadvantage is that you have to use 4 lines to model the coupled line structure.
Self test: demonstrate using basic circuit analysis techniques that this equivalent circuit will accurately propagate even and odd mode excitation (hint: the circuit will reduce to even only and odd only impedances in each case).

## Slide 6
Reduced Symmetric Coupled Model
assumes todd = teven

Note:
Notes: A simplified version of the same model can be used if one can assume that todd= teven - or if one can focus on one mode of propagation and disregard the other. For example, in case of differential signaling schemes, mainly the differential mode is excited. Therefore, one can assume that tmutual=todd and simplify the model.

## Slide 7
Computing L and C from Even- and Odd-mode parameters
Notes: If the lines have constant impedance, the computation becomes even simpler.

## Slide 8: TDR Measurement Setup
Leads being measured are symmetric
TDR pulses are symmetric
TDR pulses arrive at the DUT at the same time
Notes: Differential TDR measurements can come in handy when it is difficult to achieve good reference to a ground plane, or when a differential line analysis must be performed. Virtual ground plan, created by two TDR source of different polarity, arriving simultaneously at a device under test with clear symmetry, helps achieve the desired measurement results.

## Slide 9: Even and Odd Impedance Profile Example
Zeven>Zself>Zodd
teven>tself>todd
Note: - odd mode = differential measurement (two TDR sources of opposite polarity) - even mode = common mode measurement (two TDR sources of the same polarity)
Notes: Even and odd analysis, based on even and odd impedance profiles is an extremely useful TDR analysis tool for symmetric line systems, such as cables, connectors etc. Odd impedance profile is obtained from a differential TDR measurement with two TDR source of opposite polarity, and even impedance profile is obtained through a measurement with two TDR source of the same polarity. Differential reference short is used for computing the impedance profile

## Slide 10: Symmetric Coupled Model Example
(Coupled vs. uncoupled regions)

## Slide 11: Model Verification

## Slide 12: Conclusions
Differential measurement-based modeling approach
Useful for characterizing symmetric coupled conductors (connectors, package leads, board traces)
Models are valid for both differential and common-mode use
Parameters are compatible with proposed IBIS connector spec
Extension to n conductors(?)