## Slide 1
Proposed Improvements to the SPICE to IBIS Tool
October 14, 1999
Mohamed Nasef
mohamed_nasef@mentor.com

## Slide 2: Agenda
Introduction
VI Curves Improvements
Waveform Improvements
Summary

## Slide 3: Introduction
Avoiding the double counting in the pull up and pull down VI curves
Modeling the internal pulling termination behavior
VI curves extrapolation
Better waveform’s resolution for better IBIS models
Different simulation time for each waveform

## Slide 4: VI Curves Improvements
Avoiding double counting
  For the 3-state buffers, the original tool double counts the power clamp in the pull down and the ground clamp in the pull up.
  To avoid this double counting, the improved tool combines the power & ground clamp simulations into one DC sweep (from -Vcc to 2Vcc) and then subtracts it from both the pull up and the pull down.
  Power & ground clamp curves can be extracted from this sweep.

## Slide 5
Original tool pull down curve
Power clamp double counting
Improved tool pull down curve
No double counting
Pull down curve including clamps
Power & Ground clamp curve

## Slide 6
Modeling internal pulling termination
  The original tool uses the same technique for the buffers having or not having internal pulling (up or down) termination giving inaccurate IBIS models.
  The improved tool puts the internal pulling down behavior in the ground clamp table and the internal pulling up behavior in the power clamp table giving accurate IBIS models.
  A comment in the *.s2i file is used so that the tool could recognize that this buffer has internal pulling termination.
[model type] 3-state
| internal pull up termination

## Slide 7
Power Clamp
Ground Clamp
Internal pull up example
Internal pull up behavior exists
in the power clamp curve
Internal pull up behavior exists
in the ground clamp curve

## Slide 8
VI curves extrapolation
  In some cases, we may need to extrapolate the VI curves.
  There are three options for extrapolation:
    No extrapolation
    Horizontal extrapolation
    Linear extrapolation

## Slide 9: Waveform Improvements
Better waveform resolution

## Slide 10
Falling waveform comparison
Rising waveform comparison

## Slide 11
Different simulation time for each waveform
  As the maximum number of points per table is 100 points, so, the shorter the simulation time, the better the resolution.
  In the original tool, the minimum limit of the simulation time is set by the slowest waveform.
  In the improved tool, each waveform has its own simulation time.
  This is done by modifying the [Rising Waveform] and the [Falling Waveform] keywords sub-parameters in the *.s2i to be:
R_fix, V_fix_typ, V_fix_min, V_fix_max, C_fix, L_fix, R_dut, L_dut, C_dut, sim_time

## Slide 12
  For example:
  whereas in the original tool the simulation time for all the waveforms will be 16ns.
Source: EDA Today, 1998
[Rising Waveform] 50 0 0 0 NA NA NA NA NA 12ns
[Rising Waveform] 50 3.3 3.0 3.6 NA NA NA NA NA 3ns
[Falling Waveform] 50 3.3 3.0 3.6 NA NA NA NA NA 16ns
[Falling Waveform] 50 0 0 0 NA NA NA NA NA 4ns

## Slide 13: Summary
Avoiding the double counting in VI curves.
Modeling the internal pulling behavior
Extrapolating VI curves
Waveforms with higher resolution
Different simulation time for different waveforms
Source: EDA Today, 1998