## Slide 1: Behavioral Receivers
Round Table Discussion Notes
IBIS Summit, Fall ‘99
Stephen Peters, Intel Corp.

## Slide 2: Introduction And Background
Effort started with June IBIS summit
Working group formed
  Richard Mellitz, Arpad Muranyi, Stephen Peters (Intel) DC Sessions (Philips)
Met in July, results was four related proposals
  bird 61 - input characterization
  bird 62 - enhance receiver specification
  bird 63 - documentation of setup/hold conditions
  bird 64 - (unwritten) receiver validation waveforms

## Slide 3: Bird 61 - Characterizing a Receiver
Theory is that receiver input -> output delay is dependent on input overdrive and edge rate
Create tables for ‘delta’ delay vs. overdrive and ‘delta’ delay vs. edge rate.
Assumption: with this data simulators can calculate parameters to a behavioral model.

## Slide 4: Bird 61 - Characterizing a Receiver (cont.)

## Slide 5: Bird 61 - Characterizing a Receiver (cont.)
Open Issues:
  How ya gonna use the data?
    look up table?
    Coefficients to an equation?
    Tweak/select a standard model?
  How much data is enough?
    table requires enough to cover “most” conditions
    need many tables, how does user know it’s enough for all
  No Input Model or equation yet defined

## Slide 6: Bird 62 - Enhanced Receiver Specifications
Problem: traditional Vinh/Vinl are inadequate
  far to much slop between high and low margin
  no clue as to what happens for signal ringback
  can’t adjust threshold for VCC/process variances
Solution: Allow user to spec four margins + Vth shift due to VCC/process variations

## Slide 7: Bird 62 - Enhanced Receiver Specifications (cont.)

## Slide 8: Bird 62 - Enhanced Receiver Specifications (cont.)
Key points
  Vinh/Vinl specified wrt threshold point (Vth)
  Vth allowed to vary with process (Vinh_min, Vinh_max) and VCC (Vth_sensitivity)
  Allows for Vth to be slaved to external supply ([External Reference] keyword)
Open issues:
  New keyword needed, can’t use [Model Spec]

## Slide 9: Bird 63 - Document Setup and Hold conditions
Documents under what conditions a devices setup/hold time are specified
Specing method similar to Bird63 (offset from threshold voltage)
Open issues:
  different slew rates needed for setup and hold?
  Vth=0 means differential input. Is there a better way to indicate this?