## Slide 1: An Escape Hatch for Leading Edge Simulation
Will Hobbs
Intel Corporation

## Slide 2: The Value of IBIS
IBIS broke the model availability logjam
  Prior to IBIS, many semiconductor vendors reluctant to offer I/O models. IBIS addressed many of their concerns
  IBIS protects IP through behavioral approach
  IBIS model creation tools are available, easing model creation
  Reasonable accuracy possible
  Simulations run quickly, enabling full board simulation, Monte Carlo, etc.
IBIS is strongly supported by EDA and electronics industries
IBIS continues to advance to meet emerging needs

## Slide 3: But, ...
IBIS trails the leading edge
  Keywords and techniques must continually be invented to keep up with leading edge
  Technology is not slowing down. New challenges:
    Increasing speeds: 200, 400, 800, … MHz
    Decreasing operating voltages
    Decreasing margins: millivolts and picoseconds matter
    MP loading, MP traffic, complex packages and layout topologies
    New technologies and buses: spread spectrum, PCI-X, DDR, ...
    Subtle effects continue to increase in prominence: Ground return path, ISI, ...
  The stakes continue to rise
    Intro delays due to resonance, recalls due to power delivery -> $$
Critical circuits must be modeled at different levels of detail
An escape hatch for leading edge requirements needed

## Slide 4: Example: Recent Modeling Approach
Total delay analysis encompasses complete path from input of output buffer to output of input buffer
  Driver and Receiver modeled at transistor level, with 3D package
  Necessitated working with specific vendors, requiring customers to use only those vendors for this part of their simulation
  Incompatible with IBIS
Board traces, interconnect
Driver
Receiver
IBIS Domain
Span of this method

## Slide 5: Why API?
Needed: A way for customers to use emerging modeling techniques without being locked into specific simulators. IBIS is always playing catch-up.
Any “escape hatch” should meet the following criteria:
  Protect IP
  Be flexible enough to support unforeseen modeling techniques
  Be vendor neutral
  Allow IBIS simulators to meet leading edge needs quickly
An C-procedural interface can meet these needs, and provide support for:
  Equations with arbitrary math libraries
  C-based models
  AHDL
  Encrypted full transistor level models compiled with simulation kernel: SPICE or proprietary kernel
  3D modeling of specific I/Os
  Complex input buffers
  Dynamic compensation adjustment
  ...

## Slide 6: XMI: External/Executable Model Interface
Objectives:
  Allow arbitrary models to interoperate with IBIS simulators
  Support model portability between compliant simulators, though they might be platform-dependent
  Support model inter-operability. I.e., “X-models” from different vendors can coexist in same session.
  Protect IP. E.g., encrypted C models.

## Slide 7: Possible Parallel: OMI
Possible parallel from the logic domain: “Open Model Interface,” IEEE 1499
  May offer hints at how to implement XMI
  Solved logical issues that have analogies in the analog world:
    Initialization, parameter exchange, instantiation issues, pinlists, ...
    Two-way passing of simulation stimulus and results between simulator and models
    Support for multiple models, model libraries, independent simulation kernels
    Making selected internal model structure visible to parent simulator and user
  XMI would likely be simpler
    Support for timestep only, not events and clocks
    Simpler state resolution
    Fewer variables of interest

## Slide 8: A Quick Look at OMI
Models interface to parent simulator through a Model Manager, which controls and supports an arbitrary number of model instances. Multiple Model Managers allowed.
Interaction between the Model Manager and its Models is private

## Slide 9: OMI, Continued
A model can be packaged separately or as part of a model library.
A model supplier may provide a model and a model manager as a single executable, as separate components, or as a collection of linkable objects.

## Slide 10: Summary
“Escape Hatch” is needed to meet emerging challenges
API offers flexibility, while protecting IP
May be able to draw on work done on IEEE1499
Suggest:
  Committee consider API. If desirable:
    Create requirements document
    Study available existing technology for adaptation
    Formalize proposal
    Implement and Standardize