## Slide 1: A Proposal for Developing S2IBISv3
Paul Franzon
Michael Steer
Automated Design Tools for Integrated Mixed Signal Microsystems (NeoCAD)
Notes: 1

## Slide 2: Outline
Background
DARPA Program “NeoCad”
  Program Objectives
  Program Approach
Support for IBIS Community
  Detailed Technical Approach
  Future Planning Support
Timeline and Feedback
Conclusions

## Slide 3: Background
ARMM Group
  Analog, RF and Mixed Mode
  Strong industry connections and support
  Large base of Federal Funding
Proud of previous contributions to IBIS Community

## Slide 4: DARPA project … Big Picture
Implementation of advanced modeling and simulation abstractions, fast linear and nonlinear solvers, full-wave EM modeling for on-chip parasitics and integrated RF/microwave circuit design and modeling, digital and analog behavioral modeling, optoelectronic modeling and electrothermal modeling.
Plans and Team
DIGITAL BEHAVIORAL MODELING AND SSN MACROMODELING
Paul Franzon
GLOBAL ENVIRONMENT
Michael Steer, PI
PARASITIC EXTRACTION AND FULL WAVE MODELING OF INTERCONNECT
Andreas Cangellaris University of Illinois Urban Champaign
OPTOELECTRONIC MODELING
Mark Neifeld
Impact: A mixed-signal modeling capability that incorporates full-wave (EM) modeling of on-chip interconnects linked into a robust global simulation environment that provides a universal simulation environment for modeling.
Development of physical device models and optoelectronic device models linked into global simulation environment.
NC STATE UNIVERSITY
NC STATE UNIVERSITY

## Slide 5: TRANSIM
Unique Feature:
Nonlinear devices models based on state variables:
This provides great flexibility for the design of new models. All of the analyses are state-variable-based, including a time marching analysis (different integration methods available) and a unique wavelet transient analysis.
The state variables can be chosen to achieve robust numerical characteristics.
The calculation of derivatives are free of truncation errors at a small multiple of the run time required to evaluate the original function with little additional memory required. (ADOLC)
CONVENTIONAL DIODE MODEL
STRONG NONLINEARITY
v
i
v
x
x
NEW
NEW
MODERATE NONLINEARITY
+
i
x
v
=

## Slide 6: Parasitic and Interconnect Modeling
Model using
  Capacitance Extraction ?
  + Inductance Extraction ?
  Transmission Lines ?
  Full-Wave (full EM Modeling) 
Mixed Signal Chips
And Systems

## Slide 7
Technical Approach
PARASITIC EXTRACTION AND FULL WAVE MODELING OF INTERCONNECT
Approach and Issues:
Full-wave interconnect parasitic extraction.
Global surface impedance models capturing frequency-dependent field penetration inside conductors of arbitrary cross section.
Closed-form Green’s functions for the rapid calculation of interactions between electric charges and currents in multi-layered, lossy dielectrics. Planar, layered dielectrics need not be discretized.
Adaptive integral method (AIM)-based solvers, for the rapid iterative solution of interconnections in multi-layered substrates.
Unique Features:
Accurate capture of the broadband nature of the electromagnetic interactions, and thus account for all frequency dependencies in the interconnect medium that impact signal distortion, noise generation and coupling.

## Slide 8
Technical Approach
ON-CHIP DIGITAL BEHAVIORAL MODELING AND SSN MACROMODELING
Approach and Issues
Macromodeling tool for automatic accurate reduced-order SSN modeling of on-chip digital structures from full circuit description.
Unique Features
A macromodel production tool (similar to Spice2IBIS); Complete SSN macromodel conversion tool.

## Slide 9: Extracts of Requirements of S2IBIS3 Issued by IBIS sub-committee Outline
Scope of the Project
General Requirements
Specific Requirements
Documentation
Acceptance Criteria

## Slide 10: Scope of S2IBIS3 Project
OS Platform Independence
Generate a user-friendly IBISv3.2 compliant SPICE-to-IBIS translator runs on multiple OS platforms and be easily up-gradable to meet the requirements of future IBIS standards
Should support LINUX, AIX, HP, Windows 2000 among other platforms using a single Makefile
  (Code will be developed in the gnu environment. The same makefile can be used on 26 known operating systems with no code changes.)
We will use C++, for coding and JAVA for graphics.
Should be portable (Though it is mentioned that LEX/YACC should be avoided, We will use FLEX/BISON and achieve portability through GNU environment and Cygwin in MS Windows.)

## Slide 11: Hooks to other SPICE Engines
Testing S2IBIS3 on BerkeleySPICE2G.6, SPICE3 and HSPICE
Should have hooks to SPICE2G.6, SPICE3 and commercial SPICE simulators through configuration files
Use of SpiTranGUI (JAVA based freeware from Cadence) and possible incorporation into S2IBIS3

## Slide 12: Other Features
Graphical viewer to plot VI and VT tables (We plan to do it in JAVA)
Parser Integration for automatic validation of the output IBIS files
Project Manager for file and library maintenance

## Slide 13: Specific Requirements
Flexibility to extrapolate VI data
Flexibility to define the sweep range for VI tables
Rectification of clamp problem in S2IBIS2
Option of Ramping up Vdd (rather than single step)
Implementation of .OPTIONS feature supported by SPICE compatible simulators for non-convergence issues

## Slide 14: …Requirements
Debug through GUI control
[Iterate] feature in S2IBIS2 to be carried over
User selectable Voltage step, Time step, Sweep speed support
User selectable number of data points, decimal accuracy
Choice of choosing between the TYP, MIN and MAX instead of all process corners

## Slide 15: Features
Correction algorithm to avoid double counting for buffers with on-die termination
Cross-checking VT curves against VI curve-load line intersection and subsequent correction
Guardbanding feature for VI and VT curves
Intelligent pin list to avoid repetition of equivalent models

## Slide 16: Documentation
README File with Contents of the package and Installation instructions
User guide with Contents, Algorithms and Tutorials
Code explanation with Flow chart of the project

## Slide 17
NCSU Goals
GNU Public License
C++ (Platform Independent using GNU, Cygwin)
Class Structure to support Digital and Analog Macromodeling -IBIS is a subset
Applicable to Board level modeling and modeling of segments of Mixed Signal Chips

## Slide 18: Programming Technology
S2IBIS 2
S2IBIS 3
No Graphics
Originally not portable
C Data Structures
LEX/YACC Input/Output
Graphics in JAVA
Portable through GNU environment(Cygwin in MSWindows)
C++ Classes
LEX/YACC Input/Output

## Slide 19: Research Agenda
Support for IBIS-X (IBIS-X + 1?)
  Provide SSN macromodelling
  Investigate 3-D models
  Test accuracy against full-fidelity simulations and measurements

## Slide 20: Validation
Against Spice
Against Measurement
Industrial Collaborators

## Slide 21: Conclusion
3-year DARPA effort
  Full fidelity modeling
  Digital macromodeling
  Strong Industrial Emphasis
Deliver Spice2Ibis3
Investigate issues for IBIS-X (+1?)

## Slide 22: Backup Slides
…

## Slide 23: Chip Macromodeling
IBIS INTERFACE
BEHAVIORAL MODEL
IBIS INTERFACE
BEHAVIORAL MODEL
CIRCUIT
IBIS INTERFACE
BEHAVIORAL MODEL
IBIS INTERFACE
BEHAVIORAL MODEL
Full Chip Model

## Slide 24
IC’S On a PCB
Model using
  Capacitance Extraction ?
  + Inductance Extraction ?
  Transmission Lines 
  Full-Wave (full EM Modeling) 

## Slide 27: Board Level Modeling
Development of a Digital Macromodeling technology to enable ICs to be incorporated in a PCB
Signal Integrity should be taken care of as well
Capture of SSN and Substrate noise