## Slide 1: IBIS-X Model Examples
Lynne Green
Cadence Design Systems, Inc.
lgreen@cadence.com

## Slide 2: IBIS 3.2 Pinlist
[PIN] signal_name model_name R_pin L_pin C_pin
|
1 Vcc Power
2 GND GND
3 Sig1 buffer1 0.1 6n 9p
4 Sig2 buffer2
There is a fixed I/O Topology
Values can be overridden
Things can be omitted (Input/Output)
But nothing can be added

## Slide 3: What is a Model?
The IBIS 3.2 “Circuit” Model
  Pre-defined topology
“Component” Model
  Pins and packages
“Buffer” Model
  Numbers, Vectors, and Data tables

## Slide 4: What is a Model?
The IBIS-X “Behavioral” Model
  Model maker defines topology
“Component” Model
  Pins and packages
“Buffer” Model
  Numbers, Vectors, and Data tables

## Slide 5: Defining a Simple Model
[Define Model] my_driver
| Using a pre-defined model based on IBIS 3.2
| This defines the power/gnd/pad/pin nodes
.inherit model_base
| Add a voltage-dependent cap between output pin and Vcc
capacitor c_top1 (pad vcc) C = [C_top] (V.pad)
| Add a temperature-dependent pullup resistor
resistor R_up (pad vcc) R = [R_pull] (Temperature)
[End Define Model]

## Slide 6: Model Data
[Model] buffer1 | a name to use in the pinlist
model_type my_driver | which model_type uses this data
| followed by all the data required for my_driver models
C_comp 3pF 2pF 4pF
[Supply Voltage] 3.3v 3.0v 3.6v
[C_top]
0 1p
3 3p
[R_pull]
0 10k
125 20k
[End Model]

## Slide 7: Model Data
[Model] buffer2 | a name to use in the pinlist
model_type my_driver | which model to use
| a second buffer, same type, new data
C_comp 12p 6p 20p
[Supply Voltage] 3.3v 3.0v 3.6v
[C_top]
0 1.5p
3 4.0p
[R_pull]
0 8k
75 4k
[End Model]

## Slide 8: IBIS-X “Behavioral” Models
Behavioral model concepts
  Add components that model effects (such as vsource)
  Symbolic values (such as C_comp)
  Tables and equations for components
  Time, Temperature, etc.

## Slide 9: IBIS-X Primitives
Resistor
Capacitor
Inductor
Voltage source
Current source
Voltage-controlled voltage source
Voltage-controlled current source
Transmission lines (including coupling)

## Slide 10: IBIS-X Primitives
Resistor Examples
resistor R1 (n1 GND) R = 10k
resistor r2 (12 13) R = (10k * (1+ (Temperature-273)*0.001))
resistor a1 (VCC v1) R = (123 * v.v1 / Vcc)
resistor a2 (na GND) I = TABLE [Series MOSFET](v.na)
resistor a3 (nc, nd) V = TABLE [Table_x](i.nd)

## Slide 11: IBIS-X “Behavioral” Models
Model Maker provides
  Model behavior
  Model data
  Pinlist
User provides
  Pinlist (such as FPGA)
  Model Selector