## Slide 1: Progress and Update on the Connector Specification
Stephen Peters,
Intel Corp.

## Slide 2: ICM Specification Progress
Spec review – keyword and sub-parameter conformance to IBIS conventions
  Review of header information complete
  About ¾ the way thru connector description itself
  Various keywords eliminated, others changed
Progress on matrixes
  Added “G” matrix, most likely will add support for freq dependent simulations
  Both existing IBIS RLGC matrix and ‘S-parameter’ (touchstone format) data are being considered
With current progress, look for spec end of Jan, 02
  Caveat: no significant technical issues w/remaining items.

## Slide 3: What (Significantly) Changed?
Added conduction (G) matrix
Added “even_mode”, “odd_mode”, “quiescent” model_types
  Clarifies and adds conditions under which model data is extracted.
Went to [Path Description] type format for section descriptions
  Fork and EndFork replace Cn_stub
Several keyword changes relating to pin <-> matrix “row order” mapping.

## Slide 4: Comparison of Matrix Data Types
S-parameters
  ‘natural’ for freq domain simulators
  familiar to RF/connector folks
  Directly measurable (build model from measured data)
  Can directly extrapolate loss factors between frequencies
RLGC Matrix
  ‘natural’ for time domain simulators
  Familiar to SI engineers
  Not directly measurable (build models from field solver)
  Does not directly contain freq losses, there are questions about extrapolation