## Slide 1: Progress and Issues in IBIS-X
Stephen Peters,
Intel Corp.

## Slide 2: Current Status
Decision made to simplify path into IBIS
  Changes to IBIS template have been set aside for now
  Shortly after IBIS Ver. 4.0 is approved, expect to see a BIRD adding the [Define “class name”] keyword & concept
  Committee focusing exclusively now on macro language reference manual (IBIS-ML)
List of primitive elements agreed upon, including transmission line element
Enough of the ML spec has been written to start review of text
Based on current progress, expect spec end of Jan ‘02

## Slide 3: Where are we now
Technical Milestone tracking list
  syntax rules -- some work, documentation in flux
  primitive elements -- agreed on set, but need the operations
  netlist syntax -- done
  built in behavioral elements -- not yet discussed/documented
  programming constructs -- discussed and documented
  declarations -- documented, but need more
  data types -- documented, pretty solid
  matrix format -- discussed, not completely documented
  ISSUES:
    column selection (how to be done), needs to be put into LRM
    table interpolation types needs to be documented.

## Slide 4: The [Define “class name”] keyword
Syntax:
[Define “class_name”] “type name” (<optional port list>)
|
| IBIS-ML Constructs
|
[End “class name”] “type name’
[Define] keyword can be used in IBIS file itself – or – [Defines] are collected into a library file
Once an object is defined, it is customized as shown:
[Begin “class name”] “object name”
“class name”_type “type name”
|
| optional data specific to this instance
|
[End “class name”]
Object customization takes place in the IBIS file