## Slide 1: Power/Gnd Simulation Using IBIS Models and Pin Mapping Issues
Raj Raghuram
Sigrity, Inc.
IBIS Summit Meeting, Sep. 13, 2001

## Slide 2: Outline
Motivation – automated Power/Gnd simulation
Example of Power/Gnd simulation and effect of decaps
Examples of package pin layouts
How pin mapping helps automation
Suggestion for IBIS models to improve automation

## Slide 3: Simulation Assuming Ideal Power/Gnd Planes
GND
VCC
There is no need to know which GND and VCC pins of package drivers and receivers are connected to
GND
VCC
IN
OUT
IN
OUT

## Slide 4: Time Domain Simulation with Power/Gnd Structure in Place
GND
VCC
IN
OUT

## Slide 5: Difference between Conventional SI Solution and Solution that takes Power/Gnd Fluctuations into Account
Conventional SI does circuit + transmission line + pin RLC simulation assuming ideal ground and power planes
Advance SI/PI solution does a combined circuit + transmission line + (pin RLC) + nonideal ground and power plane simulation.
Can take care of
Power ground noise i.e. SSN or Delta-I or ground bounce
Effects of vias and return path discontinuity can be modeled
Effect of decoupling caps can be considered
Edge radiation from boards due to SSN can be calculated

## Slide 6: Use of IBIS Models in PWR/GND Analysis
For this pin mapping (absent in most IBIS files) is imperative.
In conventional SI simulation, directly simulating IBIS models eliminates the process of making models separately. Same can be true of PWR/GND analysis or Power Integrity
At Sigrity, we do a combined circuit/transmission line/power/gnd simulation with IBIS models in time domain. This can be directly done from layout, especially if IBIS models are available.
Two approaches to model pwr/gnd
Separately model pwr/gnd (maybe in frequency domain) and later do time domain simulation. Less automated, smaller structures and difficult to interface to layout

## Slide 7
Return Path Discontinuities and Simultaneous Switching Output (SSO)
G
P
power via
G
P
G
P

## Slide 8: Effects of Signal Return Path Discontinuity – Layer Geometry
S
P
S
S
G
S
Drivers
Receivers
200 m
200 m
300 m
300 m
300 m
5 cm
5 cm
5 cm
Trace width = 200m; Trace thickness=35.6m; Trace separation = 4 mm;
Series matching resistance= 55 ;
Drivers and Receivers are IBIS models from part 74LVC125A
Via
Via

## Slide 9: Top and Bottom Layers of the Board
Drvr Column
Rcvr Column
Via Columns
Decoupling capacitor columns
0805 Cap
C=1.0f
L=0.95nH
R=20m
0603 Caps
C=0.1f
L=0.8nH
R=50m
0603 Caps
C=0.1f
L=0.8nH
R=50m

## Slide 10: Voltage Waveforms at One Receiver As the Number of Simultaneous Switched Drivers Varies (no decoupling caps used)
Ideal Case: Trace in top layer
8 Drivers
4 Drivers
1 Driver

## Slide 11: Effect of Decoupling Caps on Receiver Voltage with 8 Drivers Switching Simultaneously
Ideal case: Trace in
Top layer
32 caps (0603)
plus 4 caps (0805)
No decoupling caps
4 caps (0805)
Max Overshoot/Undershoot
No decoupling caps: 772 mV
4 caps: 260 mV
36 caps: 49 mV
Ideal case: 39 mV

## Slide 12
Power/Gnd Voltage Historical Peak Surface Plot with and Without Decaps
No
Caps
With Caps
3.3 V at
Power supply location
4.6 V at Corner
3.4 V at Corner

## Slide 13: Power/Gnd Voltage Historical Peak Color Intensity Plot with and Without Decaps
No
Caps
With Caps

## Slide 14: Effect of Decoupling Caps on Edge Radiation
No decoupling caps
36 decoupling caps
Edge radiation was calculated corresponding to waveforms in the previous slides. The higher power-ground noise without decoupling caps leads to much higher edge radiation. This was measured at a horizontal distance of 3m and a vertical distance of 3m from the board

## Slide 15: Situations where Pin Mapping Essential
Many power and ground pins in one IC
More than one power supply – say 3.3V and 2.5V
Separate power pins for Core and I/O parts of IC
Pullup and power clamp may go to different power pins or pulldown and gnd clamp may go to different pins
Separate analog and digital ground pins

## Slide 16: Pin Configuration ABT244
Many VCC and GND pins. Probably all VCC connected
together inside IC. Same for Gnd. If we are simulating drivers on this IC,we connect their VCC to all VCC pads of this package on the PCB. But this is an assumption
Pad on PCB
Drvr 1
Drvr 2
Circuit part
7
18
42
31

## Slide 17: Pin Configuration for MPC951
There are separate analog and digital GND
and VCC pins. They are probably not
joined together inside the IC. So the
VCC for the buffers must come from
VCCO and not VCCA. It is even
possible that different drivers get their
VCC from different VCCO pins. This information needs to be given in the
pin mapping in order to do POWER/GND
simulations.
VCCO
VCCO
VCCO
VCCO
VCCO
VCCA
Drvr1
Drvr2

## Slide 18: Pin Configuration for IDT71V35761
Separate VDD and VDDQ pins
VDDQ – I/O pin supply
VDD – Core Logic supply
Pin Mapping given for this part
Pullup for drivers goes to VDDQ
Power clamp goes to VDD

## Slide 19: Pin configuration for CYPRESS W150
Has VDDQ2 and VDDQ3 supplies.
VDDQ2 = 2.5 V
VDDQ3 = 3.3 V
Pin Mapping given for this part

## Slide 20: Example of Pin Mapping (Cypress W150)
[Pin] signal_name model_name R_pin L_pin C_pin
1 VDDQ3 POWER 70.00m 8.00nH 1.40pF
2 REF1/FS2 ioref1x 80.00m 9.00nH 1.40pF
4 GND GND 65.00m 7.00nH 1.40pF
7 VDDQ3 POWER 40.00m 6.00nH 1.40pF
10 GND GND 40.00m 3.50nH 0.85pF
29 48MHz/FS1 iofd48 80.00m 7.00nH 1.40pF
50 VDDQ2 POWER 55.00m 4.50nH 1.40pF
[Pin Mapping] pulldown_ref pullup_ref gnd_clamp_ref power_clamp_ref
1 NC PWRBUS1
2 GNDBUS1 PWRBUS1
4 GNDBUS1 NC
7 NC PWRBUS2
10 GNDBUS2 NC
29 GNDBUS2 PWRBUS2
50 NC PWRBUS4

## Slide 21: Conclusions
Pin Mapping section essential in IBIS Models to do power/gnd simulation.
Power/Gnd simulation is a zeroth order effect. Accuracy of IBIS model may be a secondary issue for many situations.
When pin mapping is available, a completely automated linkage of circuit models during board translation beocmes possible. This is true even for power/gnd analysis.