## Slide 1
Modeling the Radiated Emission of Micro-controllers
Etienne Sicard
etienne.sicard@insa-tlse.fr
http://intrage.insa-tlse.fr/~etienne
Etienne SICARD
AUTOMOTIVE SA
Christian MAROT
André PEYRE LAVIGNE
Claude HUET

## Slide 2
Contents
1. Context of the study
2. System design methodology for EMC
3. The IERSET project on EMC for ICs
4. Core emission model
5. Emission model with Ios
6. Emission model in TEM cell
7. Conclusion

## Slide 3
0.7µm, 2 metal layers
Up to 100,000 devices on a chip
CPU frequency 50MHz
0.12µm, 6 metal
Up to 200,000,000 devices
CPU frequency 1GHz
1991
2001
IC
1000 pins
40 pins
10 years of
evolution
1. Context of the study

## Slide 4
Stronger di/dt
Scaled current
Voltage supply decreases
Current amplitude keeps constant
Faster switching
Increased EMC problems
Time
di/dt
Voltage
Current
di/dt
Voltage & Current
1. Context of the study

## Slide 5
MHz
dBµV
0
20
40
60
80
100
10
100
1000
FM
GSM
RF
Ultimate target
Supplier A
Supplier B
10dB
40dB
Probably EMC compliant
Not EMC compliant
Low parasitic emission is a key argument
1. Context of the study

## Slide 6
Interference with local RF & Bluetooth links
433 MHz, 2.5GHz
Interference with
mobile phone
900, 1800,1900MHz
1. Context of the study
Example for automotive
Parasites internal devices (ABS)
Similar EMC problems in aerospace

## Slide 7
2. System Design Methodology for EMC
DESIGN
Architectural
Design
Design Entry
Design Architect
FABRICATION
Version n°
EMC Measurements
GO
NO GO
+ 6 months
+ $$$$$$$$
Compliance ?
Version n°
EMC compliant
Obsolete Design Methodology
System on chip
specification

## Slide 8
1. Context of the study
2. System Design Methodology for EMC
Obsolete Design Methodology
PCB design
Prototype board
EMC scan
frequency
dB
peaks
Electromagnetic incompatibility found too late

## Slide 9
DESIGN
FABRICATION
EMC compliant
EMC Simulations
Compliance ?
GO
2. System Design Methodology for EMC
Target Design Methodology
System on chip
specification
Architectural
Design
Architecture
Guidelines
Training
Design Entry
Design Architect
Design
Guidelines
IC Models
Tools

## Slide 10
2. System Design Methodology for EMC
Target Design Methodology
PCB design
With IBIS and
core model
Good forecast of radiated
emission
A core model is mandatory for accurate emission prediction
With IBIS
Wrong prediction of the radiated emission

## Slide 11
2. The IERSET project
European Research Centre on Electronics for Transportation identifies and co-ordinate co-operative research.
AIRBUS
TOULOUSE
AUTOMOTIVE SA
Objectives
Definition and validation of a model to be used in PCB CAD tools to guarantee the EMC of electronic systems
One model from 1MHz to 1GHz, for conducted and radiated emission
Project EMC for ICs

## Slide 12
2. The IERSET project
ICEM (Integrated Circuit Electromagnetic compatibility Model)
Technical work at IERSET Toulouse, France
1997-2001
Draft standard
UTE
France
02/2001
05/2001
Commitee Draft for Voting 62014-3
ICEM
Cookbook
version 1.c
aug. 2001
08/2001

## Slide 13
2. The IERSET project
ICEM presentations
03/01
IBIS summit
Munich
Presentation
IEC 93
Singapoure
Presentation
01/02
EMC compo
Toulouse
Presentation
Paper IEEE EMC
09/01
IBIS meeting
Pres. to Mentor
Presentation
Date 02
Paris
03/02
IEC 93
Presentation
EMC Europe
09/02
CEM 02 Grenoble
IBIS meeting
Pres to Zuken
Paper IEEE Pack.

## Slide 14
Ib
Rvdd
Cd
Lvdd
Rvss
Lvss
Cb
External VDD
External VSS
IC model
4. Core Emission Model
ICEM includes a simple core model, not handled by IBIS
Basic parameters
Cd, Ib
Advanced param.
R,L,Cb
-10
0
10
20
30
40
50
60
70
80
1
10
100
1000
f (MHz)
dBµV
Measurements
Simulation Cd, Ib
Peak harmonics
Primary resonance
Secondary
resonance
All parameters

## Slide 15
4. Core Emission Model
Current generator estimation
Physical Transistor level (Spice)
Gate level Activity
Interpolated Transistor level (Powermill)
Huge simulation
Limited to analog blocks
Difficult adaptation to usual tools
Limited to 1 M devices
Simple, not limited
Fast
Not very accurate
Equivalent
Current generator Ib

## Slide 16
5. Emission Model with IOs
Comparison between simulation and measurement on a 16 bit micro-controller
Validation for a 16 bit micro-controller
Within 10dB, but I/Os not handled
-10
0
10
20
30
40
50
60
70
80
1
10
100
1000
f (MHz)
dBµV in conducted mode
Simulation (PSPICE)
EMC model
Measurement (Conducted 1)

## Slide 17
5. Emission Model with IOs
Add IBIS I/O data
Zsub: basically a 1-10 serial resistance
Cio : decoupling capacitance for IO supply
IO block: reuse of IBIS
Ib
Rvdd
Core VDD
Core VSS
Cd
Lvdd
Rvss
Lvss
Cb
I/O
Zsub
I/O VSS
I/O VDD
Cio

## Slide 18
5. Emission Model with IOs
Validation
IO modify the spectrum at high frequencies (>300MHz)

## Slide 19
6. Emission in TEM cell
Cdie_gnd
Lpackage
Lseptum
50 
50 
Chip under test
Cdie_septum
KCoupling
To PCB
Receiver
Chip under test
PCB
Proposed model: capacitance & inductance coupling

## Slide 20
6. Emission in TEM cell
Model fits correctly up to 400MHz
At high frequencies, close from noise floor
Validation for the core alone

## Slide 21
6. Emission in TEM cell
Validation for the core & IOs
Model fits correctly up to 800MHz
At high frequencies, IO effects dominate

## Slide 22
Conclusion
Technology scale down illustrated
More complex chips increase parasitic emission
An EMC model for Ics is mandatory
A simple model has been proposed
Satisfactory prediction of conducted emission
Prediction of the core emission in TEM investigated
Model proposal standardized by UTE (ICEM)
Presentation and promotion to CAD & IC providers