## Slide 1: IBIS PARSER BUG90 Ad-Hoc Presentation
Robert Haller
rhaller@sisoft.com
Signal Integrity Software, Inc.
978-461-0449 X 15
Notes: Introduce Self and Company
SiSoft – EDA and consulting
Self - Software,Hardware (IC,PWB and LAB ) and PWB manufacturing.
Today I’m will give my opinions on PASS/FAIL criteria for high speed digital interfaces and answer Greg’s 2 questions

## Slide 2: What is BUG90 About
If an IBIS file has a Vmeas outside Vih/Vil no warning is issued.
  I.e. Vmeas = 1.65V, Vinh = 1.6V, Vinl = 0.9V
In most cases this is representative of a flawed IBIS File
  This parser check only applies to I/O's
The IBIS Quality Committee proposes that a new Parser warning message be created. The "Caution" would be created to add a class of checks to significantly enhance the present IBIS Parsers capability.
  The new checks would be enabled with a command line switch to minimize additional spurious warnings for traditional IBIS model users, but will aid the model creator, reviewer and advanced users with enhanced automatic IBIS parser checking capability.
One reason why the Vinl and Vinh enclose Vmeas check is a caution is because there are legitimate cases, but predominantly its a mistake if this is done.

## Slide 3: BUG90
Good News
  Accepted and classified by IBIS open Forum !
Bad News
  Is IBIS parser Funding adequate ?

## Slide 4: What Do you think ?
Push one caution through
Prioritized list of cautions
Deprecate some warnings to cautions
Identify cautions (missing checks) that should be warning

## Slide 5: Partial List
[Comment Char] - Changing the comment character is not advised.
[Package] Parasitics must be reasonable - Reasonable values are: L<10nH, C<20pF, R<1 ohm
[Pin] RLC complete - RLC is optional on pins. If not defined either leave blank or use
[Diff Pin] Vdiff and Tskew complete and reasonable-Vdiff defined and should be non-zero and positive
[Model] C_comp is reasonable - C_comp must be defined, positive and less than 20pF
[Model] C_comp is correct-C_comp must represent the TOTAL die capacitance as specified in data sheet
[Model] Vinl and Vinh enclose Vmeas - For I/O buffers Vinl and Vinh values should be below and above,respectively,Vmeas .LEVEL 0 [Model Spec] Vinl+/Vinh+ greater than Vinl-/Vinh- - Vinh+ is greater than Vinh-, and Vinl+ is greater than Vinl-
[Model Spec] Vinl+/- and Vinh+/- enclose Vmeas
[Model Spec] Pulse_time reasonable - Pulse_time is less than the minimum rise time and fall time
[Model Spec] S_Overshoot subparam complete -All input and I/O buffers have S_overshoot_high and S_overshoot_low
I-V tables have correct typ/min/max order-Area calculation
[Pullup] voltage sweep range is correct-The sweep for [Pullup] should be made between -vcc to 2*vcc
[Pulldown] voltage sweep range is correct-The sweep [Pulldown] should be made between -vcc to 2*vcc
[Power Clamp] voltage sweep range is correct - The [Power Clamp] should turn on near supply voltage
[GND Clamp] voltage sweep range is correct-[GND Clamp] should turn on ~ one Diode drop below 0.0