## Slide 1: IBIS “Over Clocking” Case
Robert Haller
Eric Brock
rhaller@sisoft.com
Signal Integrity Software, Inc.
978-461-0449 X 15

## Slide 2: When Does “Over Clocking” Occur
VT curve time comparable to simulation data rate
  Excessive Dead time in VT curves
  Large variation between Slow and Fast VT Curves
Results in Unpredictable Simulator Behavior
  i.e. SPICE
  Others ?

## Slide 3: Example VT Curve
VT curve time small versus data rate (Final DC levels ~ 3.5ns)
  1 of 4 VT curves shown (Rise, Fall, VDD, Ground) ~ 1ns Delta

## Slide 4: Example Simulation
Simulation results 100 MHz (10ns Cycle time, 5 ns Data rate)

## Slide 5: Over Clocked Case – VT Before
VT curve time comparable to data rate
  Large delta between beginning of Fast and end of Slow Process corners ~.7ns

## Slide 6: Over Clocked Case – Simulation Before
Hspice versus IBIS Correlation
Simulation results 1.8 GHz ( 0.556 ns Data rate)

## Slide 7: Over Clocked Case – VT After
VT curve time Shifted
  Reduce delta between Fast and Slow Process corners (~ 450ps)

## Slide 8: Over Clocked Case – Simulation After
Hspice versus IBIS Correlation
Simulation results 1.8 GHz ( 0.556 ns Data rate)

## Slide 9: SiSoft Implementation
Implemented parameter (in .ibs file)
SiSoft uses “|Sisoft” parameters to augment IBIS capabilities
“|” character is a comment character for IBIS
  Industry tools will ignore
  |SiSoft is Keyword in SiAuditor / Quantum SI
SiSoft parameter used
  SPICE2IBIS processing
  |SiSoft VT_offset typ, min, max
Lost FF to SS timing relationship
  Comment in .ibs file to document this