## Slide 1: Version 3.2 Experience Modeling Fast, Two-tap Pre-emphasis Buffer
Bob Ross
IBIS Summit Meeting
DesignCon East 2005
Worcester, Massachusetts
September 19, 2005

## Slide 2: The Project Constraints
Semiconductor vendor
  Two-tap pre-emphasis buffer with On-Die Terminator (ODT)
  “Cannot be done in IBIS”
  Encrypted HSPICE under 3-way NDA
Customer (required IBIS Version 3.2)
  For specific IBIS tool (with no HSPICE access)
  Tool supports [Driver Schedule]
  Minimal customer IBIS knowledge
Business issue (several final deliverables)
  Two week delivery for four CML differential buffers within full 400+ pin ASIC model … after legal contract closure delays
Tips, experiences and unexpected issues here

## Slide 3: Other Related Discussions
Arpad Muranyi, March and January 2005, April 2004,
  Either enhanced or reduced buffer switched in
  Or main and one-bit delay boost
  Six individual edges and state machine for *_AMS solution with C_comp
Hazem Hegazy, LVDS Modeling, June, 2001
  Either enhanced or reduced buffer switched in
Michael Mirmak, C_comp Issues, October and April, 2004
  Factored out C_comp from V-T tables, but more work needed
Used Cookbook [Driver Schedule] pre-emphasis method
  Main and one-bit delay boost
Highlights of real issues, not the full process

## Slide 4: Project Factors
Process overview
  Isolate, test SPICE model from limited documentation
  Set up some SPICE extraction programs
  Set up spread sheet calculation pages for processing all the buffer setups
  Resolve unexpected situations
  Test the prototype IBIS buffer in the EDA tool
  Refine and deliver
Customer goal was timely design exploration
  No time for “perfect” solution or extensive research
  Compromises needed

## Slide 5: SPICE Configuration, Differential Control and [Driver Schedule]
MAIN
BOOST
TX+
TX-
Inverse 1-bit delays
Input bit pattern
[Driver Schedule]
| Model_name Rise_on_dly Rise_off_dly Fall_on_dly Fall_off_dly
MAIN 0 NA 0 NA
BOOST NA 0.47059ns NA 0.47059ns
IN+
IN-
+
-
+
-

## Slide 6: CML Structure with IBIS Open_drain Models, Connected by [Diff Pin]
Top-level
  ODT [Power Clamp]
  MAIN [Pulldown]
    Extracted waveforms with ODT & 50 
    Pre-emphasis = 0
  [Driver Schedule]
MAIN [Pulldown]
  Scaled waveforms
BOOST [Pulldown]
  Scaled waveforms

## Slide 7: Unexpected SPICE Offset and TX+ and TX- Differences
[Power Clamp] ODT predicts no offset from 1.8 V
  Added top-level [Gnd Clamp] to compensate for offset
  Some configurations go to 1.8 V
TX+ and TX- different, but no reason to model this
  SPICE code appeared symmetrical
  Used TX+ extractions as reasonable approximation
ODT [Power Clamp]
TX+
TX-
TX+
TX-

## Slide 8: SPICE TX+ and I-V Tables
Aligned SPICE typ-min-max I-V sweeps to get ODT as a [Power Clamp] and MAIN and BOOST [Pulldown] tables by subtraction
  ODT: High-state MAIN only for [Power Clamp]
  ODT+MAIN: Low-state MAIN for [Pulldown]
  ODT+BOOST: Low-state BOOST for [Pulldown]
Removed (out of range) non-monotonic data
Top-level [Gnd Clamp] mismatch adjustment for actual “1.8 V” high side levels, when needed

## Slide 9: Time Extraction from TX+
50  to 1.8 V, no pre-emphasis captures MAIN plus ODT reference waveform
Set R_fixture=25  for MAIN and BOOST Open_drain buffers
  Used ibischk4 to determine low end-point of swing (high is Vdd)
  Scaled the reference waveform
  Keeps MAIN over about same voltage range
  Correlates MAIN, BOOST delays
  C_comp=0 pF (more later)
Reference waveform for TX+ rising edge
(Falling edge reference for TX+ not shown)

## Slide 10: Unexpected Correlation Issues
IBIS leading edge truncation and slope difference skews
Ending levels near (non-symmetrical) SPICE levels
IBIS TX+, TX- same, out of phase
SPICE
IBIS
IBIS
SPICE

## Slide 11: Tested with C_comp (later)
Unexpected IBIS shift without response degradation
Either a tool or tool setup issue, but could produce better (tool dependent) results
IBIS
SPICE

## Slide 12: Expected C_comp Degradation
C_comp in IBIS [Driver Schedule]
  IBIS should add C_comp as top-level load
  Buffer impedance reduces driving mode degradation
  (Bad??) IBIS choice
Up to 3 pF, 25  = 75 ps time constant or about 165 ps rise time degradation (less with pulldown impedance)
Simulation rise time of less than 100 ps
Total rise time approximately sqrt (t12 + t22) or 193 ns (or less)

## Slide 13: Further C_comp Investigation
Compensate using C_fixture with R_fixture
  Algorithm could use total specified loads (C-fixture, L_fixture, R_fixture, V_fixture, C_dut, L_dut, R_dut)
  Or simplified with C_fixture (C_dut) added to C_comp – no change in mathematics
  Use same waveforms
Add C_fixture to both MAIN and BOOST waveform tables (but keep C_comp=0.0 pF)
Use only top-level C_comp
Extra MAIN, BOOST capacitive currents drive top-level C_comp
(Similar programmed approach, which still needed further tuning, Mirmak, 2004)

## Slide 14: Investigation with Another IBIS Tool
C_comp=0.0 pF
  Better delay correlation with SPICE
C_comp=3.0 pF
  C_fixture=3.0 pF
  Left shifted edges and some distortion
  Promising approach
C_comp=3.0 pF
C_comp=0.0 pF

## Slide 15: More C_comp Comments
Why Top-Level C_comp
  Simple, known receiving mode C_comp for I/O
  Avoids inheritance of all Driver Schedule C_comps question
    Is it always there or under certain scheduled conditions?
  Avoids estimating C_comps for scheduled buffers
Other C_comp issues
  Voltage dependent, frequency dependent (or effective reactance)
  Can be split among rails
  Driving and receiving modes differences not supported
  C_comp corners specified by magnitude rather than correlated with process, temperature, voltage
  Plus differential C_comp issues
So C_comp is an effective value, and refinement requires many IBIS additions

## Slide 16: Conclusions
Unresolved (further checking) issues
  Reasons for SPICE model issues
  Possible tool setup and operation issues
  C_comp tool issues
C_comp handling within [Driver Schedule] approach could be improved
IBIS Version 3.2 model satisfied customer’s immediate needs
Unfortunately, target EDA tool(s) and operation remain a practical consideration