## Slide 1: Extracting On-Die Terminators
Bob Ross
IBIS Summit Meeting
DesignCon East 2005
Worcester, Massachusetts
September 19, 2005

## Slide 2: Process Motivation
Issues with “Clip and Extend” recommendations
“Black box” rules from experiences since 1992 (Zeelan with Quad format)
  Decompose model consistent with the internal architecture
    Example: Output and clamps isolated by curvature changes (Nasef, October 1999 IBIS Summit)
  Extrapolate for continuous slope
    Outputs above and on-die extractions here
    Known SPICE MOSFET level slope discontinuity issues
Extrapolation recommended in IBIS Cookbook

## Slide 3: Creating Clamp Tables
Goal: Mimic physical device 3-terminal simulation
  [Gnd Clamp Ref] Vg, [Power Clamp Ref] Vp anchors
    ESD or substrate “diodes”
    On-Die Terminator (ODT) “resistance” structure
  Best currents thru Vp and Vg for rail analysis
  I/O node correct with Vg and Vp changes
Default algorithm covers most practical cases
  Based on deviation from Thevenin resistor ODT
  “pullup” and “pulldown” ODTs are subsets
  DEC: Deviate Extrapolate Calculate

## Slide 4: Example: 50 , 1.2 V ODT
75 
150 
Vp = 1.8 V
Vg = 0 V
1.2 V
50  Total I-V curve with 0.6 V “stick” diodes anchored to each rail
Total I-V

## Slide 5: Clip and Extend
75 
150 
Vp = 1.8 V
Vg = 0 V
1.2 V
50  Total I-V curve with 0.6 V “stick” diodes anchored to each rail
[Gnd Clamp]
[Power Clamp]

## Slide 6: I(V) Blocks and Simulations
75 
150 
Vp = 1.8 V
Vg = 0 V
~1.2 V
0.6 V
50  or Open
8 ma, 225 
0 ma, 50 
Vg = 0 V
Vp = 1.8 V
~1.2 V or Unknown
1.2 V
50  or Open
0 ma, 25 , 50  or Open
0 ma, Open, less/equal 100 
Clip and Extend Model
Resistor Network

## Slide 7: Problems with Clip and Extend
Wrong circuit impacting IBIS 3.2 and beyond
  DC currents different (with, without I/O node circuit)
  AC Thevenin impedances different and open
  Higher frequency effects from non-linear elements
  Driver at I/O node sees different impedance
Tool dependencies including
  Slope discontinuities issues
  Open 0 ma discontinuities with potential simulation ambiguities and failures (Errors)
  Unpredictable performance even with validation
Avoid “Clip and Extend”, use DEC
Be wary of any truncation recommendation

## Slide 8: DEC (from Resistors) Algorithm
Draw box bounded by (Vg, Ig) and (Vp, Ip) and draw the zero current axis
Draw the three lower-left to upper right diagonals, where the upper region is for the [Gnd Clamp], and the lower region is for the [Power Clamp]
Deviate: Proportionally allocate “Total I-V” delta deviation to [Gnd Clamp] and [Power Clamp] diagonals
Extrapolate [Gnd Clamp] data ABOVE Vp
Extrapolate [Power Clamp] data BELOW Vg
Calculate [Gnd Clamp] data BELOW Vg (Total - PC)
Calculate [Power Clamp] data ABOVE Vp (Total - GC)
(Backup slides for some computational details)

## Slide 9: Diagonals and Resistors
0 ma
Vg
Vp
Total I-V
[Gnd Clamp] Resistor
[Power Clamp] Resistor
Calculate
Calculate
Extrapolate
Extrapolate

## Slide 10: DEC Algorithm
0 ma
Vg
Vp
Total I-V
[Gnd Clamp]
[Power Clamp]
Calculate
Calculate
Extrapolate
Extrapolate
Ig
Ip
delta
delta*Ip/(Ip+Ig)
delta*Ig/(Ip+Ig)

## Slide 11: ODT Example (delta=0)
150  [Gnd Clamp]
75  [Power Clamp]
Total I-V

## Slide 12: DEC Observations
Emulates ODT circuit for Vg and Vp changes
  At I/O node, Thevenin 1.2 V shifts correctly, and source impedance = 50 
  Vp to Vg rail-to-rail impedance = 225 
  Diodes correctly anchored to Vg and Vp
Supports single resistor ODT subsets
  “pullup” ODT
  “pulldown” ODT
Backup slides for a suggested computation details
  Typ-min-max data alignment
  Vcc relative [Power Clamp] calculation
Shape anchoring and internal reference overrides next

## Slide 13: Anchor Shape to [Gnd Clamp]
0 ma
Vg
Vp
Total I-V
[Gnd Clamp]
[Power Clamp]
Calculate
Calculate
Extrapolate
Extrapolate
Ig
Ip
delta

## Slide 14: Anchor Shape to [Power Clamp]
0 ma
Vg
Vp
Total I-V
[Gnd Clamp]
[Power Clamp]
Calculate
Calculate
Extrapolate
Extrapolate
Ig
Ip
delta

## Slide 15: Real “50 ” ODT Choices
Clip and Extend 52.8 
Default DEC 94.2  and 120 
[Gnd Clamp] Shape
[Power Clamp] Shape

## Slide 16: Total I-V as [Gnd Clamp]
0 ma
Vg
Vp
Total I-V
[Gnd Clamp]
[Power Clamp]
Calculate
Calculate
Extrapolate
Extrapolate
Ig
Ip
delta

## Slide 17: Application
Total I-V in [Gnd Clamp] table tracks Vg changes
For legacy IBIS “clip” ranges
  [Gnd Clamp]: -Vcc to Vcc
  [Power Clamp]: Vcc to 2*Vcc
TTL Input: 2.1 V ”diode” anchored to Vg per IBIS
Current could have been anchored to Vp (default)
Both anchors partially applicable
[Gnd Clamp]

## Slide 18: 50 , 1.2 V Anchored to Vg
[Gnd Clamp]
[Power Clamp]
0 V
1.2 V 50 

## Slide 19: Total I-V as [Power Clamp]
0 ma
Vg
Vp
Total I-V
[Gnd Clamp]
[Power Clamp]
Calculate
Calculate
Extrapolate
Extrapolate
Ig
Ip
delta

## Slide 20: 50 , -0.6 V Anchored to Vp
[Power Clamp]
[Gnd Clamp]
1.8 V
50  0.6 V

## Slide 21: Real “50 ” ODT Choices
Clip and Extend 52.8 
Default DEC 94.2  and 120 
I-V in [Gnd Clamp]
I-V in [Power Clamp]

## Slide 22: Shape between Vg and Vp
In general Total I-V shape between Vg and Vp remains reasonable for Vg and Vp modulation
DEC method applies for other reference shapes and other overrides
Such as linear resistor partitioned into quadratic components next

## Slide 23: Quadratic Clamps
Linear Thevenin terminator with “quadratic” resistors
  [Gnd clamp] chosen with slope = 0 at Vp
  Use same Extrapolate and Calculate rules
[Gnd Clamp]
[Power Clamp]
Total I-V

## Slide 24: Conclusions
Many choices exist to partition an I-V table into clamp tables
DEC algorithm based on ODT resistor deviation covers practical cases
Overrides shown, based on additional knowledge (could be expanded)
DEC favored over “Clip and Extend” for accuracy, robustness, and portability

## Slide 25: Backup – Suggested Calculations
Uses both a Vg (Gnd) referenced Total I-V and a Vp (typ, min, max Vcc) referenced Total I-V
  Typ, Min, Max for each case
    From –Vcc to 2*Vcc
    Same sample points aligned for typ, min, max data
  [Gnd Clamp] uses Vg referenced data
  [Power Clamp] uses Vp referenced data
  (One Total I-V table could be calculated from the other over a larger sweep range to get aligned data)
DEC – Extrapolate 0 to –Vcc, Calculate, do simple extrapolation above Vcc to 2*Vcc

## Slide 26: [Gnd Clamp] Calculation
0 ma
0 V
Vcc (typ, min, max)
Total I-V (Gnd_Relative)
[Gnd Clamp] (Gnd_Relative)
Calculate
Extrapolate
Extrapolate
Ig
Ip
delta
delta*Ip/(Ip+Ig)
PC = Total – GC (a few points to extrapolate)

## Slide 27: [Power Clamp] Calculation
0 ma
0 V
Vcc (typ, min, max)
Total I-V (Vcc_Relative)
[Power Clamp] (Vcc_Relative)
Calculate
Extrapolate
Extrapolate
Ig
Ip
delta
GC = Total – PC (a few points to extrapolate)
delta*Ig/(Ip+Ig)

## Slide 28: Comments
Extrapolations below 0 V
  Based on extrapolating a few calculated points
  All data points at Total I-V voltages
Extrapolate above Vcc (typ, min, max)
  The typ and min columns need entries or NA’s to Vcc (max)
  Extrapolate columns to 2*Vcc
    Fill in remaining values
    Optionally, one value at 2*Vcc