## Slide 1: IBIS 4.1 Macromodel Library for Simulator Independent Modeling Arpad Muranyi, Mike LaBonte, Todd Westerhoff Sam Chitwood, Ian Dodd, Barry Katz, Scott McMorrow, Bob Ross, Ken Willis

## Slide 2: Agenda
History – How did we get here?
Macromodeling concepts
A call to action
The working group
Current building block library
Current issues
Next steps

## Slide 3: History – How Did We Get Here?
IBIS isn’t keeping up with the demands of new I/O technologies
  SPICE use in SI analysis is increasing
IBIS 4.1 allows AMS models to be called from IBIS, but adoption has been slow
Macromodeling proposed at January 2005 summit by Donald Telian of Cadence as an alternative to full AMS implementations
  Proposal was for Berkeley SPICE extensions

## Slide 4: History – How Did We Get Here?
Study group formed (Intel, Cisco, Teraspeed, SiSoft, Cadence) to explore macromodeling concept
Macromodeling in AMS proposed as a bridge to full AMS models, without requiring IBIS specification changes that would be required for SPICE extensions
Proof-of-concept models built and presented at DAC 2005 IBIS Summit

## Slide 5: Mar 2005: First Attempts at Mixing Spice/AMS
Spice
AMS

## Slide 6: The Macromodel Concept
Create a library of AMS “elements” that can be instantiated and interconnected to create complex buffer models
Model AMS elements after sources and elements found in popular SPICE tools
Express the reference definitions of element behavior using an AMS language.
Ensure elements can be implemented by substitution in SPICE engines without native AMS support
Standardize AMS element library across all model providers
IBIS files reference netlists constructed from reference “templates”, which instantiate the AMS elements

## Slide 7: Macromodel Hierarchy
[External Circuit]
or
[External Model]
Template
(eg. PRE_EMPH)
Template
(eg. DIFF_RCVR)
AMS Element (eg. VSOURCE)
AMS Element (eg. BUFFER_IN)
Element
(eg. E1)
Element
(eg. B1)
IBIS File
[External Circuit] or
[External Model] call
macro model templates
Macro model templates call elements from common AMS library
AMS Elements are written
using the analog only features
of the *-AMS languages, and
can be substituted with native
SPICE elements in SPICE tools
if necessary
…

## Slide 8: Macromodel example
scaler
delay
Adder
main
boost
IN
TX+
scaler
delay
Adder
main
boost
TX-
Pre-emphasis buffer template
Template
port
AMS Element
Callouts

## Slide 9: AMS Element Mapping
Native AMS Simulator
SPICE Simulator
b_io PUrefB PDrefB IoB InB En PCrefB GCrefB
+ file=‘mybuf.ibs' model=‘mybuf' +power=on buffer=2
IBIS_BUFFER_OUT ioB #(.ibis_file(“mybuf.ibs”), .ibis_model(“mybuff”))
(InB, En, RcvB, IoB, PCrefB, PUrefB, PDrefB, GCrefB);

## Slide 10: Macromodels in Verilog-A simulators
Part.ibs
Bld_blks.va
EXTRACT/ MERGE DATA
IC website
IBIS website
Verilog-A
simulator
Netlists.va
Customized buffer modules

## Slide 11: Macromodels in VHDL-AMS simulators
Part.ibs
IC website
IBIS website
VHDL-AMS
simulator
Bld_blks.vhd
EXTRACT NETLIST, TRANSLATE
Netlists.vhd

## Slide 12: Macromodels in SPICE/IBIS simulators
Part.ibs
Bld_blks.va
EXTRACT BUFFERS, TRANSLATE
IC website
IBIS website
SPICE/IBIS
simulator
Netlists.XXX
Bld_blks.XXX
sync
Buffers.ibs

## Slide 13: June 14, 2005: A Clear Strategy
AMS models that can be translated into SPICE implementations

## Slide 14: A Call to Action
IBIS/AMS macromodeling proposal presented at IBIS Summit, June 2005
Letters sent out to major simulator vendors inviting them to participate in library definition
Working group formed
  Arpad still does most of the coding and testing …

## Slide 15: The Working Group
Intel – Arpad Muranyi
Cadence Design Systems – Ken Willis
Cisco Systems – Mike LaBonte, Todd Westerhoff
Mentor Graphics – Ian Dodd
Sigrity – Sam Chitwood
SiSoft – Barry Katz
Teraspeed - Scott McMorrow, Bob Ross

## Slide 16: Current Library - Basic Elements
 | Fixed | Voltage Controlled | Current Controlled
R | IBIS_R | IBIS_VCR | IBIS_CCR
L | IBIS_L | IBIS_VCL | IBIS_CCL
C | IBIS_C | IBIS_VCC | IBIS_CCC

## Slide 17: Current Library - Sources
 | Fixed | Voltage Controlled | Current Controlled | Voltage Controlled with Delay | Current Controlled with Delay
Voltage Source | IBIS_V | IBIS_VCVS | IBIS_CCVS | IBIS_VCVS_DELAY | IBIS_CCVS_DELAY
Current Source | IBIS_I | IBIS_VCCS | IBIS_CCCS | IBIS_VCVS_DELAY | IBIS_CCCS_DELAY

## Slide 18: Current Library – Operators
 | Current Controlled Current (with scaler) | Voltage Controlled Voltage (with scaler)
Adders | IBIS_CCCS_SUM | IBIS_VCVS_SUM
Multipliers | IBIS_CCCS_MULT | IBIS_VCVS_MULT
Dividers | IBIS_CCCS_DIV | IBIS_VCVS_DIV

## Slide 19: Current Library – Operators (Cont.)
 | Voltage Controlled Current (with scaler) | Current Controlled Voltage (with scaler)
Adders | IBIS_VCCS_SUM | IBIS_CCVS_SUM
Multipliers | IBIS_VCCS_MULT | IBIS_CCVS_MULT
Dividers | IBIS_VCCS_DIV | IBIS_CCVS_DIV

## Slide 20: Current Library – Active Devices
WORK IN PROGRESS
 | Input / Output | Output Only | Input Only
Buffer | IBIS_BUFFER_IO | IBIS_BUFFER_OUT | IBIS_BUFFER_IN
 | Open Drain | Open Source | Series
Buffer | IBIS_BUFFER_OD | IBIS_BUFFER_OS | IBIS_BUFFER_SERIES
WORK IN PROGRESS

## Slide 21: Current Library – Other Models
Inductive Coupler | IBIS_K
Transmission Line | IBIS_T

## Slide 22: Sample AMS Element Code
module IBIS_R (p, n);
electrical p, n;
branch (p, n) Out;
parameter real Rval = 1.0;
parameter real Scale = 1.0;
analog begin
V(Out) <+ Scale * Rval * I(Out);
end
endmodule
module IBIS_K (p1, n1, p2, n2); output p1, n1, p2, n2; electrical p1, n1, p2, n2; branch (p1, n1) Out1; branch (p2, n2) Out2; parameter real Lval_1 = 1.0; parameter real Lval_2 = 1.0; parameter real Kval = 0.0; parameter real I0_1 = 0.0; parameter real I0_2 = 0.0; parameter real Scale = 1.0;
// This should be declared as "localparam" so that it
// couldn't be changed from the outside
//localparam real M = Kval * sqrt(Lval_1 * Lval_2); parameter real M = Kval * sqrt(Lval_1 * Lval_2);
analog begin if (Scale * Lval_1 > 0.0) begin I(Out1) <+ (idt(V(Out1), I0_1*Scale*Lval_1) – M*(I(Out2)-I0_2)) / (Scale*Lval_1); end else begin V(Out1) <+ 0.0; end if (Scale * Lval_2 > 0.0) begin I(Out2) <+ (idt(V(Out2), I0_2*Scale*Lval_2) – M*(I(Out1)-I0_1)) / (Scale*Lval_2); end else begin V(Out2) <+ 0.0; end end
endmodule
Simple Resistor
Inductive Coupler

## Slide 23: Current Issues
Verilog-A(MS) does not allow a string to be passed as a file name to the $table_model keyword
  Every instance of the building block would have to be duplicated with a hard coded file name, or
  we could pass the data into the building block as parameters from the netlist when instantiating it
Verilog-A(MS) provides NO file parsing capabilities to read data from external files
  The data will have to be extracted from the IBIS file manually or by a separate script (VHDL-AMS doesn’t have this limitation)
Verilog-A(MS) has very limited array features
VHDL-AMS and Verilog-A(MS) do not allow expressions to be passed as parameters like (H)SPICE

## Slide 24: Next Steps
Create more templates to find out what additional building blocks need to be written
We need semiconductor vendor participation – using the library to model current parts
Translator implementation for EDA companies without native Verilog-A(MS) / VHDL-AMS support

## Slide 25: Final Thoughts
This approach should help speed the adoption of AMS as a modeling language for signal integrity purposes
Full AMS models (as opposed to templates based on macromodels) will appear once all EDA vendors support AMS