## Slide 1: IBIS Algorithm Including Reactive Loads
Xuefeng Chen
xfchen@synopsys.com
Asian IBIS Summit
Beijing, China
September 11, 2007

## Slide 2: Outline
Accuracy Issue of Reactive Loads
- Concept of Reactive Loads
- Related Presentation Before
- Example of the Issue
IBIS Algorithm with R/L/C/V_fixture
- Algorithm Steps and Equations Involved
- Recall the Example with Above Algorithm
Conclusions

## Slide 3: Reactive Loads
The general Reactive load in this presentation is the
R/C/L/V_fixture load shown in the diagram
The presentation does not consider additional components
L/R/C_dut defined in the IBIS standard (not shown)
to mimic the package model of a specific pin

## Slide 4: Related Presentation in Past Meetings
Arpad Muranyi: http://www.vhdl.org/pub/ibis/summits/feb06/muranyi2.pdf
Deals with a series capacitor (C_load) in series with R_load.
Found difficulties applying the 2EQ/2UK process.
Manfred Maurer: http://www.vhdl.org/pub/ibis/summits/apr07/maurer.pdf
Considered using R_fixture, L_fixture, C_fixture by superposition.
Not yet resolved for series C_load with R_load problem.
Bob Ross: http://www.vhdl.org/pub/ibis/summits/feb06/ross1.pdf
Suggested using C_fixture (if handled by IBIS processing algorithm) for
buffer peaking to compensate for connected buffers and C_comp loading
interactions.
Michael Mirmak: http://www.vhdl.org/pub/ibis/summits/apr04/mirmak2.pdf
Considered C_comp extraction issues when buffers are connected
and interact.

## Slide 5
Example: Accuracy Issue with L, C, R, V Loads
out1ibis: IBIS Model extracted with
L_fixture=0, C_fixture=0,
R_fixture=50,V_fixture=5
out1spice:Transistor Level Model with loads
L=10n, C=5p, R= 50, V=5
out2ibis: IBIS Model extracted with
L_fixture=0, C_fixture=5p,
R_fixture=50,V_fixture=5

## Slide 6: IBIS Algorithm with R/L/C/V_fixture
Two steps to get scaling coefficients of PU, PD (Ku,Kd)
Get Idie(t) by VT waveforms, C_comp and *_fixture
Use the well known 2EQ/2UK algorithm
0 = Ku(t) * Iu(Vwfm1(t)) + Ipc(Vwfm1(t)) - Kd(t) * Id(Vwfm1(t)) - Igc(Vwfm1(t)) - Idie(Vwfm1(t))
0 = Ku(t) * Iu(Vwfm2(t)) + Ipc(Vwfm2(t)) - Kd(t) * Id(Vwfm2(t)) - Igc(Vwfm2(t)) - Idie(Vwfm2(t))

## Slide 7: IBIS Algorithm with R/L/C/V_fixture (Cont.)
- Compute Idie(t) of preceded step 1
Ccomp * dVwfm / dt
Idie(t) = ICcomp(t) + ILfix(t)
dILfix(t)/dt = (VCfix(t) – Vwvf(t)) / Lfix
dVCfix(t)/dt = ((Vfix – VCfix(t)) / Rfix – ILfix(t)) / Cfix
VCfix(0) = Vwvf(0)
ILfix(0) = (Vfix – Vwvf(0)) / Rfix
Differential equations:
With initial values:

## Slide 8: Example: Fitting Result if Model is Extracted with all L,C,R,V fixtures
out1spice:Transistor Level Model with loads
L=10n, C=5p, R= 50, V=5
out3ibis: IBIS Model extracted with
L_fixture=10n, C_fixture=5p,
R_fixture=50,V_fixture=5

## Slide 9: Substantial Accuracy Improved
xvpu1/xvpd1: model extracted with L_fixture=0, C_fixture=0, R_fixture=50,V_fixture=5
xvpu2/xvpd2: model extracted with L_fixture=0, C_fixture =5p, R_fixture=50, V_fixture=5
xvpu3/xvpd3: model extracted with L_fixture=10n, C_fixture=5p, R_fixture= 50, V_fixture=5
xvpu: scaling coefficient of PU
xvpd: scaling coefficient of PD

## Slide 10: Conclusions
For reactive loads, IBIS model result can be perfectly fitting with Transistor level model if proper R_fixture , V_fixture, C_fixture , L_fixture are used in model extraction
The proper values of them are based on practical loads

## Slide 11: Special Thanks to Bob Ross For the help of providing research background, review and good suggestions for this presentation

## Slide 12
Predictable Success