## Slide 1
September 11, 2007
Asian IBIS Summit, Beijing China
IBIS4.2 FOR
DDR2 TIMING ANALYSIS
Guan Tao
guantao@huawei.com

## Slide 2: Outline
New technologies have brought challenges to IBIS model
DDR2 timing analysis
  The read cycle timing analysis
  The write cycle timing analysis
IBIS4.2 model meets the challenges

## Slide 3: Challenges
More SI and timing problems emerge as the rate of bus increases , these problems can be eliminated by new techniques :
  ODT (On Die Termination);
  OCD (Off-chip Driver).
Challenges of DDR2 modeling:
  How to model the ODT circuit;
  How to use the slew rate table.
The setup and holdup time are varying with the slope of the signal in DDR2.

## Slide 4: DDR2 Timing Analysis Method
A proper method of a DDR2 timing analysis should contain the following essentials:
Seeking for a balance between simulation efficiency and waveform quality.
The parallel simulation and crosstalk can be processed by EDA platforms.
The EDA platform can process the PRBS (pseudo-random bit sequence) code;
Topology 、matching and transmitter/receiver buffer can be automatically analyzed
The settle and switch delay between standard load and practical load can be considered;
Influence of voltage and temperature can be included in the simulation;
The ODT circuit and slew rate table can be considered.
Current simulation method is not good enough to support the features listed here!

## Slide 5: Timing Relationships of DDR2
Three timing relationships in DDR2 timing analysis:
ADDRESS、COMMAND and CK/CK#;
DQ and DQS/DQS#;
DQS and CK/CK#.

## Slide 6: Data Valid Window
The SSTL_18 is intended for DDR2 interface application.

## Slide 7: DDR2 Timing Analysis with IBIS 3.2
Following is an example of timing analysis of DQ and DQS. The ADDRESS/COMMAND timing analysis is similar.
The topology of DQ/DQS is point to point feature.
The models of CONTROLLER and MEMORY are IBIS3.2 model.

## Slide 8: Read Cycle Timing Analysis (fast)
In fast mode, the simulated eye diagram of read cycle is as follow.
  data valid window :1.255ns
  waveform distortion: 0.245ns

## Slide 9: Read Cycle Timing Analysis (slow)
In slow mode, the simulated eye diagram of read cycle is as follow.
  data valid window: 1.217ns
  waveform distortion :0.283ns

## Slide 10: Read Cycle Timing Calculation

## Slide 11: Write Cycle Timing Analysis (fast)
In fast mode, the simulated eye diagram of write cycle is as follow.
  data valid window :1.426ns
  waveform distortion :0.074ns

## Slide 12: Write Cycle Timing Analysis (slow)
In slow mode, the simulated eye diagram of write cycle is as follow.
  data valid window:1.271ns
  waveform distortion: 0.229ns

## Slide 13: Write Cycle Timing Calculation

## Slide 14: Drawbacks
Inefficient
The method of DDR2 timing analysis above is a time-consuming and manual procedure. Simulations are run on each net to generate eye diagrams, through which signal integrity and timing characteristics of an individual net can be evaluated.
Sometimes meaningless
The simulation is meaningless, when the margin is negative.
The DDR2 timing analysis is made under absolute worst-case conditions. Owing to the worst-case prediction of all parameters applied to a single net, the margin analysis method described above may predict a failure when in fact the actual design is sound.

## Slide 15: Deficiencies of IBIS3.2
IBIS3.2 model has the following several deficiencies for timing analysis of DDR2:
The IBIS3.2 model is not programmable, so that it is difficult to implement a flexible simulation and process slew rate table automatically.
The IBIS3.2 model is not flexible enough to accommodate new techniques.
The IBIS3.2 model is a parameterized model, not able to process the simulated waveforms.

## Slide 16: IBIS4.2 Model Meets the Challenges
Randy Wolff 、Gary L. Pratt. P.E and their collaborators solve these problems in IBIS4.2 model. IBIS4.2 is an extension of IBIS3.2.
IBIS4.2/AMS multiplexer permits the simulator to select between an IBIS model with ODT and one without ODT;
Supports seamless switch of read cycle and write cycle simulation;
Through running a section of VHDL code, the simulator is able to measure the slope of relevant signals;
Automatically determines the corresponding value in the slew rate table;
It’s a good solution to problems we are facing now.

## Slide 17: IBIS 4.2 for Timing Analysis
Using the IBIS4.2 model ,we can make the following measurements automatically:
Automatic overshoot area measurements
Automatic setup and holdup timing measurements
Slew-dependent timing calculation

## Slide 18: One Solution of ODT Circuit

## Slide 19: VHDL-AMS Code for Multiplexer

## Slide 20: Slew Rate Table Calculation

## Slide 21: Output Results

## Slide 22: Advantages
Flexible
The IBIS4.2 model is programmable, so that the model is flexible and appropriate to new technology.
Real-time
The margin is properly measured on every edge in the method of timing analysis, which takes the influence of slew rate table into consideration.
Automatic
The procedure of timing analysis is automatic and prompt. The output results are reasonable and simple.

## Slide 23: Requirements from System Vendors
The IBIS4.2 model is a good solution to the high rate bus of memory timing analysis,
1. There is still few EDA vendors to fully support the IBIS4.2 model;
2. Due to no spice2AMS tool in place, the majority of IC vendors do not have a schedule to provide the IBIS4.2 model;
3. The results are consistent , when we use the same IBIS model on different platforms;
4. The IBIS model should be accurate enough to depict electrical characteristics of chip properly;
5. Building the package model should be paid more attention to as the bus rate increases;
The development of IBIS needs our efforts！