## Slide 1: Understanding and Using ICM Models
Asian IBIS Summit,
Beijing China,
September 11, 2007
Meng, Yubao (yubao@cadence.com)
Cadence Shanghai SPB R&D Center
Notes: 理解并使用互联模型

## Slide 2: Topics
IBIS ICM Model Introduction
  What’s IBIS ICM Model
  What can we do with ICM model
  ICM model structure
ICM model usage scenario
  Black box model
  Package model
  Connector model
  S-parameter support
  ICM swath model support
Summary
Notes: 这里包含三个主题，一是介绍IBIS互联模型，ICM的结构、格式等；二是介绍什么情况下使用ICM，以及ICM所支持的数据结构；最后做个简单总结

## Slide 3: IBIS ICM
IBIS Interconnect Modeling Specification
  ICM stands for InterConnect Modeling
The goal of the ICM
  Provide a better, *more accurate*, non-proprietary interconnect data exchange format
    Faster & accurate simulations
    Smaller file size
ICM history
  Final Draft 1.0 released publicly May 16, 2003
    See IBIS web site under “Connector Info”
  Version 1.1 “ICM” specification approved in July 2005
Notes: 这里介绍了ICM是IBIS Interconnect Modeling Specification的缩写，ICM目标是提供GHz以上信号完整性仿真要求的高精度、不涉及IP、不泄露厂家机密的互联器件新模型。
2003年5月16日发布了ICM最终草稿版1.0；2005年7月ICM正式版1.1发布。

## Slide 4: What can we do with ICM model
ICM supports models for Connectors, PCB traces and IC-Packages
ICM can include
  RLGC Matrices
  Swaths
  S-parameters
Notes: 我们能用ICM做什么？或者说什么能用ICM来表述？
ICM不仅可以用于描述连接器，也可以描述IC封装，甚至是PCB上的互联线，只要是无源的信号互联结构，这种连接结构需要保密，就可以使用ICM的格式来产生ICM模型。
ICM支持的数据结构包括spice格式的RLGC矩阵，为了减小ICM模型文件的大小，ICM有几种方式描述这种矩阵，比如说稀疏矩阵，对角矩阵等。
ICM也支持s-parameter数据文件，即整体结构参数由一个s-parameter文件描述。
ICM swath model 是ICM模型的一大特点，由于一般的互联结构具有对称特性，所以其电气特性也具有对称性，这样我们就可以用局部的电气参数推导出全局特性，从而大大减小了矩阵的维数和模型文件的大小。

## Slide 5: Section of ICM
Each section is made up of a Single Line Model (SLM) or Multiple Line Model (MLM)
A matrix section is a set of tables of numerical values that represent the electrical relationships between all conductors of a given geometry
S-parameter can be used in place of RLGC matrix
Notes: Section 是ICM模型的基本机构单元，它将ICM模型按照信号传输的方向进行分段参数刻画， 有利于保证每个section都是比较规则、简单的。
每个section是由单线或多线电气耦合特性数据构成， 即给定几何尺寸范围内所有信号导体之间的耦合参数
通常情况下section是由RLGC耦合数据矩阵构成，但也可以由s-parameter构成，但此时ICM模型只能有一个section.

## Slide 6: Section: ICM core unit structure
Sections are basic units and core structure of one ICM model

## Slide 7: ICM model usage scenario
ICM models can be used during pre-layout and post-layout analysis
Three cases are presented
  Case1: In pre-layout simulation, ICM model is used as a Black box model in a topology
  Case2: In post-layout simulation, ICM package model is assigned to a component IBIS model on the PCB
  Case3: Connector model
Notes: 使用ICM的几种情况：
根据前后仿真的不同，仿真工具需要对ICM模型进行相应处理：
前仿真撘建拓扑时，需要以器件的形式展示ICM模型，仿真器将其封装成black box类型形式，从而可以任意组建拓扑。
后仿真时对于IC封装的ICM模型，仿真器将其直接翻译成packagemodel类型形式，
对于连接器的ICM模型，仿真器将其翻译成connector类型形式

## Slide 8: Example: ICM model of PCI express package
Notes: 这是Cadence工具提供的对ICM模型处理方法。
将ICM模型调入Cadence MI后， MI会对其进行语法结构检查，正确后，MI可以对ICM模型进行三种类型转换，一类是black box类型，一类是packagemodel类型，最后一类是connector类型。
例子是一个PCI express芯片封装的ICM模型。

## Slide 9: Device model case (Black box model)
Notes: 这里是将PCI express的封装ICM模型转换成black box类型，

## Slide 10: Case 1: ICM acts as device model (Black box model)
The package ICM model has been wrapped into one black box model, just like one connector
Notes: 在这个拓扑里类似连接器的black box器件是那个pci express封装的ICM模型转换来的

## Slide 11: Case 1: Simulation Results comparing (with/o ICM model)
The pink line represents the simulation with ICM model
The black line represents the simulation without ICM model
Notes: 黑色的是拓扑中没有考虑封装模型时接收到的信号波形；
粉色的是经过封装后的波形；

## Slide 12: Package model case (associating with its corresponding IBIS model)
Notes: 这里是将PCI express封装的ICM模型转换成packagemodel类型，这样可以和相应的IBIS模型一起赋给芯片

## Slide 13: Case 2: ICM acts as package model
Notes: 这里展示的是分配相关环节。

## Slide 14: Case 2: Simulation Results comparing (with/o ICM model)
Notes: 蓝色的波形是经过封装前的信号，粉色波形是经过封装后的信号

## Slide 15: S-parameter support
Notes: 这里展示的是一个s-parameter类型的ICM模型，这里将其转换成了black box类型和packagemodel类型；在后面我们将看到转换成connector类型

## Slide 16: ICM Swath model support
Swath model
  Is a method of using a small matrix section to define a much larger and variable size section of a connector
  This facilitates faster simulation, smaller file size, and makes the creation of a family of connectors much easier
Notes: ICM swath模型大大减小了对称连接器模型的数据量，更利于仿真器快速处理模型，厂家也大大方便了模型创建，同一个swath 模型可以描述不同尺寸同类的连接器。

## Slide 17: Case 3: Connector model assign
Notes: ICM swath模型转换成connector类型，然后直接分配给接插件，完全类似于给芯片分配IBIS模型。注意这里connector类型是完全针对接插件的一个新类。

## Slide 18: Summary
ICM models offer open, non-proprietary way for vendors to provide interconnect models to their customers
ICM models can be accurate for simulation at higher frequencies
Notes: ICM 模型给供应商找到了一个开放的没有IP问题的新途径来产生接插件的模型

## Slide 19
Thanks!