## Slide 1: IBIS AMI Model Developers Toolbox
Hemant Shah (shah@cadence.com)
Asian IBIS Summit - Beijing, China
September 11, 2007

## Slide 2: What’s in it
Sample Model Rx
  Source code
  Executable on Linux
  Model params file
Tester Program
  Executable on Linux
  Tester config file
Starter model templates
Documentation
Use sample model and tester program to understand the details of the IBIS AMI API
Create your own algorithmic models using starter model templates
Use the tester program to test the model

## Slide 3: Sample Rx Model
Continuous Time Filter (CTF) RX model
  Combination of feed forward and feed backward filter
  Modifies the waveform given a set of coefficients
  Tested for 6.25Gbps data rate
  User configurable forward and backward taps
Parameters needed by the model
  Number of forward taps, Number of backward taps, Coefficients
  Can be provided in a file
To Compile:
  a) gcc -c ibis_ctf_rx.c
  b) gcc -shared -o ibis_ctf_rx.dll ibis_ctf_rx.o
Σ
.
.
.
.
.
.

## Slide 4: CDNS AMI Tester Program
Inputs
  Bit Stream: “(0111100001111)”
    Alternatively, users can specify the number of bits and let tester generate random bits
  Data Rate
  Impulse Response
  DLL to interface to
  Model specific parameters
Outputs
  Wave_out: *voltage-time pairs in txt file* wave form data modified by the Model
  Wave_in: *voltage-time pairs in txt file* Represents waveform passed to the model
  ImpulseResponse: IR data if it is modified by the model (init)
CDNS_AMI_Tester
DLL

## Slide 5: CDNS AMI Tester Program
Usage: CDNS_TESTER [-h] ctf_rx_model
Bit Stream “(10111000)”
AMI File contains:
  - Measurement Delay
    Ignore data for spec delay
  - Model specific parameters
Tester config file contains
  - Information generally set by end users through the EDA platform
    - Data Rate
    - Number of bits
    Input file names
    Output files names
AMI
File
DLL
Wave_in
Wave_out
Wave in
Wave out
.txt files with voltage-time pairs
IR
IR output if modified by init
Params
Tester cfg
File
CDNS_AMI_Tester

## Slide 6: How to get the kit
Cadence AMI Developers toolbox will be available through IBIS web site soon
In the mean time, you can send request for the toolbox to: shah@cadence.com

## Slide 7: Resources
Many presentations on Algorithmic Modeling starting from June 2006 can be found at:
  http://www.vhdl.org/pub/ibis/macromodel_wip/archive-date.html
Updates on the AMI work can also be found in ATM subcommittee updates provided at DAC 2007 and DesignCon 2007 IBIS Summits
  Presentations can be accessed from this page: http://www.vhdl.org/pub/ibis/summits/
To reach the IBIS-ATM group on this topic, you can send email to: ibis-ami-toolkit@freelists.org