## Slide 1: SerDes Modeling: IBIS-AMI Evaluation Toolkit
Presented by: Todd Westerhoff, SiSoft
twesterh@sisoft.com
IBIS Summit
Beijing, China
September 11, 2007

## Slide 2: Challenges
IBISCHK cannot check compiled models
  Similar problem to AMS model calls
Several possible sources of platform/model incompatibility
  Incorrect EDA tool implementation
  Incorrect model implementation
  Incompatible run-time libraries
A “reference standard” for IBIS-AMI is needed
  Reference platform implementation
  Reference model implementation

## Slide 3: IBIS_AMI_Test
Allows IBIS-AMI .dll models to be run as standalone “executables”
  Facilitates model debug
  Provides standard environment for testing model compliance
Authored by SiSoft, source code to be turned over to IBIS Open Forum
  Executable will be publicly available

## Slide 4: IBIS_AMI_Tx Model
(IBIS_AMI_Tx
(Dll
(linux ibis_ami_tx_lnx.so)
(solaris ibis_ami_tx_sun4.so)
(windows ibis_ami_tx.dll)
)
(Reserved_Parameters
(Ignore_Bits (Type Integer) (Default 21))
(Max_Init_Aggressors (Type Integer)(Default 25))
(Init_Returns_Impulse (Type Bool)(Default True))
(GetWave_Exists (Type Bool) (Default True))
) | End Reserved
(Model_specific
(txtaps
(tapid (Range -1 3) (type int) )
(txtapcoeff
(-1 (Range -0.1 0.1 0.1) (Type float) (Default 0))
(0 (Range 1 1 0) (Type float) (Default 1))
(1 (List -0.1 0.1) (Type float)(Default 0))
(2 (Range -0.01 0.02 0.005) (Type float) (Default 0))
(3 (Range -0.01 0.02 0.005) (Type float) (Default 0))
) | tapcoeff
) | txtaps
(tx_freq_offset (Range 0 150 1) (Type ppm) (Default 0))
) | End User_Defined
) | End IBIS_AMI_tx
Reference IBIS & AMI files
Reference Algorithmic model
  Impulse response and waveform processing
  4 tap equalizer
    Pre-cursor tap
    Cursor tap
    2 post-cursor taps
    Model normalizes tap sum
  Scalable transmit swing
  Executable and source code publicly available
AMI
File
Algorithmic Model Code

## Slide 5: IBIS-AMI Evaluation Toolkit
Goal: allow interested parties to evaluate & develop IBIS-AMI models
Available on-line from IBIS-ATM task group website and from www.sisoft.com
Contents
  IBIS_AMI_Test utility
  Sample TX model and source code
  Sample input data, scripts, documentation
Email discussion group established: ibis-ami-toolkit@freelists.org

## Slide 6: Sample Results: No TX EQ
Impulse Response
Eye Diagram
Signal @ Rx pad, Stimulus

## Slide 7: Sample Results: TX EQ: (-.15, .7,-.125,-.025)*0.8
Impulse Response
Eye Diagram
Signal @ Rx pad, Stimulus

## Slide 8: IBIS-AMI Toolkit
Provides a “reference implementation” for testing EDA platforms and IBIS-AMI models
Allows users to assess IBIS-AMI model functionality and performance
Users can run analyses based on their own designs and channel impulse responses