## Slide 1: A Review of existing Multi-Gbps Serial Channel Analysis Methods and the Evolution of the Proposed IBIS ATM Algorithmic Modeling Standard
Ian Dodd, Signal Integrity Market Segment Specialist
Richard Ward, Texas Instruments.
Sanjeev Gupta, SI Product Marketing Manager, Agilent Technologies
IBIS Open Forum, Tokyo, Japan
14th September 2007
contact: ian_dodd@exch.agilent.com
(Previously presented at the IBIS Open
Forum Beijing, China, 11th September 2007)

## Slide 2: Introduction
The IBIS Advanced Technology Modeling (ATM) committee has a proposal for a flexible approach to system level modeling of multi-Gbps channels
The principal target for this modeling technology is the PCB system designer
Other standards bodies such as the IEEE and INCITS have undertaken major efforts to define standards for multi-Gbps channels
This includes standardized modeling for these channels, principally targeted at the IC designer
This paper contrasts the modeling approaches and shows how the IBIS ATM proposal promises to solve problems not addressed by previous solutions
It also suggests how some of the features of previous approaches could be incorporated into the IBIS ATM proposal at future date.

## Slide 3: Overall goal – Design and implement reliable 1-10Gbps self clocked serial channels
The Silicon Vendor
  Design Transmitter and Receiver meeting specified channel standard and BER
    Must be interoperable with other vendors designs for that channel standard e.g. 802.3ap and CEI11
    Simulate Transmitter, Receiver and representative interconnect
    Create Prototype silicon and PCB, measure actual performance
    Silicon design must tolerate a range of real PCB channel layouts with connectors, vias and cables
    Correlate simulation results to measurements to fine tune the modeling process
  The PCB System Implementer
  Choose IC vendors and technology
  Plan channel implementation: set constraints on layers, lengths, via types
  Simulate Transmitter, Receiver with representative interconnect
  Layout channel, re-simulate with accurate modeling of channel
  Fabricate PCB, measure actual performance
    Correlate simulation results to measurements to fine tune the modeling process

## Slide 4: Distribution of multi-Gbps models from the IC vendor to the PCB systems implementer
In creating models, the IC vendor wishes to satisfy customers while:
  Protect their intellectual property
  Delivery accurate, easy to use models that require a minimum of support
  Minimize the incremental cost in providing externally distributed models
The PCB System Implementer has additional preferences:
  Compatibility of models between IC vendors and support from multiple SI analysis tools
  Simulation speeds that allow full coverage of a design including corner case analysis
    This presents new model creation challenges for the IC vendor
  Historically many IC vendors internally utilized SPICE to design their general purpose buffers
  IBIS was the preferred format for model distribution, frequently created from the IC vendors internal SPICE models using SPICE to IBIS utilities
  Some IC vendors preferred to delivered encrypted versions of their internal SPICE models.
  Today IC vendors are internally using a mixture of SPICE, RTL and system level tools to design multi-Gbps buffers and the channel control logic

## Slide 5
The topology of a typical 6 Gbps serial channel
Pre-emphasis control
Data
Serializer
Clock
Multiplier PLL
System
Clock
Encoding (8,10 etc)
Driver
Training pattern
Transmitter
Package
Via
Trace
Connector
Trace
Via
Package
Physical Channel
Neighboring channels not shown
Trace
DC blocking
Capacitor
Equalization FFE, DFE
Clock / Data Recovery
Training pattern
System Clock
Clock Multiplier PLL
Data
Decoding
De-Serializer
Data
Recovered
Clock
Receiver

## Slide 6: Approaches to multi-Gbps simulation
Transistor and circuit level
  Drivers and receivers are modeled using SPICE, IBIS and SPICE macro-models
  Packages and interconnect are modeled using transmission line and ‘S’ parameter models
  Minimize the incremental cost in providing externally distributed models
  Good accuracy but poor simulation speed
Circuit and system level co-simulation
Drivers and receivers are modeled using IBIS and SPICE macro-models co-simulating with RTL, Verilog AMS, VHDL-AMS, System-C, Proprietary ‘C’ or ‘C++” and system level simulation tools.
  Packages and interconnect are modeled using impulse response, transmission line and S- parameter models
  Good accuracy and moderate simulation speed
    System level simulation
  Drivers and receivers are modeled using RTL, Verilog AMS, VHDL-AMS, System-C, Proprietary ‘C’ or ‘C++” and system level simulation tools.
  Channels are characterized using impulse response or S-parameter models
  Moderate Accuracy with good simulation speed

## Slide 7
Circuit and system level co-simulation of a multi-Gbps channel
Channel
Package, Breakout, Traces and Vias inc S-Parameter Models from 3D Field Solution
Analog
Non-linear Transmitter
Analog
Non-linear
Receiver
(Load Section)
Equalization FFE, DFE
Clock Recovery
Phased Lock Loop
Data Recovery
Data
Clock
High Speed Window sampling
Encoding (8,10…) Pre-emphasis
Circuit Simulation (Non-linear)
System Level or Behavioral Co-Simulation
Recovered Data Eye Diagram (includes periodic and random jitter)
Random Noise Extrapolation
BER and Jitter Plot Generation
Stimulus
Random Noise
including training pattern, periodic jitter
Adjacent channels not shown
Jitter/BER Plots
Decoding
(10,8…)
Training
pattern

## Slide 8: Circuit and system level co-simulation
Introduction
Presently favored by IC vendors for internal use
Explicitly implemented as co-simulation between a circuit level and system level simulator
Implicitly implemented as structural and behavioral modules in a AMS/SPICE simulation
The number of nodes in the circuit simulation generally governs simulation performance
    For best results use IBIS or behavioral models for the analog portion of buffers
It is critical to choose a tool with fast and accurate S-parameter simulation
Major Benefits
Can use the primary models used to design the silicon
Can include channel protocol logic e.g. training patterns in original design language e.g. RTL
Supports non-linear drivers and loads with complex random jitter sources
Disadvantages
No standard interface between the models and the simulator
    Can an extension to the IBIS ATM proposal be used to solve this issue?
Waiting for IEEE standardized HDL encryption

## Slide 9: Example of circuit and system co-simulation
DFE
DFE
DFE
FFE
FFE
FFE
Initial Eye
Eye after training
Eye after modified stimulus
FFE and DFE coefficients
FFE and DFE coefficients
FFE and DFE coefficients
Simulation of a representative 10 Gbps channel with initial training and dynamic equalization
3000 bit training sequence
The initial eye is completely closed
The FFE and DFE coefficients can be seen to change as a function of the stimulus
Environmental variables such as supply voltage, temperature and humidity will also affect coefficients

## Slide 10: Obtaining meaningful data from a limited dataset
Random jitter will include low probability events that have a major influence of the overall bit error rates for a channel
Statistical methods allow the full random jitter distribution to be predicted from the results of simulating a channel for a comparatively short number of bits
The figures on the right show the statistical separation of random jitter from the combination of deterministic jitter and random jitter and the subsequent extrapolation of a worst case BER plot
Other statistical methods such as improved importance sampling can achieve a similar result.
Instruments used to do hardware validation of multi-Gbps channels use similar statistical analysis to predict BER from a finite data sample
Jitter Analysis
Worst Case BER Plot

## Slide 11: Observations on circuit and system co-simulation
Circuit and system co-simulation allows the behavior of multi-Gbps channels to be modeled to a very high level of accuracy
This includes the accurate modeling of random jitter and the prediction of its effect on the overall BER
It is important to note that there are many sources of random jitter
As an example, just a few sources of random jitter present in the transmitter include:
    Thermal noise
    Jitter in the system clock,
    Jitter inherent in the clock multiplier PLL design and noise introduced into it from the reference planes
    Although this analysis of circuit and system co-simulation concentrates on driver and receiver modeling, it is also essential to also accurately model the interconnect over the full range of frequencies used for signaling.
In particular, vias and breakouts if not designed appropriately, will severely compromise channel reliability.
    3D EM modeling is generally required
    Decomposition techniques that ignore the significant fringing fields generally produce inadequate results

## Slide 12: Established system level multi-Gbps solutions: StatEye
The StatEye tool was developed during the creation of the Optical Internetworking Forum CEI standard
Original authors: Anthony Sanders and Edoardo Prete of Infineon
Available as open source
Included as an integral part of compliance testing for multiple high speed channel standards
Provides a fast standardized analysis including:
Transmitter FFE and receiver FFE and DFE equalization with automatic optimization
Channel ISI and crosstalk noise from adjacent channels
Random jitter
Computes output pulse spectrum, bathtub curve and eye diagrams for different BER’s

## Slide 13: StatEye Example
Simulation of a representative 10 Gbps channel
Circuit simulation provides the impulse response of the channel, optionally including crosstalk from adjacent channels
The StatEye module calculates the optimal FFE and DFE coefficients
The BER and statistical eye is then generated

## Slide 14: New system level multi-Gbps solutions: IBIS ATM
There is a critical need for standardized system level analysis for multi-Gbps channels
Moving forward, we need the ability to model much more complex drivers and receivers than those presently built into StatEye.
Need transmitter and receiver models that are interchangeable between IC vendors as EDA tools
Require a standard interface so models can be automatically incorporated into simulations
The IBIS Advanced Technology Modeling working group has proposed a system level simulation framework
Well defined programmatic interfaces to algorithmic transmitter and receiver models
Standardized parameter passing
Initial effort has been to develop fast system level solutions suitable for PCB interactive and batch analysis
This framework and standardized model interface promises to solve many of the current system level simulation issues
At this time, reference models are available and their use in simulations demonstrated
Further details of the progress of the working group will be presented in an separate paper

## Slide 15: The Standardized Interfaces of the IBIS ATM Algorithmic Transmitter and Receiver Models
Graphic courtesy of Todd Westerhoff, SiSoft

## Slide 16: Observations on the IBIS ATM multi-Gbps proposal
The IBIS ATM working group proposal offers a flexible solution to system level multi-Gbps modeling
The working group has exhaustively considered alternate approaches and found this to be the most practical
At this time the proposal includes a well defined interface between the simulation framework and the models including parameter passing from the IBIS source file
It took a lot of hard work on behalf of the working group to achieve this result!
A general review of multi-Gbps analysis methods suggests that once the existing proposal is passed it could be further refined:
Standardized information as to which sources of jitter are included in the model
    Allows appropriate statistical post-processing to obtain worst case BER
  A standardized approach for including RTL and other system level descriptions into the receiver and transmitter modules
    Many IC vendors use RTL to synthesize their silicon designs
    The conversion of RTL into ‘C’ or other conventional programming languages would add costs and be a major source of modeling errors
    There appear to be few technical obstacles to this extension

## Slide 17: Conclusion
There are a multitude of approaches to multi-Gbps channel analysis
This paper has presented just a few examples
IC vendors have historically favored a combination of circuit and system level simulation
PCB system designers have a need to do system level channel analysis
The lack of a standard way of deriving system level models that protect IP from the IC vendors internal models is a major issue.
The IBIS ATM working group has made considerable progress in solving this crucial issue