## Slide 1
Sep.14,2007
IBIS Summit in Japan
Guidance of Passive EDA models
JEITA EDA-WG
Hiroaki Ikeda
Japan Aviation Electronics Industry ,Ltd
© JEITA 2007. All Rights Reserved.
Notes: Good afternoon everyone. Firstable, I have to apologize for my poor English.
I was too busy working Jeita activity to study English.
If you don’t understand my English presentation, please ask Mr. Shohji.
He can answer your question in English instead of me.
After this presentation, I will talk about this outline, in Japanese.
I am welcome to have any questions in Japanese. For English speaking, please ask Mr. Shohji. Thank you Mr. Shohji.
Let’s start my presentation now.
Title is guidance of passive EDA models.

## Slide 2
Contents
1. SI Modeling Issues in Passive Devices
2. Guidance of Passive EDA models
3. Summary
© JEITA 2007. All Rights Reserved.
Notes: There are today’s contents.
First section, SI modeling issues in passive devices .
Second , guidance of passive EDA models.
Last is summary.

## Slide 3
Previous report of Interconnect model
We had studied interconnect model in JEITA EDA-WG
last year and reported that simulation and measurements
results were nearly good match. (The EDA models were provided
by component manufacturer, but not specially prepared models. )
Measurement
SimA
SimB
SimＣ
© JEITA 2007. All Rights Reserved.
Notes: This slide shows time domain simulation using EDA models and measurement results last year in EDA-WG.
This graph shows transient waveform. Bit rate is 10Gbps. Horizontal axis is time. Vertical axis is voltage of receiver end.
Red lines is measurement results.
Green, blue, and the Magenta color correspond to simulator A, B, and C
respectively.
These results are good match.

## Slide 4
The EDA models were described by S-parameters and equivalent
circuit. It had no problem with the equivalent circuit models but
the S-parameters had some problem as below.
1. No DC point of S-parameters.
2. Bandwidth limitation. (300KHz-8.5GHz)
3. Each bandwidth of the EDA models might not be the same.
4. Each number of points of S-parameters might not be the same.
5. It is uncertain how S-parameters are measured.
Problem of Passive EDA models
© JEITA 2007. All Rights Reserved.
Notes: I will talk about problem of passive EDA models.
Generally, the EDA models are described by S-parameters of equivalent circuit.
We studied simulation using the EDA models and measurement using actual PCB , therefore equivalent circuit models had no problem.
But S-parameters had some problem as below.
No DC point of S-parameters.
Simulation based S-parameters might include DC point, but measurement based S-parameters do not include DC point.
Because, VAN can not measure DC point of S-parameters. At later slide, I show measuring method of DC point , using TDR and software.
2. Bandwidth limitation. (300KHz-8.5GHz)
3. Each bandwidth of the EDA models might not be the same.
For examples, S-parameter of filter is the bandwidth from 300kHz to 6GHz, S-parameter of connector is the bandwidth from 10MHz to 8GHz,
other device is bandwidth from 0Hz to 4GHz.
4. Each number of points of S-parameters might not be the same.
For examples, S-parameter of filter has 400 points , the connector has 1000points.
5. It is uncertain how S-parameters are measured.
Measuring method of S-parameter is not described in EDA models. And EDA models user can not know that how to measure the S-parameters.
For examples, To measure S-parameter of filter, fixture PCB is needed, must de-embed excessive etching pattern and SMA connector that connects between VNA and fixture PCB.

## Slide 5
Discussion of the EDA Models
In the EDA –WG, We discussed various problems,
and concluded it as follows.
1. Must include DC point of S-parameters .
2. Consider upper limitation of S-parameters for rise time.
3. Not able to standardize bandwidth of S-parameters of
each EDA models in all manufacturer.
4. Not able to standardize number of points of S-parameters
each EDA models as well.
5. Some manufacturers have disclosed measuring method
to the public on Web.
© JEITA 2007. All Rights Reserved.
Notes: We discussed previous problem, and concluded it as follows.
Must include DC point of S-parameters .
I show measuring method of DC point of S-parameters at later slides.
2. Consider upper limitation of S-parameters for rise time.
We have been examining the matter.
3. Not able to standardize bandwidth of S-parameters of each EDA models in all manufacturer.
Because the usage and the purpose are different, it is difficult to standardize bandwidth of each EDA models.
4. Not able to standardize number of points of S-parameters each EDA models as well.
this reason is same as No3.
5. Some manufacturers have disclosed measuring method to the public on Web.
Some filter vender have disclosed measuring instrument measuring method on the Website.

## Slide 6
The method of measuring of DC point of S-parameters
is disclosed to the public.
2. To do transient analysis, it is necessary to consider minimum
bandwidth and number of points of S-parameters.
3. The method of measuring the EDA models is disclosed
to the public.
4.The usage of the EDA models is disclosed to the public.
Guidance of Passive EDA models
© JEITA 2007. All Rights Reserved.
Notes: I explain guidance of passive EDA models in this slide.
1.The method of measuring of DC point of S-parameters is disclosed to the public.
I explain this point at later slide.
2. To do transient analysis, it is necessary to consider minimum bandwidth and number of points of S-parameters.
We have been examining the matter.
3. The method of measuring the EDA models is disclosed to the public.
4.The usage of the EDA models is disclosed to the public.
We have been preparing No3 and No4.

## Slide 7
Measuring method of DC point of S-parameters
DUT
TDR Oscilloscope
Port 1
Port 2
Port 3
Port 4
Port 1
Port 2
Port 3
Port 4
Measurement
I-CONNECT
(FFT)
S11
S21
S31
S41
© JEITA 2007. All Rights Reserved.
Notes: This shows Measuring method of DC points of S-parameters
Left side figure shows measuring instrument.
Upper right side graph shows time domain waveform.
This waveform were measured by TDR oscilloscope.
Lower graph was translated from time domain waveform using software.
Lower graph shows s-parameters.

## Slide 8
Port 1
Port 2
Port 3
Port 4
Flat cable connector and fixture PCB
Port 1
Port 3
Port 2
Port 4
Differential pair line with
solid ground plane
Differential pair line with
meshed ground plane
Device Under Test
Port 1
Port 3
Port 2
Port 4
Flat cable
Filter and Fixture PCB
Port 1
Port 3
Port 2
Port 4
© JEITA 2007. All Rights Reserved.
Notes: These photos are DUTs.
Upper left side photo is flat cable and fixture PCB.
Lower left side photo is differential pair line with meshed ground plane.
Upper right side is differential pair line with solid ground plane.
Lower right side is filter and fixture PCB.

## Slide 9
S-parameters of TDR vs. VNA (DC-20GHz)
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Measured S-parm (VNA)
Measured S-parm (VNA)
Measured S-parm (VNA)
Measured S-parm (VNA)
Flat cable connector and fixture PCB
© JEITA 2007. All Rights Reserved.
Notes: This slide shows measurement results of VNA and TDR.
Bandwidth is form 0Hz to 20GHz.
The DUT used here is flat cable connector and fixture PCB.
Red line is S11 and calculated S-parameters from TDR results.
S11 means return loss.
Green line is S21, blue line is S31, magenta is S41.
S21 means insertion loss. S31 means near end cross talk. S41 means far end cross talk.
Black lines show measured S-parameters using VAN.
TDR and VNA results are good match to 10GHz well.
In the frequency of 10GHz or more, TDR results have ringing.
I think about the reason is that the discontinuance error margin because of the use of FFT occurred.

## Slide 10
© JEITA 2007. All Rights Reserved.
S-parameters of TDR vs. VNA(DC-100MHz)
Flat cable connector and fixture PCB
Calculated S-parm (TDR)
Measured S-parm (VNA)
Calculated S-parm (TDR)
Measured S-parm (VNA)
Calculated S-parm (TDR)
Measured S-parm (VNA)
Calculated S-parm (TDR)
Measured S-parm (VNA)
Notes: This slide shows the result of S parameter from bandwidth 0HZ to 100MHz.
The DUT is the same as previous slide.
TDR and VNA results are good match excluding S11.
Excluding S11, S parameters from DC to 20GHz can be made from S parameters of DC point of calculated TDR and VNA results.
I had questioned the cause of error measurement result of S11 to the measuring instrument vender.
The cause was VNA calibration error.
We measured S parameters using Electric calibration. The performance of E-cal was not good in a low frequency.
We’ll retry using anther E-cal or mechanical calibration kit.

## Slide 11
S-parameters of VAN vs. TDR (DC-20GHz)
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Measured S-parm (VNA)
Measured S-parm (VNA)
Measured S-parm (VNA)
Measured S-parm (VNA)
Differential pair line with solid ground plane
© JEITA 2007. All Rights Reserved.
Notes: This slide also similarly shows the measurement result of TDR and VNA.
Bandwidth is form 0Hz to 20GHz.
The DUT used here is differential pair line with solid ground plane.

## Slide 12
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Measured S-parm (VNA)
Measured S-parm (VNA)
© JEITA 2007. All Rights Reserved.
S-parameters of VAN vs. TDR (DC-100MHz)
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Measured S-parm (VNA)
Measured S-parm (VNA)
Differential pair line with solid ground plane
Notes: The DUT is same as previous slide.
Bandwidth is from 0Hz to 100MHz.
Similarly, the result of TDR and VNA is good ,excluding S11.

## Slide 13
S-parameters of VAN vs. TDR (DC-20GHz)
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Measured S-parm (VNA)
Measured S-parm (VNA)
Measured S-parm (VNA)
Measured S-parm (VNA)
Differential pair line with meshed ground plane
© JEITA 2007. All Rights Reserved.
Notes: These are measurement results of TDR and VNA.
The DUT is differential pair line with meshed ground plane.
Colored lines are TDR results and , black lines are VNA results.

## Slide 14
© JEITA 2007. All Rights Reserved.
S-parameters of VAN vs. TDR (DC-100MHz)
Differential pair line with meshed ground plane
Calculated S-parm (TDR)
Measured S-parm (VNA)
Calculated S-parm (TDR)
Measured S-parm (VNA)
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Measured S-parm (VNA)
Measured S-parm (VNA)
Notes: These are results of DUT same as previous slide
Bandwidth is from DC to 100MHz.
As you can see, S11 result of VNA of 10MHz is also not good in this DUT

## Slide 15
S-parameters of VAN vs. TDR (DC-20GHz)
Common mode filter
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Measured S-parm (VNA)
Measured S-parm (VNA)
Measured S-parm (VNA)
Measured S-parm (VNA)
Filter and Fixture PCB
© JEITA 2007. All Rights Reserved.
Notes: The DUT is filter and fixture PCB.
These are TDR results.
These are VNA results.

## Slide 16
S-parameters of VAN vs. TDR (DC-100MHz)
Filter and Fixture PCB
Calculated S-parm (TDR)
Calculated S-parm (TDR)
Measured S-parm (VNA)
Measured S-parm (VNA)
Calculated S-parm (TDR)
© JEITA 2007. All Rights Reserved.
Calculated S-parm (TDR)
Measured S-parm (VNA)
Measured S-parm (VNA)
Notes: These are results of DUT same as previous slide
Bandwidth is from DC to 100MHz.
In this DUT, S11 result of VNA and TDR are good match.
Because, we changed calibration kit to measure S parameters.

## Slide 17
Summary
1. The problem of the EDA model was shown.
2. The problem of the EDA model was discussed.
3. The method of measuring of DC point of S-parameters
was shown.
© JEITA 2007. All Rights Reserved.
Notes: Summary at last.
1. The problem of the EDA model was shown.
2. The problem of the EDA model was discussed.
3. The method of measuring of DC point of S-parameters was shown.
Today, this was interim report.
I believe someone, not me, can talk about the problem we have been examining at EDA WG next time.

## Slide 18
Gratitude to cooperation in measurement
ATE Service Mr. Sinobu Seki
Mr.Yutaka Honda
JAE Mr. Yuichi Saito
Mr. Tatsuya Syukuzawa
© JEITA 2007. All Rights Reserved.
Notes: I wish to express my gratitude to people who cooperated in the Measurement.
Thank you very much .