## Slide 1: IBIS Quality Activities in JEITA EDA WG
2007/09/14
Yasumasa Kondo
Toshiba Corp.

## Slide 2: What's the "Quality"?
There are many view points for "Quality"….
In the Dictionary, "Quality" means that "standard of something when it is compared to other things like it".
At first, we define the "Quality" in this activity as "standard of simulation result with the device EDA models when it is compared to the measurement result with the device"
But, this definition is very difficult…

## Slide 3: The difference between Meas. and Simulation ?
Measuring
Instrument
Meas.
Difference
Simulation result does not necessary agree with measuring waveform.
What causes this difference??
There are so many reasons…
Actual devices on PCB
DRV
PKG
Distributed
Circuit
PKG
RCV
Simulation
Tool
Sim.
Constructing Circuits and device models
depending on simulator

## Slide 4: What causes this difference?
Measuring
Instrument
Operator
DRV
PKG
Distributed
Circuit
PKG
RCV
SPICE
Model
SPICE
Model
Simulator
Tool
Operator
1.The problem on the Measuring instrument…
2.The operator cannot use Measuring instrument well…
3.SPICE Model accuracy is too poor…
4.Simulation tools with SPICE Model cannot simulate accurately…
5.The operator cannot use Simulation tools well… (including not knowing how to set it up rightly)
1,2 are dependent on the measuring matter,
3,4,5 are dependent on semi-conductor vendors internal.
JEITA doesn't focus on them as the "Quality".
Please, let the semi-conductor vendors do well.

## Slide 5: The next focus on the "Quality"
We redefine the "Quality" in this activity as "standard of the simulation result using IBIS models when it is compared to that using SPICE models"
Unfortunately, even this definition has some problems…
The discripancy between IBIS and SPICE waveform results are caused by not only the different model (IBIS and SPICE) but also different simulators , operators , setting up the environment , viewing tool of waveform depending on the simulator ( ex. time step control for viewing) .

## Slide 6: What should we focus on for the "IBIS Quality"?
DRV
PKG
Distributed
Circuit
PKG
RCV
IBIS
Simulator
Tool B
Operator
Y
When two waveforms are different, can you assert that this differences are caused by the distinctions of IBIS and SPICE model?
Sometimes Yes, actually we don't know.
When semi-conductor vendors receive the question from customers, they must confirm their customer's simulation environment and reappear the customer's problems with same tools…
JEITA consider that "IBIS Quality" is NOT only IBIS Model accuracy itself.
What should we focus on for the "IBIS Quality"?
Output
waveform
Simulator
Tool B
IBIS
Simulator
Tool B
DRV
PKG
Distributed
Circuit
PKG
RCV
SPICE
Simulator
Tool A
Operator
X
Output
waveform
Simulator
Tool A
SPICE
Simulator
Tool A

## Slide 7: JEITA activities for "IBIS Quality" (1)
DRV
PKG
Distributed
Circuit
PKG
RCV
IBIS
Simulator
Tool A
Operator
X
Assumption:
(1)Operator is fixed; besides that operator has the best ability.
(2)Simulator is fixed; besides that simulator can calculate circuits using IBIS and SPICE accurately. ==＞ The difference is caused by the distinction of IBIS and SPICE. What's more assumption: (3)SPICE is accurate
==＞ IBIS is Wrong!!
Output
waveform
Simulator
Tool A
IBIS
Simulator
Tool A
DRV
PKG
Distributed
Circuit
PKG
RCV
SPICE
Simulator
Tool A
Operator
X
Output
waveform
Simulator
Tool A
SPICE
Simulator
Tool A
accurate
accurate
Task Group in JEITA study this…
"IBIS Guide for the Japanese Engineer"

## Slide 8: JEITA activities for "IBIS Quality"(2)
DRV
PKG
Equiv lumped
Circuit
PKG
RCV
IBIS
Simulator
Tool B
Operator
X
Output
waveform
IBIS
DRV
PKG
Equiv lumped
Circuit
PKG
RCV
IBIS
Simulator
Tool A
Operator
X
Output
waveform
IBIS
Assumption:
(1)Operator is fixed; besides that operator has the best ability.
(2)IBIS is accurate
Condition:
(1)Changing "distributed circuit" to equivalent "lumped circuit" using LCR
(2)using same viewing tool (like EXCEL)
Is the simulation result calculated by different simulators same??
→ JEITA studies this matter in the activity.

## Slide 9: The steps in this activity
Considering test circuits for "IBIS Quality". Single / Differential model simple 50Ohm resistance load / with complex transmission line ….
Cooperating with the EDA vendors for this activity
Selecting IBIS Models from JEITA members

## Slide 10
Single-ended
Model type
Input/Output
Voltage range
2.6V
Used V-T data (ramp/waveform)
Golden Waveform

## Slide 11: Evaluation circuit 1
DRV
R = 50 Ohm
Input : PULSE
Frequency=100MHz
PKG
R_pkg = 35.5 mOhm
L_pkg = 4.23 nH
C_pkg = 1.06 pF
PKG
probe

## Slide 12: Result
time adjustment

## Slide 13: Evaluation circuit 2
DRV
C = 3 pF
Input : PULSE
Frequency=100MHz
PKG
Lumped Circuit
10states
probe
PKG
R_pkg = 35.5 mOhm
L_pkg = 4.23 nH
C_pkg = 1.06 pF
R_lump = 5 mOhm
L_lump = 301 pH
C_lump = 120.4 fF
Lumped Circuit

## Slide 14: Result
time adjustment

## Slide 15
Differential Signal
Model type
3-state
Voltage range
3.3V
Used V-T data (ramp/waveform)
ramp

## Slide 16: Evaluation circuit 3
DRV_p
R = 100 Ohm
Input : PULSE
Frequency=100MHz
PKG
probe
DRV_m
PKG
probe
C = 3 pF
C = 3 pF
PKG
R_pkg = 50.0 Ohm
L_pkg = 1.164 nH
C_pkg = 0.207 pF

## Slide 17: Result
time adjustment

## Slide 18: Evaluation circuit 4
DRV_p
R = 100 Ohm
Input : PULSE
Frequency=100MHz
PKG
probe
DRV_m
PKG
probe
C = 3 pF
C = 3 pF
Lumped Circuit
Lumped Circuit
10steps
PKG
R_pkg = 50.0 Ohm
L_pkg = 1.164 nH
C_pkg = 0.207 pF
R_lump = 5 mOhm
L_lump = 301 pH
C_lump = 120.4 fF
Lumped Circuit

## Slide 19: Result
time adjustment

## Slide 20: The next steps in this activity
Considering test circuits for "IBIS Quality". Single / Differential model simple 50Ohm resistance load / with complex transmission line ….
Cooperating with the EDA vendors for this activity
Selecting IBIS Models from JEITA members
Planning the next step…
Simple test circuit
Complex standard
test circuits
Inside JEITA
Over the world
Some EDA vendors
many EDA vendors
In cooperation

## Slide 21: In the future…
This activity is under preparation in present…
JEITA hopes that many simulator vendors take part in our activity.
We must expand and improve the standard test circuits.
Finally, this test circuits will be public inside JEITA members. IBIS users (companies) will make use of test circuits for checking their simulation environments and proceeding operator's ability.
If there is the same activity in EIA, let's join that.
Verification and Validation are very important for ISO9001 in the near future.

## Slide 22
Than you!!