## Slide 1: Understanding and Using ICM Models
Asian IBIS Summit,
Tokyo, Japan,
September 14, 2007
Previously presented on September 11, 2007 at Beijing
Meng, Yubao (yubao@cadence.com)
Cadence Shanghai SPB R&D Center

## Slide 2: Topics
IBIS ICM Model Introduction
  What’s IBIS ICM Model
  What can we do with ICM model
  ICM model structure
ICM model usage scenario
  Black box model
  Package model
  S-parameter support
  ICM swath model support
Summary

## Slide 3: IBIS ICM
IBIS Interconnect Modeling Specification
  ICM stands for InterConnect Modeling
The goal of the ICM
  Provide a better, *more accurate*, non-proprietary interconnect data exchange format
    Faster & accurate simulations
    Smaller file size
ICM history
  Final Draft 1.0 released publicly May 16, 2003
    See IBIS web site under “Connector Info”
  Version 1.1 “ICM” specification approved in July 2005

## Slide 4: What can we do with ICM model
ICM supports models for Connectors, PCB traces and IC-Packages
ICM can include
  RLGC Matrices
  Swaths
  S-parameters

## Slide 5: Section of ICM
Each section is made up of a Single Line Model (SLM) or Multiple Line Model (MLM)
A matrix section is a set of tables of numerical values that represent the electrical relationships between all conductors of a given geometry
S-parameter can be used in place of RLGC matrix

## Slide 6: Section: ICM core unit structure
Sections are basic units and core structure of one ICM model

## Slide 7: ICM model usage scenario
ICM models can be used during pre-layout and post-layout analysis
Two cases are presented
  Case1: In pre-layout simulation, ICM model is used as a Black box model in a topology
  Case2: In post-layout simulation, ICM package model is assigned to a component IBIS model on the PCB

## Slide 8: Example: ICM model of PCI express package

## Slide 9: Device model case (Black box model)

## Slide 10: Case 1: ICM acts as device model (Black box model)
The package ICM model has been wrapped into one black box model, just like one connector

## Slide 11: Case 1: Simulation Results comparing (with/o ICM model)
The pink line represents the simulation with ICM model
The black line represents the simulation without ICM model

## Slide 12: Package model case (associating with its corresponding IBIS model)

## Slide 13: Case 2: ICM acts as package model

## Slide 14: Case 2: Simulation Results comparing (with/o ICM model)

## Slide 15: S-parameter support

## Slide 16: ICM Swath model support
Swath model
  Is a method of using a small matrix section to define a much larger and variable size section of a connector
  This facilitates faster simulation, smaller file size, and makes the creation of a family of connectors much easier

## Slide 17: Expanding the swath matrix
Three methods can be used to expand a swath matrix into a full-sized interconnect
  Centering the Swath around the pins of interest
  Expansion and Centering: Expanding the Swath matrix into a larger sized Swath matrix and centering it about the paths of interest
  Expansion to Full Sized Interconnect: Expanding the swath matrix to the full sized interconnect matrix

## Slide 18: Summary
ICM models offer open, non-proprietary way for vendors to provide interconnect models to their customers
ICM models can be accurate for simulation at higher frequencies *they can include coupling*

## Slide 19
Thanks!