## Slide 1: Issues Combining Buffer and Interconnect Model Formats
Michael Mirmak
Intel Corporation
Chair, EIA IBIS Open Forum
michael.mirmak@intel.com
マイケルマ一マク
インテルコ一ポレ一ション
会長，アイビス
IBIS Summit
Tokyo, Japan
September 14, 2007
(originally presented in Beijing, China on September 11, 2007)

## Slide 2: Legal Disclaimer
THIS DOCUMENT AND RELATED MATERIALS AND INFORMATION ARE PROVIDED "AS IS" WITH NO WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY IMPLIED WARRANTY OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, NON-INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS, OR ANY WARRANTY OTHERWISE ARISING OUT OF ANY PROPOSAL, SPECIFICATION, OR SAMPLE. INTEL ASSUMES NO RESPONSIBILITY FOR ANY ERRORS CONTAINED IN THIS DOCUMENT AND HAS NO LIABILITIES OR OBLIGATIONS FOR ANY DAMAGES ARISING FROM OR IN CONNECTION WITH THE USE OF THIS DOCUMENT.
Performance tests and ratings are measured using specific computer systems and/or components and reflect the approximate performance as measured by those tests. Any difference in system hardware or software design or configuration may affect actual performance.
Intel may make changes to specifications, product descriptions, dates and plans at any time, without notice.
Copyright © 2007, Intel Corporation. All rights reserved.

## Slide 3: An Additional Disclaimer
  The following information is presented as the opinion of one person at Intel. This presentation does not necessarily represent Intel policy, commitments or preferences.
  This is not presented on behalf of the IBIS Open Forum and does not represent the official IBIS Open Forum direction.

## Slide 4: Agenda
  The System Viewpoint
  Buffer Model Formats
  Package and Interconnect Model Formats
  Combining Components into a System
    Summary of Today’s Industry Options
  Steps Toward a Unified Solution

## Slide 5: The Number of Model Formats is Increasing!
IC designers can model buffers in many ways
  Proprietary SPICEs (transistor or behavioral)
  Traditional IBIS (3.2/4.0): table-based
  Verilog-A (for analog-only simulation)
  Verilog-AMS/VHDL-AMS (for mixed-signal)
  Multi-lingual IBIS 4.1/4.2 (IBIS+*-AMS, IBIS+Verilog-A, IBIS+SPICE)
There are just as many ways to model packages & interconnects
  Proprietary SPICEs (lumped-element, RLGC)
  Traditional IBIS (3.2/4.0) for packages
  S-parameters (Touchstone*, CITI*)
  ICM (RLGC or Touchstone*)
… and many ways to combine these models in a system
  Both system and IC vendors simulate system designs
  System sims involve all of the above plus other components
How well do all these options work together?
Notes: IC vendors must support system design customers in a way accessible to them, with familiar tools and formats.

## Slide 6: SI Models - The System View
Board Trace
(Interconnect) Models
Package Trace
(Interconnect) Models
SerDes
Example
TX
Package
VIA
RX
VIA
VIA
VIA
Package
PCB Traces
PCB Traces
Series
Caps
Buffer
(Device) Models
Via
(Interconnect) Models
Models for
Other Elements
… plus the language or format that connects them all

## Slide 7: Buffer Models
“Traditional” table-based IBIS 3.2/4.0 has some advantages
    Standard and enjoys widespread support
    Fast (behavioral) and protects IP
    Supports integration with layout (pin and signal information)
    Free syntax checking (IBIS Golden Parser)
    Reasonably simple to learn
Format has increasing issues
  Best for single-ended, time-domain design
  Frequency-domain support is weak (e.g., C_comp as buffer capacitance)
  Also weak for SerDes: equalization, frequency-dependence, jitter
≠
C_comp
Notes: Data-dependence and single-value C_comp are particular problems;

## Slide 8: “SPICE” vs. “AMS” vs. Algorithmic Models
Several options exist to improve buffer model support
IBIS 4.2 supports Verilog-AMS, VHDL-AMS,
Verilog-A and (Berkeley) SPICE;
IBIS-ATM working on SerDes algorithmic models
SPICE
“AMS”
VHDL-AMS, Verilog-AMS
Mixed-signal (digital + analog)
Also Verilog-A (analog-only)
Industry standard
Languages, not just formats
More familiar to IC designers than SI/system designers
Expensive to implement for lower-cost EDA tools
Languages are not easily cross-ported
HDLs, not general purpose mathematical languages
Can be used behaviorally
Familiar to most engineers
Versions implemented in most EDA tools
Not standard
A format, not a language
Analog-only
Not suited to algorithmic modeling
Still data-driven
Notes: Algorithmic modeling will be covered in-depth during the summit, in other presentations. VHDL-AMS implemented as analog-only has not yet been seen in public. These give enough options to system and IC designers to accommodate most designs.

## Slide 9
Package modeling through IBIS 4.2
[Package] keyword
  Required for each component
  Contains corner values for R_pkg, L_pkg and C_pkg
[Pin] keyword
  Each pin can have a distinct R_pin, L_pin or C_pin value
  Only a single value can be used (no corners)
[Package Model] keyword (also Electrical Board Description)
  Can reference an external file or data within the same .IBS file
  Two methods available currently in IBIS
    Coupled, single-matrix RLC description
    (full, banded, and sparse matrix formats available)
    Uncoupled multi-section description using RLC, length
No coupling for multi-section packages,
no AC loss
Not suitable for today’s fastest designs!
Notes: Note that EBD suffers from the same problems.
High-edge-rates require distributed models, not lumped;

## Slide 10
A typical application
BGA (Ball Grid Array) Package structure
    Bond wire (usually gold): connects die pad to traces
    Package trace: lossy routing path in package FR4
    Via: connects trace to solder ball
    Solder ball: attach point for device to PCB
    Plating par: lossy stub left from separation of packages
die pad
bond wire
package trace
plating bar
solder ball
via
BGA Package Structure
Drawing
courtesy
A. Muranyi
Can we describe this today
using EBD, IBIS or PKG?
Not with adequate loss and coupling.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: SPICE and ICM
Many vendors use SPICE to address IBIS package shortcomings
    Most SPICEs support lumped or distributed RLGC
    Proprietary! One model set may not work across multiple tools
ICM (IBIS Interconnect Modeling specification) available but new
    Standard, with industry support picking up
    A separate specification – no direct connection to IBIS yet
    Not intended to support series components (e.g., series capacitance)
Connector
Stub
Connector
T-line
Described by
[Begin ICM Model]
…
(path description)
…
[End ICM Model]
Described by
[Begin ICM Section]
…
(RLGC or S-params)
…
[End ICM Section]
Connector
Stub
T-line

## Slide 12: Package & Interconnect Formats
IBIS (.PKG)
Per-pin & global lumped data
Distributed single-line data
Single-segment matrices
Industry standard
Standard (2+ formats!)
Frequency-dependent
No pin or other connection
information
S-Parameters
Usually proprietary
Most are frequency-dependent
Can describe lumped or
distributed circuit
May not be supported across
multiple tools
RLGC
Industry standard (ANSI)
Freq.-dependent RLGC matrices
  Loss, coupling, length variation
Link to Touchstone* S-parameter files
Supports images, edge rate information
Modular pinlist, electrical data
ICM 1.1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Combining Models – A Dilemma
Full System Description
Standard
Format
Different
from buffer,
interconnect…
EDA
tool
specific
Standard
Format
Same as buffer,
interconnect…
Do you create a new
description for each
tool? How many
tools?
Can one format
support all elements
of the system?
How many formats
do you have to
learn? How many
do your tools support?
Notes: Some system designers expect full system models, for simulation and analysis, from IC vendors

## Slide 14: SPICE as a Topology Format
Some IC vendors want to provide complete system “decks”
Using proprietary SPICEs is popular, but faces several issues
  Inconsistency in format
    SPICE is not standard! Elements and features vary across SPICEs
    Some analysis functions are proprietary (e.g., S-parameters)
  Lack of expandability
    Users cannot define new elements or analyses, only new subcircuits
  Inconsistency in results
    With different engines, the same model can give different results
  Integration with layout is not automatic
All are barriers to using SPICE
to represent systems across tools
Notes: Full system decks in one tool gets around the analysis/interpretation problem

## Slide 15
Models in Combination
Model Type | Buffer | Interconnect (Board, Package, etc.) | “System Assembly”
Behavioral SPICE | Which SPICE? Frequency-dependent interconnect? Features compatible across several tools? |  | 
Traditional IBIS | Weak C_comp, no core-side information… | No distributed, frequency-dependent interconnect |  not intended
IBIS 4.2 + Berkeley SPICE |  | No distributed, frequency-dependent interconnect |  not intended
IBIS 4.2 + *-AMS |  | Need custom transmission line libraries |  not intended
ICM 1.1 |  not intended |  | No active models, limited series components
Verilog-A |  | Need custom transmission line libraries | 
Notes: <number>
<footer>
<header>
<date/time>
Verilog-A and behavioral SPICE also do not support automatic pin list integration with layout.

## Slide 16: Steps Toward a Unified Solution
Options exist for a unified buffer+interconnect+system format
    e.g., Verilog-A can be treated as a SPICE-like standard analog language
    Standard transmission line libraries would be required to support interconnects under Verilog-A
The IBIS Open Forum is addressing several of these issues
    IBIS-ATM is adding algorithmic model support for SerDes
    IBIS-ICM links are being developed for a future version of IBIS
    A standard SPICE superset syntax has been proposed
      “The 3S Proposal” – http://www.eda.org/ibis/summits/feb07/mirmak.pdf
Market forces will determine the most popular combination
    e.g., IBIS 4.2 + ICM 1.1 + Verilog-A might be possible, but it might not be least expensive or easiest to learn
Make your preferences known!