## Slide 1: IBIS AMI Model Developers Toolbox
Hemant Shah (shah@cadence.com)
IBIS Summit - Tokyo, Japan
September 14, 2007

## Slide 2: Interoperability with < 6Gbps SERDES devices
PCB Design & Simulation env from EDA companies
  Simulators need models
  Models come from IC Companies
Design Environment managed by EDA companies
End users happy with Interoperability
Design Environment managed by EDA Cos
IBIS
Spice
IBIS
Spice
IC Co 1
IC Co 2
Package-PCB Topology
Tx
Rx

## Slide 3: Interoperability with > 6Gbps SERDES devices
SERDES Devices that operate at 6+ Gbps can’t be modeled with current modeling standards in PCB SI space
  FFE/DFE tap coefficient optimization CDR algorithms
  proprietary noise cancellation techniques and post-processing of data
IC companies
  Forced to develop, distribute and support internal tools to model SERDES IP / IO
  Must protect IP
Systems Companies
  Have to learn different tools from different IC companies
  Want interoperability
Rx
DFE, Clock Recovery Algorithms
Tx
FFE Algorithms

## Slide 4: Algorithmic Modeling Proposed Architecture & Flow
Operate on “traditional” CA waveform output with additional algorithms
  SERDES transmitter, receiver models as DLL
Provide framework for customers to evaluate IP in PCB system environment that offers interoperability with other drivers/receivers
Waveform
Processing
New Waveforms
Tx,
Rx DLL
Libs
Tx
Rx
CHANNEL
XTALK CHANNEL
XTALK CHANNEL
Cadence / EDA vendor
IC Co IP

## Slide 5: Integration with PCB Design Environment
Tx + Rx
Channel
+
=
~
channel
~
Xtalk channel
~
Xtalk channel
Rx
Tx
Channel
(Pkg + conns +
PCBs +
Backplane)
Rx
circuit

## Slide 6: Simple API
Init
  Initialize and optimize channel with Tx / Rx Model
  This is where the IC DSP decides how to drive the system: e.g., filter coefficients, channel compensation, …
  Input: Channel Characterization, system and dll specific parameters from config file
    bit period, sampling intervals, # of forward/backward coefficients, …
  Output: Modified Channel Characterization, status
GetWave
  Modify continuous time domain waveform [CDR, Post Processing]
  Input: Voltage at Rx input at specific times
  Output: Modified Voltage, Clock tics, status
Close
  Clean up, exit
Parameters passed by the system simulation platform are in red

## Slide 7: AMI_init
Tx
Rx
CHANNEL
XTALK CHANNEL
XTALK CHANNEL
Pass characterization’
DSP algorithms modify characterization
Internal storage
modified characterization
Model
EDA Platform

## Slide 8: AMI_getwave
Tx
Rx
CHANNEL
XTALK CHANNEL
XTALK CHANNEL
Z-1
Z-1
Z-1
CDR
DSP Filter
Wave_in (vector)
Fltered wave_in
Clock vector
Model
EDA Platform

## Slide 9: What’s in it
Sample Model Rx
  Source code
  Executable on Linux
  Model params file
Tester Program
  Executable on Linux
  Tester config file
Starter model templates
Documentation
Use sample model and tester program to understand the details of the IBIS AMI API
Create your own algorithmic models using starter model templates
Use the tester program to test the model

## Slide 10: Sample Rx Model
Continuous Time Filter (CTF) RX model
  Combination of feed forward and feed backward filter
  Modifies the waveform given a set of coefficients
  Tested for 6.25Gbps data rate
  User configurable forward and backward taps
Parameters needed by the model
  Number of forward taps, Number of backward taps, Coefficients
  Can be provided in a file
To Compile:
  a) gcc -c ibis_ctf_rx.c
  b) gcc -shared -o ibis_ctf_rx.dll ibis_ctf_rx.o
Σ
.
.
.
.
.
.

## Slide 11: CDNS AMI Tester Program
Inputs
  Bit Stream: “(0111100001111)”
    Alternatively, users can specify the number of bits and let tester generate random bits
  Data Rate
  Impulse Response
  DLL to interface to
  Model specific parameters
Outputs
  Wave_out: *voltage-time pairs in txt file* wave form data modified by the Model
  Wave_in: *voltage-time pairs in txt file* Represents waveform passed to the model
  ImpulseResponse: IR data if it is modified by the model (init)
CDNS_AMI_Tester
DLL

## Slide 12: CDNS AMI Tester Program
Usage: CDNS_TESTER [-h] ctf_rx_model
Bit Stream “(10111000)”
AMI File contains:
  - Measurement Delay
    Ignore data for spec delay
  - Model specific parameters
Tester config file contains
  - Information generally set by end users through the EDA platform
    - Data Rate
    - Number of bits
    Input file names
    Output files names
AMI
File
DLL
Wave_in
Wave_out
Wave in
Wave out
.txt files with voltage-time pairs
IR
IR output if modified by init
Params
Tester cfg
File
CDNS_AMI_Tester

## Slide 13: How to get the kit
Cadence AMI Developers toolbox will be available through IBIS web site soon
In the mean time, you can send request for the toolbox to: shah@cadence.com

## Slide 14: Resources
Many presentations on Algorithmic Modeling starting from June 2006 can be found at:
  http://www.vhdl.org/pub/ibis/macromodel_wip/archive-date.html
Updates on the AMI work can also be found in ATM subcommittee updates provided at DAC 2007 and DesignCon 2007 IBIS Summits
  Presentations can be accessed from this page: http://www.vhdl.org/pub/ibis/summits/
To reach the IBIS-ATM group on this topic, you can send email to: ibis-ami-toolkit@freelists.org