## Slide 1: IBIS-ATM Update: SerDes Modeling and IBIS
(Originally presented at the Sept 11th Summit in Beijing)
Presented by: Todd Westerhoff, SiSoft
twesterh@sisoft.com
IBIS Summit
Tokyo, Japan
September 14, 2007

## Slide 2: Typical SerDes Analysis Flow
S
S
S
Network
Characterization
Communication
Analysis
Analysis
TX EQ
RX EQ
With TX, RX EQ

## Slide 3: Why Two Analysis Steps?
Performance
  Communications analysis processes ~ 1,000,000 bits per minute
  SPICE-based analysis throughput is much less
Leverage existing tools and techniques
  Communications methods & algorithms established in other domains
  Equalization and clock recovery well suited to algorithmic description
  Modeling/analysis algorithms are suitable for commercial numerical computation tools

## Slide 4: Network Characterization
Uses circuit analysis techniques to determine network behavior under reference conditions
Characterization can take multiple forms
  Impulse / step / pulse response (time-domain)
  Transfer function (frequency-domain)
S
S
S

## Slide 5: Communications Analysis
Uses circuit characterization data to predict link behavior
Many methods exist – fundamental concepts are similar, but implementation details vary
  Commercial numerical computation tools
  Collaboration efforts (StatEye)
  In-house SerDes vendor solutions
  Commercial systems-level analysis tools
Analysis
TX EQ
RX EQ
With TX, RX EQ

## Slide 6: SerDes Analysis
Serial Links present new analysis requirements
  Model SerDes TX/RX equalization
  Model RX clock recovery behavior
  Predict link behavior over >> 107 bits
  Predict link bit error rate
  Protect SerDes vendor IP
Serial Link analysis often combines analytical methods
  Circuit analysis (network characterization)
  Communications analysis (equalization, clock recovery modeling)
Modeling standards are essential, there can be no interoperable models or analysis tools without them

## Slide 7: IBIS-ATM SerDes Task Group
Goal: SerDes Rx/TX model interoperability
  Multiple EDA platforms
  Multiple SerDes vendor models
  Protect SerDes vendor IP
IBIS-ATM committee participation
  EDA: Agilent, Cadence, Mentor, SiSoft
  Semiconductor: IBM, Intel, Micron, ST-Micro, TI, Xilinx
  System: Cisco
Two part modeling standard
  Characterization model: existing IBIS syntax models TX / RX analog characteristics
  Algorithmic model: equalization, clock recovery, device optimization algorithms

## Slide 8: IBIS-AMI Serial Link Analysis
Transmit Equalizer
Package Interconnect
System Interconnect
Clock
Recovery
Data
Recovery
Serializer
Package Interconnect
Receive Equalizer
TX
RX
Channel & Analog I/O
Linear, Time-Invariant
RX EQ, CDR LTI or non-LTI
TX EQ
LTI or non-LTI
Channel Characterization
(Impulse response)
TX Equalization
TX Optimization
RX Equalization
RX Clock Recovery
RX Optimization

## Slide 9: IBIS-ATM Algorithmic Models
Communication models provided as [binary] code
  Fast, efficient execution
  Protects vendor IP
  Extensible modeling capability
  Allows models to be developed in multiple languages
Standardized execution interface
  Module loading mechanism & call signature
  Data input/output formats
Standardized model parameter interface
  “Reserved parameters” interpreted by EDA platforms
  Model-specific parameters can be exposed to and set by end-users

## Slide 10: IBIS-ATM Algorithmic Models
TX
“GETWAVE”
RX
“GETWAVE”
Stimulus
With TX EQ
With TX, RX EQ
Recovered Clock
Waveform Processing
TX
“INIT”
RX
“INIT”
Channel Impulse Response
With TX EQ
With TX, RX EQ
Model Setttings
Model Settings
Impulse Response Processing
Model Settings
Model Settings

## Slide 11: Executable (DLL) Call Arguments
Init (impulse response processing)
  Bit time
  Number of waveform samples per bit
  Number of crosstalk aggressors
  Channel impulse response(s)
  Model parameters and values
  Pointers to free memory, data return area
Getwave (waveform processing)
  Input waveform(s)
  Pointers to data return area
    Equalized waveform
    Clock times
    Optimized parameters

## Slide 12: Model Parameters
Additional data passed between executable model & simulator:
Model-specific parameters
  Allow IP vendors to define data required for / provided by a specific model
  Defined parameter declaration and usage format
    Allows end-users to set and display model-specific data
Reserved parameters
  Predefined parameter list used by EDA tools to alter analysis flow
  Allows models to tell EDA platform what data the model does/doesn’t provide

## Slide 13: IBIS-ATM Status
Original proposal submitted by Cadence & IBM
  Current version authored by Cadence, Mentor, SiSoft
First draft of BIRD approved by IBIS-ATM task group for prototype model & EDA platform development
  Prove interoperability & refine proposal before bringing back to IBIS Open Forum
Subcommittee work, presentations & BIRD available on-line:
  http://www.vhdl.org/pub/ibis/macromodel_wip/
Public TX/RX models, modeling “toolkits” will be available

## Slide 14: Next Steps
 | Preliminary approval by IBIS-ATM subcommittee
 | Complete BIRD documentation
 | Develop sample models & prototype EDA integration; demonstrate interoperability
Target: Sep 2007 | Refine BIRD based on prototype experience
Target: Oct 2007 | Bring to IBIS-ATM task group for final approval
 | Bring BIRD to IBIS Open Forum for approval
 | Incorporate BIRD into updated IBIS specification