## Slide 1: IBIS Modeling for High Speed Designs
Dr. Lynne Green
April 2004
lgreen22@mindspring.com

## Slide 2: Overview
Morning:
  IBIS Specification and IBIS Models
  Validation Methodology
  Common Problems and Solutions
Afternoon:
  High-speed modeling techniques
  Differential buffer models
  Package models

## Slide 3: Acknowledgements
IBIS training materials
  Arpad Muranyi, Intel Corp.
IBIS Summit Presenters
  Luca Giacotto, Ecole Doctorale EEATS
  Arpad Muranyi, Intel
  Jim Bell, SiQual
  Barry Katz and Doug Burns, SiSoft

## Slide 4: Links
IBIS Web Site
  Home Page http://www.eigroup.org/ibis/ibis.htm
  Specifications http://www.eigroup.org/ibis/specs.htm
    Also Cookbook and BIRDs
  Parser http://www.eda.org/pub/ibis/ibischk3/
  IBIS Summit papers http://www.eigroup.org/ibis/articles.htm
    Also Training Materials
  Quality Checklist http://www.sisoft.com/ibis-quality/checklist/
FREE Model Review Service

## Slide 5: Email Reflectors
ibis-users and ibis
  ibis-request@eda.org
SI-list
  si-list-request@freelists.org
Send email with “subscribe” in the subject line

## Slide 6: AM Overview
IBIS Specification
IBIS File Structure
IBIS Component
IBIS Models
AMS Models
IBIS Model Creation
Validation Methodology
Identifying Problems and Solutions

## Slide 7: The Cost of Modeling Is Relative Compared to cost of systems failure
Images Courtesy NASA/JPL-Caltech

## Slide 8: Creation and Use of IBIS Models In a typical design flow
Circuit design Simulation PCB design
Cell layout Model extraction SI simulation
I/O netlist IBIS file Application
Information gets lost each time data is thrown “over the fence”. One common item is the diode resistance (RS in SPICE).
Notes: The I/O designer, the model maker, the model user
No matter which one you are, you have an impact on model quality.
Both model maker and model user suffer if “bad” models get out there. May need to re-extract model data, redo simulations, or even redo a PCB layout, depending on when model problems are found and fixed.

## Slide 9: IBIS: I/O Buffer Interface Specification
Support fast signal integrity simulation
  Reflections and delays
  Overshoot and ringing
Provide for portable model data
  I/O buffers, series elements, terminators, packages
  SPICE models are not portable
Protect intellectual property
  Protect circuit and process IP
  Models can be built from test-bench data

## Slide 10: EIA/ANSI 656-A I/O Buffer Interface Specification
Version 1.0 in 1993
  Intel, Cadence Design Systems, HyperLynx, Quad Design
Version 4.1 in 2004
  Added support for SPICE and AMS models
  About 30 member companies (Model makers, users, EDA)
ICM (IBIS Interconnect Model) spec in 2003
Publicly available parsers
  IBIS 4.0 and ICM 1.0 parsers available
  IBIS 4.1 parser coming
Notes: The IBIS specification was originally driven by Intel, Cadence, Mentor, and HyperLynx. The intent in IBIS modeling was to protect circuit and foundry IP.
Since model data can be derived from SPICE or bench testing, IBIS models can be built without access to the SPICE model.
An IBIS file describes both components and buffers. An IBIS file may contain more than one component model, and usually contains more than one buffer model.
Note that in common use “Model” may refer to:
  Entire IBIS file
  One Component
  One Buffer model
  One SPICE netlist or process file

## Slide 11: IBIS Model Quality What companies deliver
“A Critique of IBIS Models Available for Download on the Web”, SiQual (IBIS Summit, 2002)
Notes: SiQual studied literally thousands of IBIS models that were available on the web. Although it is hard to see in this picture, 69% of the models has one or more significant errors or warnings.
They also broke out the errors and warnings into common problems. For example, non-monotonic warnings are very common. However, some models failed to even pass the IBIS syntax checks.
The complete paper is available on the IBIS web site.

## Slide 12: Creating IBIS Models
s2ibis2 and s2ibis3 (usually customized)
IBISCenter
Cadence’s Model Integrity
Various other tools available
Text editors (cut/paste values into columns)
Scripts (custom flow)

## Slide 13: The IBIS Specification
Syntax
  Keywords, sub-parameters, tables
Data interpretation
  I-V tables for pullup and pulldown
  I-V tables for power and ground clamps
  V-t tables
Typ/Min/Max ordering
  Different from datasheets
  Package: use Typ, Min value, Max value
  Models: use Typ, Slow/Weak, Strong/Fast
Notes: Unless the model maker understands IBIS syntax and data interpretation, it is difficult to build a high-quality model. A model that does not pass the IBIS parser may not work in some EDA tools for SI analysis.
The IBIS specification also specifies how data is to be interpreted. For example, data columns are specified to be in TYP/MIN/MAX order. This is different from the order in the data sheet. Using the order from the data sheet leads to an incorrect model.

## Slide 14: The IBIS Specification Typ, Min, Max
Min Corner
  Weakest current
  Slowest edge rates
  Lowest voltage
Typ Corner = Nominal
Max Corner
  Strongest current
  Fastest edge rates
  Highest voltage

## Slide 15: The IBIS Specification Typ, Min, Max
Typ = Nominal voltage, temperature, process
CMOS
  Min @ min voltage, max temperature, and slow process
  Max @ max voltage, min temperature, and fast process
Bipolar
  Min @ min voltage, min temperature, and slow process
  Max @ max voltage, max temperature, and fast process
Important note: Temperature is die temperature, not ambient. Important in setting up SPICE simulations.

## Slide 16: IBIS Syntax
Keywords
  Enclosed in [ ]
  Use “ ” or “_”
  Case insensitive
Sub-parameters
Names
  Components, pins
  Signals, models
  Layout tool naming
Comment character
[Component] XYZ
[Manufacturer] Nobody
[Package]
| variable typ min max
R_pkg 0.10 0.05 NA
L_pkg 1.80n 1.0n 3n
C_pkg 0.50p NA 1p
[Pin]
|pin_name signal_name model_name
1 trans1 demo1
B2 GND GND
C1 VCC1 POWER
D2 NC NC

## Slide 17: IBIS Data Interpretation
I_dn = [GND clamp] + [Power clamp] + [Pulldown]
I_up = [GND clamp] + [Power clamp] + [Pullup]
I_rcvr = [GND clamp] + [Power clamp]
Pullup
V-t
Pullup
V/I
Power
Clamp
Package
Circuit
Enable
Logic
GND
Clamp
Pulldown
V/I
Pulldown
V-t
C_comp
Notes: The DC output current form a buffer is the sum of one drive table (pullup or pulldown) plus BOTH clamp tables. This is because the clamp diodes, if they exist, are present whether the output is being driven high or low. When used in tri-state or receiver mode, the drive current is zero, but the clamp currents continue to exist.
Note that you can represent the current of an on-die termination resistor that goes to GND or Power using one of the clamp tables. This will be addressed in the second half.

## Slide 18: IBIS Data Interpretation
Output transitions (dV/dt)
V-t tables preferred
[Ramp] values are used before simulation
[Driver Schedule] for multiple output stages
Pullup
V-t
Pullup
V/I
Power
Clamp
Package
Circuit
Enable
Logic
GND
Clamp
Pulldown
V/I
Pulldown
V-t
C_comp

## Slide 19: IBIS Data Interpretation
Output transitions under loading conditions
Multiple V-t tables are allowed
Often get good accuracy with only one set
http://www.ntu.edu.sg/home/ehntan/glsvlsi.zip
http://www.sigrity.com/papers/ectc96/DOectc96ibis.htm

## Slide 20: IBIS File Structure
Header
Comments
Component data
  One or more components
  Pin, signal, model, package
  Diff pin pairs, etc.
Model data
  One or more models
Notes: The IBIS file structure divides into 3 basic sections.
The Header provides information on the file itself, such as the copyright and legal disclaimers.
Each Component section describes the pinout of a chip. A component can (and usually does) use more than one model.
Each Model section describes one buffer model. A model can be used by more than one component.

## Slide 21: IBIS File Structure Header
IBIS version
  Highest version supported
  First keyword in file
File properties
Date and file revision
Legal disclaimer
Copyright
Documentation
[IBIS Ver] 4.0
[File Name] mine.ibs
[File Rev] 0.0
[Date] April 1, 2004
[Source] Dummy data.
[Notes] This model does not represent any part from any vendor.
[Disclaimer] Demo model.
[Copyright] LGreen

## Slide 22: IBIS File Structure Header
Disclaimer
  Similar to what appears on the datasheet
  Model is not guaranteed for any specific use ...
  Subject to change without notice ...
File revision
  0.x: silicon and file in development
  1.x: pre-silicon file data from silicon model only
  2.x: file correlated to actual silicon measurements
  3.x: mature product, no more changes likely

## Slide 23: IBIS File Structure Components
[Component]
  Can have more than one per file
[Manufacturer]
[Package]
[Pin]
  Every pin on physical package
  Optional package parasitics
  Case-sensitive
  Match pin case to layout
[Component] XYZ2
[Manufacturer] Nobody
|
[Package]
| variable typ min max
R_pkg 100m NA NA
L_pkg 6n NA NA
C_pkg 1.5p NA NA
|
[Pin] signal_name model_name
1 io1 demo1
2 io2 demo1
B2 Vcc POWER
C3 Gnd GND
A10 unused NC

## Slide 24: IBIS File Structure Components
[Diff Pin] pairs
[Series Pin Mapping] pairs
[Model Selector]
[Diff Pin] inv_pin vdiff tdelay_typ tdelay_min tdelay_max
1 2 0.150V -1ns 0ns -2ns
[Series Pin Mapping] pin_2 model_name function_table_group
1 2 CBTSeries 1
[Series Switch Groups]
| Function Group States
On 1 2 /
[Model Selector] Progbuffer1
OUT_2 2mA buffer without slew rate control
OUT_4S 4mA buffer with slew rate control

## Slide 25: IBIS File Structure I/O Buffer Models
Model used by one or more pins
May be used by more than one component
Model name is unique within the IBIS file
17 pre-defined model types
  Input, Output, I/O, 3-state, Open_sink, I/O_open_sink, Open_source, I/O_open_source, Input_ECL, Output_ECL, I/O_ECL, 3-state_ECL
  Series, Series_switch, Terminator
IBIS 4.1 allows external model files
  SPICE 3f5, VHDL-AMS, Verilog-AMS

## Slide 26: IBIS File Structure I/O Buffer Models
Model header
Voltage keyword(s)
Input values
  Logic levels
Output values
  Polarity
  Enable
  Standard load
  [Ramp]
[Model] demo1
Model_type I/O
Polarity Non-Inverting
Enable Active-High
Vinl = 0.80
Vinh = 1.75
Cref = 2p
Vmeas = 1.7
| variable typ min max
C_comp 3p NA NA
[Temperature Range] 50 125 0
[Voltage Range] 3.3 3.0 3.6
|[Pullup Reference] 3.3 3.0 3.6
|[Pulldown Reference] 0.0 0.0 0.0
|[POWER Clamp Reference] 3.3 3.0 3.6
|[GND Clamp Reference] 0.0 0.0 0.0
[Ramp]
dV/dt_r 1.20/0.9n 0.96/1.5n 1.46/0.7n
dV/dt_f 1.60/0.9n 1.38/1.4n 1.78/0.7n
R_load = 50

## Slide 27: IBIS File Structure I/O Buffer Models
 | Power_ Clamp | GND_ Clamp | Pullup | Pulldown | Vinh, Vinl | Vmeas
Input | Opt* | Opt* | No | No | Req | No
Output | Opt | Opt | Req | Req | No | Opt!
I/O | Opt* | Opt* | Req | Req | Req | Opt!
3–State | Opt* | Opt* | Req | Req | Opt! | Opt!
Open_Sink | Opt* | Opt* | No | Req | No | Opt!
I/O_Open_ Sink | Opt* | Opt* | No | Req | Req | Opt!
Open_ Source | Opt* | Opt* | Req | No | No | Opt!
IO_Open_ Source | Opt* | Opt* | Req | No | Req | Opt!
! Required for software timing checks.
* Should not be omitted unless the corresponding input clamping and leakage currents are 0 Amp.

## Slide 28: IBIS File Structure I/O Buffer Models
I-V tables
  [Pullup]
  [Pulldown]
  [Power Clamp]
  [GND Clamp]
Column ordering
Monotonicity
[Pulldown]
| voltage I(typ) I(min) I(max)
-3.6 -1.0e-1 -8.1e-2 -1.2e-1
-1.0 -7.3e-2 -5.1e-2 -7.7e-2
-0.4 -3.5e-2 -2.8e-2 -4.1e-2
-0.1 -9.3e-3 -7.6e-3 -1.0e-2
0.0 0.0 0.0 0.0
0.1 9.1e-3 7.5e-3 1.0e-2
0.6 5.1e-2 4.0e-2 5.7e-2
1.0 7.6e-2 6.1e-2 8.9e-2
2.0 1.1e-1 8.4e-2 1.4e-1
2.5 1.2e-1 8.5e-2 1.5e-1
3.0 1.2e-1 8.6e-2 1.6e-1
3.3 1.2e-1 8.7e-2 1.7e-1
3.6 1.2e-1 8.7e-2 1.8e-1
6.6 1.2e-1 8.7e-2 1.8e-1

## Slide 29: IBIS File Structure I/O Buffer Models
Monotonicity
  Total current
Simulator convergence
  0A at reference voltage
  Range of –Vcc to 2Vcc
  Best points selection
Physical operation
  Feedback effects
  Driver scheduling

## Slide 30: Generating I-V Table Data
I-V tables
  Range is –Vcc to +2Vcc
  Setting DC voltages (Typ/Min/Max)
Note: Currents are considered positive when their direction is into the component.
DUT
Power
supply
Vds
Id
D
E
DUT
Power
supply
Vds
Id
D
E
Pulldown + GND clamp
Pullup + Power clamp
Courtesy of Arpad Muranyi, Intel.

## Slide 31: Generating I-V Table Data
Separating the drive and clamp currents
Fully ON
diode
current
Vgate=0V
Vgate=1V
Vgate=2V
Vgate=3V
Vgate=4V
Vgate=5V
Vgs=0V
Vgs=1V
Vgs=2V
Vgs=3V
Vgs=4V
Vgs=5V
channel
current
Courtesy of Arpad Muranyi, Intel.

## Slide 32: Generating I-V Table Data Extracting I-V tables
I-V table
Separating into Clamp and Drive tables
Changing reference for Pullup and Power clamp tables
Vgs=5V
Vgs=4V
Vgs=3V
Vgs=2V
Vgs=1V
Vgs=0V
Vgate=0V
Vgate=1V
Vgate=2V
Vgate=3V
Vgate=4V
Vgate=5V
Vout
Vtable = Vcc-Vout
Courtesy of Arpad Muranyi, Intel.

## Slide 33: Generating I-V Table Data Separating I-V tables
Separate total currents into:
  Pulldown
  Pullup
  Power clamp
  GND clamp
Make Pullup and Power clamp Vcc-referenced

## Slide 34: Generating V-t Table Data
V-t tables
  Stop time => steady-state voltage reached
  Time step < 0.10 * Tedge
  Data step (Core edge rate) (Typ/Min/Max)
  Specified load (such as 50 Ohms)
  Resistive load. No ringing!
Start and end times
  Start: signal from core into buffer toggles
  End: Just enough for Min signal to settle

## Slide 35: Generating V-t Table Data
Set of four V-t tables
  Data rising, V_fixture=0
  Data rising, V_fixture=Vcc
  Data falling, V_fixture=0
  Data falling, V_fixture=Vcc
Output crosses through Vmeas
DUT
Power
supply
D
E
R_fixture
V_fixture
Vstep
Courtesy of Arpad Muranyi, Intel.

## Slide 36: Generating V-t Table Data Leading time in tables
[Rising Waveform]
| Time V(typ)
0.00s 25mV
0.20ns 35mV
[Falling Waveform]
| Time V(typ)
0.00s 325mV
0.20ns 322mV
[Rising Waveform]
| Time V(typ)
10.00s 25mV
10.20ns 35mV
[Falling Waveform]
| Time V(typ)
10.00s 325mV
10.20ns 322mV
[Rising Waveform]
| Time V(typ)
5.00s 25mV
5.20ns 35mV
[Falling Waveform]
| Time V(typ)
55.00s 325mV
55.20ns 322mV
IBIS 3.2 – Tables could both start at 5ns, or start at different times; tool dependent.
IBIS 4.0 – Tables have the same start time.

## Slide 37: Model Creation Interpreting V-t tables
[Rising Waveform]
| Time V(typ)
0.0ns 25mV
2.0ns 25mV
2.20ns 2mV
....
5.00ns 34uV
20.00ns 34uV
What about those “flat” times
V-t is not changing, but table contains data
Actual internal buffer delays
Different tools do different things!

## Slide 38: Model Creation Ways to Obtain C_comp
Remember the goals
  Signal integrity (reflections, crosstalk)
  Timing (PCB delays)
Things to include in C_comp
  Metal capacitances
  Silicon junction capacitances
There is no one C_comp value!
  Might want to manually adjust value

## Slide 39: Model Creation Ways to Obtain C_comp
Time domain (large signal) effects
  Edge rate
  Voltage step values
Frequency (small signal) effects
  Frequency (small signal)
  DC bias voltage sensitivity
As seen at die pad

## Slide 40: Model Creation Ways to Obtain C_comp
Step response I = C dV/dt
  Using PCB edge rates and voltages
Tuned tank resonance = 1/sqrt(C_comp*Lext)
  Voltage sensitivity
  Narrowband frequency sweep
Zout pole frequency = 1/RC
  Single bias
  Wideband frequency sweep

## Slide 41: IBIS File Structure Recent additions to IBIS
IBIS 4.0 added
  [Receiver Thresholds] : Input threshold parameters
  External Reference] : DC voltage (for pseudo-differential)
  [Add Submodel] : Adds Fall_back
IBIS 4.1 added
  External models and external circuits
  SPICE 3f5, VHDL-AMS, Verilog-AMS

## Slide 42: IBIS File Structure I/O Buffer Parameters
[Model Spec] : Timing sub-params
  Vinh, Vinl
  Vinh+, Vinh-, Vinl+, Vinl-
  S_overshoot_high, S_overshoot_low D_overshoot_high, D_overshoot_low, D_overshoot_time Pulse_high, Pulse_low, Pulse_time
  Vmeas, Vref, Cref, Rref
  Cref_rising, Cref_falling, Rref_rising, Rref_falling Vref_rising, Vref_falling, Vmeas_rising, Vmeas_falling
These override [Model] sub-params
  Vinh, Vinl, Vmeas, Vref, Cref, Rref

## Slide 43: Static and Dynamic Checks
| D_overshoot_time ->| |<-
| | |
D_overshoot_high - - - - - - -+ - - -+
| | oo | Passes - Does Not Exceed Bounds
| |o o |
S_overshoot_high - - - - - - -x o +- - - - - - - - - - - - - - - - - - |
| o o ooooooooo
| o o o
| o o
| o o
| o o
| o o
| o o
| o o Fails -
| o o Exceeds Bounds
| o o | | |
| o o V V V
|oooooo-------------------------------------------o---------o---oooo
S_overshoot_low - - - - - - - - - - - - - - - - - - - - - x +x x x - -
| |o x x
| | o o|
D_overshoot_low - - - - - - - - - - - - - - - - - - - - - + -x x-+
| | x |
D_overshoot_time ->| |<-
Time -->

## Slide 44: IBIS File Structure Series and Series Switch Models
Calling a Series model for the component
Pins must be in [Pin] list
[Series Pin Mapping] pin_2 model_name function_table_group
|
2 3 CBTSeries 1 | Four independent groups
5 6 CBTSeries 2
9 8 CBTSeries 3
12 11 CBTSeries 4
|
32 33 Fixed_series | No group needed
|
[Series Switch Groups] | Function Group States
On 1 2 3 / | Default = ON
Off 4 / | Default = OFF

## Slide 45: IBIS File Structure Series model types
Series and Series_switch models
Series model always On
Series-switch state set at simulation time
  [On], [Off]
  Used with each Series_switch model type
Connect two pads on same component (by pin name)

## Slide 46: IBIS File Structure Series model types
Fixed value series components
  [R Series]
  [L Series], [Rl Series]
  [C Series], [Lc Series], [Rc Series]
R Series
+---/\/\/\/\---------------------+
| |
Pin 1 | L Series Rl Series | Pin 2
<---+---@@@@@@@@---/\/\/\/\----------+--->
| |
| | | |
+---| |---@@@@@@@@@---/\/\/\/\---+
| | Lc Series Rc Series
C Series

## Slide 47: IBIS File Structure Series model types
[Series Current]
  One I-V table
[Series MOSFET]
  Multiple I-V tables
  One table for each Vgs
Table Current
------>
+ Table Voltage -
Pin 1 |---------| Pin 2
<---+ +--->
|---------|
Table Current
------> Ids
Voltage = Vcc – Vs
+ Vds -
Vcc
| g
__|__
----- NMOS
Pin 1 | | Pin 2
<---+ +---> +
d |_____| s
PMOS --+--
| g
GND

## Slide 48: Terminators
[POWER Clamp Reference]
o
|
POWER_ o---o---o
clamp | |
|--o--| \
| | /
| I-V | \ Rpower [Package] Keyword
| | / Subparameters *
|--o--| | |<----------------->|
| |
| | PIN
o-----o-------o-----o-----/\/\/\--@@@@@@---o--o
| |GND_ | | R_pkg L_pkg |
| |clamp | | |
| |--o--| | | |
| | | \ | |
| | I-V | /Rgnd | |
| | | \ \ |
| |--o--| / / Rac |
| | | \ |
| o---o---o / |
| | | |
C_comp === o === Cac C_pkg ===
| [GND Clamp | |
| Reference] | |
o-------------------o----------------------o
|
o
GND
[Rgnd]
[Rpower]
[Rac]
[Cac]

## Slide 49: Advanced Buffer Models
[Model] ExBufferSPICE
Model_type I/O
Vinh = 2.0
Vinl = 0.8
[Voltage Range] 3.3 3.0 3.6
[Ramp]
dV/dt_r 1.57/0.36n 1.44/0.57n 1.73/0.28n
dV/dt_f 1.57/0.35n 1.46/0.44n 1.68/0.28n
|
[External Model]
Language SPICE
| Corner corner_name file_name circuit_name (.subckt name)
Corner Typ buffer_typ.spi buffer_io_typ
Corner Min buffer_min.spi buffer_io_min
Corner Max buffer_max.spi buffer_io_max
|
| Ports List of port names (in same order as in SPICE)
Ports A_signal my_drive my_enable my_receive my_ref
Ports A_puref A_pdref A_pcref A_gcref A_extref
|
| D_to_A d_port port1 port2 vlow vhigh trise tfall corner_name
D_to_A D_drive my_drive my_ref 0.0 3.3 0.5n 0.3n Typ
D_to_A D_enable my_enable A_gcref 0.0 3.3 0.5n 0.3n Typ
|
| A_to_D d_port port1 port2 vlow vhigh corner_name
A_to_D D_receive my_receive my_ref 0.8 2.0 Typ
|
[End External Model]
SPICE 3f5
VHDL-AMS
Verilog-AMS
External Circuit

## Slide 50: Advanced Buffer Models
[Model] Ext_VHDL_Diff_Buff
Model_type I/O_diff
Rref_diff = 100
| typ min max
[Voltage Range] 3.3 3.0 3.6
|
[Ramp]
dV/dt_r 1.57/0.36n 1.44/0.57n 1.73/0.28n
dV/dt_f 1.57/0.35n 1.46/0.44n 1.68/0.28n
|
[External Model]
Language VHDL-AMS
| Corner corner_name file_name circuit_name entity(architecture)
Corner Typ diffio_typ.vhd buffer(diff_io_typ)
Corner Min diffio_min.vhd buffer(diff_io_min)
Corner Max diffio_max.vhd buffer(diff_io_max)
|
| Parameters List of parameters
Parameters delay rate pre-emphasis
|
| Ports List of port names (in same order as in VHDL-AMS)
Ports A_signal_pos A_signal_neg D_receive D_drive D_enable
Ports A_puref A_pdref A_pcref A_gcref
|
[End External Model]
SPICE 3f5
VHDL-AMS
Verilog-AMS
External Circuit

## Slide 51: The System Design Perspective
Digital Electronics
Analog Electronics V, I, R, L, C DC, AC, Time
A2D and D2A
Thermal
Optical
MICROMODELS Electrons
E, H, J, 
Mechanical

## Slide 52: The System Design Perspective
Digital Electronics VHDL/Verilog
IBIS 4.1
Analog Electronics SPICE, IBIS 4.1
A2D and D2A IBIS 4.1
MICROMODELS PISCES
IBIS 4.1
IBIS 4.1
IBIS 4.1
IBIS 4.1
VHDL-AMS and Verilog-AMS

## Slide 53: Event-Driven Domain
All changes occur instantaneously
Time of event is pre-determined
Nothing happens between events
When CLK toggles
Wait 2.7nsec
Copy D into Q
Loop;
CLK Q<-D
CLK Q<-D
2.7nsec
2.7nsec

## Slide 54: Analog Domain
Changes occur continuously
KVL and KCL solved at each time step
Derivatives and integrals used
Idc = IS * (exp(Vj/$vt) - 1)
Iac = Cj * ddt(Vj)
Iout = Idc + Iac
Iout
Time

## Slide 55: Interactions Between Domains
Changes in one affect the other
Analog section must converge
  Before and after interaction
When Iout crosses 0 rising
Toggle Q
Loop;
Iout
Time

## Slide 56: Interactions Between Domains
Changes in one affect the other
Analog section must converge
  Before and after interaction
Inew = d2a(Q) * Iout
Inew
Time

## Slide 57: Example: Ideal LED Model Such as an indicator light
module led(p, n, ps);
inout p, n; output ps; electrical p, n, ps; real I_in;
// ideal led current and linear optical power
analog begin
// diode current
I_in = exp(V(p,n)/$vt) - 1.0;
I(p,n) <+ I_in;
// optical output power at 0.5mW/mA
V(ps) <+ 0.5*I_in;
end
endmodule

## Slide 58: Example: Optical Fiber Model
Analog section of fiber model
analog begin
// power transfer function
// units conversion, since alpha is power loss in dB/km
loss = NA*NA * exp(-ln(10)*alpha*length*1e-3/10);
p_out <+ V(p_in) * loss;
// pulse spreading
V(pout) <+ laplace_zp(p_out, {1}, {-D_sigmaLambda*length,0});
// Input current does not matter, so use 0.
I(p_in) <+ 0;
end

## Slide 59: Addressing Common Problems A Validation Methodology
Parse to check syntax (ibischk3, ibischk4)
Examine parameters
View tables graphically
Other data checks
Simulate
Release for design use
Close the loop
Notes: This methodology can be easily integrated into any PCB design flow.
Incoming QA can save the design team days of troubleshooting a design.
Getting the model make to do validation up front is even better, but no reason to skip QA.

## Slide 60: AMS Validation Methodology
Verify pin order and parameters
Otherwise the same as before:
  Visually check parameters
  Other data checks
  Simulate
  Release for design use
  Close the loop
Notes: This methodology can be easily integrated into any PCB design flow.
Incoming QA can save the design team days of troubleshooting a design.
Getting the model make to do validation up front is even better, but no reason to skip QA.

## Slide 61: Validation Methodology in Design Flow
During buffer design
  I/O operation compared to I/O interface requirements
  First IBIS model for test board designers
Final buffer design
  IBIS models generated and validated
  IBIS and package models released
Silicon back from fab
  IBIS models validated against hardware
  Buffer and package models updated
Notes: This methodology can be easily integrated into any PCB design flow.
Incoming QA can save the design team days of troubleshooting a design.
Getting the model make to do validation up front is even better, but no reason to skip QA.

## Slide 62: Validation Methodology in Design Flow
Understanding what is expected
  Simple CMOS buffers
  More complex buffers
Viewing data
  Visual checks
  Graphical checks
Reporting problems
  And fixing them whenever possible
Notes: This methodology can be easily integrated into any PCB design flow.
Incoming QA can save the design team days of troubleshooting a design.
Getting the model make to do validation up front is even better, but no reason to skip QA.

## Slide 63: IBIS Tables: Graphical View [Power Clamp] and [GND Clamp]
-Vcc
2 Vcc
Large Current
Voltage
Notes: Clamp diodes are typically used for ESD protection. The two clamp currents are opposite in sign.
The clamp diodes turn on about 0.7 Volts from the respective rail. Because they have a small series resistance, the curves appear nearly linear at large currents. Note that each clamp voltage is measured relative to that clamp’s rail.
A clamp table’s currents may be non-zero even for V>0, if the table represents a termination resistor.

## Slide 64: IBIS Tables: Graphical View [Pullup] and [Pulldown]
Small Current
Voltage
Monotonic slopes
Flat slopes
-Vcc
2 Vcc
Notes: The Pullup and Pulldown tables have a classic shape, similar to the I-V curves for bipolar and MOSFET devices. The Pullup and Pulldown currents are opposite in sign.
Note that the slope is nearly constant as the curve passes through the origin, and the curve becomes flat at higher voltages.
Advanced I/O designs may not follow this classic curve.

## Slide 65: IBIS Tables: Graphical View [Rising Waveform] and [Falling Waveform]
Voltage
Time
Flat slope
Vmeas
Notes: The Rising and Falling Waveforms are often non-monotonic. Feedforward through the gate-drain capacitance causes the output to change before the transistor has fully turned on.
Once the transistor has turned on, the output is pulled to its final voltage. The initial and final voltage values dependent on the parameters V_fixture and R_fixture and C_fixture.
Normally, these waveforms are generated with C_fixture=0. This is because the typical load is a transmission line that looks more like a resistor that a capacitor.

## Slide 66: Common Problems Power and GND clamp tables
Little or no power clamp current
Current >100A (even 1e18 Amps!)
Table does not cover –Vcc to +2Vcc
Large Current
Voltage
-Vcc
2 Vcc
Notes: Common problems, common solutions.
No power clamp, or power clamp currents of nA. If there is no power clamp, then this is reasonable. However, if there is a power clamp, then there was a problem in extracting the model.
Large current is typically below 100A. More current than that will burn out the clamp diode. Excessive current indicates that the diode’s series resistance was not included in the diode’s SPICE model.
The tables should cover the full range of –Vcc to 2Vcc. This is particularly important if the clamp current is not exactly 0A above 0V.

## Slide 67: Common Problems Pullup and Pulldown tables
Non-monotonic tables can lead to DC convergence problems
Tables do not cover –Vcc to +2Vcc
-Vcc
2 Vcc
Small Current
Voltage
Notes: Common problems, common solutions.
Most models available today have non-monotonic tables. Sometimes, this is simply due to the numeric resolution used in creating the model, whether from SPICE or bench measurements. A good test of non-monotonicity is to view the curves, and see if the non-monotonic regions are visible.
In this example, there are two non-monotonic regions. The one on the left is caused by incorrect subtraction of the clamp currents, usually caused by the numeric resolution of the extraction software. Since the simulator will sum the currents back together, this is not a physical problem so much as a numeric problem.
The non-monotonic region on the right represents a real problem, since it is not caused by extraction problems. In fact, for some loads, there can be physically metastable operating points. The physical circuit may experience oscillations; in the simulator, these may be disguised as convergence problems.

## Slide 68: Common Problems Pullup and Pulldown tables
Double counting of clamp currents
Incorrect subtraction of clamp currents
  I_pdn = [GND clamp] + [Power clamp] + [Pulldown]
  I_pdu = [GND clamp] + [Power clamp] + [Pulldown]
-Vcc
2Vcc
I_pdn Current
Voltage
Notes: If the clamp tables are not zero, and the same currents also appear in the pullup or pulldown tables, then it is possible the currents have been double-counted.
The only time the clamp currents should appear in the pullup and pulldown tables is when the buffer is an Output that can not be tri-stated. If the buffer can be used as a receiver, then the clamp tables are needed to correctly predict the loading seen by a received signal.

## Slide 69: Common Problems Not enough points in transition region
Courtesy of Cadence Design Systems
Notes: What problems do you see here?
The V-t curves actually look nice, although a shorter end time could have been used.
If you were to look closely at the transition regions, you would notice that there are less than 10 points. A better model would have more points in the transition region and fewer outside the transition region.

## Slide 70: Common Problems Use a “Best points” algorithm
Courtesy of Mentor Graphics/HyperLynx
Notes: What problems do you see here?
The V-t curves actually look nice, although a shorter end time could have been used.
If you were to look closely at the transition regions, you would notice that there are less than 10 points. A better model would have more points in the transition region and fewer outside the transition region.

## Slide 71: Common Problems Rising and Falling V-t tables
AC endpoint (DC point does not match I-V load line)
One loadline point for V_fixture=Vcc, one for V_fixture=GND.
I_fixture = V - V_fixture R_fixture
V at loadline with R_fixture
V @ I_fixture
Voltage
Time
-Vcc
2 Vcc
Current
Voltage
V_fixture R_fixture
V_fixture
Notes: The Rising and Falling tables are not required to start at Time=0.
One of the most common problems in V-t tables is a mismatch between the endpoints in the V-t tables and the equivalent I-V points for the load R_fixture.
A number of things can cause this. The most common problem is an early end to the V-t table.
There are two ways to check the endpoint values. The IBIS parser uses the IBIS loadline to obtain the DC value. Another method is to calculate the current based on the V-t endpoint and locate the DC voltage point for the same current. In the figure, there is a mismatch between the loadline point and the endpoint of the V-t curve.

## Slide 72: Common Problems Rising and Falling V-t tables
End slope not flat
Tables not starting at same time
Excessively long V-t tables
Not enough points in the transition region
Output does not cross Vmeas
Voltage
Time
Notes: Common problems, common solutions.
If the end slop is not flat, then the data was not collected for a long enough time. This sometimes happens because the SPICE simulation stopped converging, or the end time was set too soon.
Any offset in timing between Rising and Falling tables may be caused by actual differences in the internal buffer circuits, or by differences in how the SPICE netlist was created. To make sure it is completely clear, the tables should all start at the same Time value.

## Slide 73: Common Problems Rising and Falling V-t tables
Signal fails to settle (not simple Rload)
Notes: Common problems, common solutions.
If the end slop is not flat, then the data was not collected for a long enough time. This sometimes happens because the SPICE simulation stopped converging, or the end time was set too soon.
Any offset in timing between Rising and Falling tables may be caused by actual differences in the internal buffer circuits, or by differences in how the SPICE netlist was created. To make sure it is completely clear, the tables should all start at the same Time value.

## Slide 74: Simulation Validation with your EDA tool!
Courtesy of Cadence Design Systems
Notes: The acid test is running an actual simulation, and comparing simulation results with what you would expect.
In this model, the simulation can be checked for the “DC” levels at the beginning and end of each transition, as well as the transition time. Note that rising and falling transition times should match the times given for the [Ramp] parameter.

## Slide 75: Addressing Common Problems A Validation Methodology
Identifying problems quickly takes experience
Identifying problems easier with good tools
Fixing problems requires judgment calls
  When in doubt, talk to the model maker!

## Slide 76: Addressing Common Problems A Validation Methodology
Parse to check syntax (ibischk3, ibischk4)
Examine parameters
View tables graphically
Other data checks
Simulate
Release for design use
Close the loop
Notes: This methodology can be easily integrated into any PCB design flow.
Incoming QA can save the design team days of troubleshooting a design.
Getting the model make to do validation up front is even better, but no reason to skip QA.

## Slide 77: Addressing Common Problems A Validation Methodology
Cadence IBIS model validation webinars
http://www.cadence.com/webinars/webinars.aspx?xml=Modeling
http://www.cadence.com/webinars/webinars.aspx?xml=Modeling2
Other links with IBIS papers
http://www.teraspeed.com
http://www.specctraquest.com, http://www.allegrosi.com
http://www.eigroup.org/ibis/articles.htm

## Slide 78: PM Overview
High-speed modeling techniques
Differential buffer models
On-die terminations
Interconnect Models

## Slide 79: High-speed Modeling Techniques
Datasheet information
  Pin and model assignment
  Operating parameters: Vih, Vil, Vmeas, etc.
  Single-ended and differential pins
Buffer characteristics
  Transistor-level simulations (HSPICE, Spectre, Eldo)
  Test bench measurements
  Programmable buffer options

## Slide 80: High-speed Modeling Techniques Pin/Model Assignment
[Pin]
| Pin name Model Name
D1 IO_1 | Single-ended I/O
DD1 IO_1 | Differential I/O, non-inverting
DD2 IO_1 | Differential I/O, inverting
4 In1 | Diff input, non-inverting
5 In1 | Diff input, inverting
6 In1 | Single-ended input
9 GND | Ground pin #1
10 GND | Ground pin #2
11 POWER | Power Pin #1
12 POWER | Power Pin #2

## Slide 81: High-speed Modeling Techniques Pin Relationships
[Diff Pin] inv_pin vdiff tdelay_typ tdelay_min tdelay_max
DD1 DD2 NA -1.0ns 0ns 0.1ns
4 5 150mV NA NA NA
[Series Pin Mapping] pin_2 model_name function_table_group
4 5 Rser1 1 | Series Resistor, always ON
DD1 DD2 MOS1 1 | Series Resistor, two values
|
[Series Switch Groups] | Function Group States
On 1

## Slide 82: High-speed Modeling Techniques Pin Association for SSN
| For SSN analysis
[Pin Mapping] pdn_ref pup_ref gnd_cl_ref power_cl_ref
DD1 9 11 9 11
DD2 9 11 9 11
D1 9 11 9 11
4 10 12 10 12
5 10 12 10 12
6 10 12 10 12

## Slide 83: High-speed Modeling Techniques Dual-voltage buffers
Dual-voltage I/O operation
  Do Vcc_core and Vcc track?
  Where is level shifting done?
SPICE: 8-corner vs. 16-corner vs. 32-corner
  Factor of 2 for each independent variable
  Vcc, Temp, N_process, P_process, Vcc_core, ...
  Which combinations are “min” and “max”?
Use those “min” and “max” in Spice-to-IBIS

## Slide 84: Overview
High-speed modeling techniques
Differential buffer models
On-die terminations
Interconnect Models

## Slide 85: Differential Signals
Non-inverting pin signal
Inverting pin signal
Differential signal
Common mode signal

## Slide 86: Differential Signals Timing Relationships
It does not matter what causes the shift
  Anything that shifts signal in time or voltage
  Driver skew, routing skew, crosstalk, etc.
Voltage shift
Time shift

## Slide 87: Differential Signals LVDS Example
Ideal LVDS switching
1.4V
1.2V
1.0V
+0.2V
-0.2V

## Slide 88: Pseudo-Differential Signals
Single Buffer
Single trace to route
Receiver referenced to Vext
More sensitive to crosstalk
Sensitive to bounce in Vext
Vext

## Slide 89: Paired-differential Signals
Inverting and non-inverting buffer pair
Better than single-ended differential
  Reduces crosstalk sensitivity
Data is inverted
IBIS assumes independent buffers
  Independent voltages and currents
  Slew rise/fall not required to match
  Put driver slew in V-t tables or in tdelay, but not both

## Slide 90: Model Creation Differential I-V tables
No package when generating buffer tables
Differential driver
  Complementary current
DUT
Power
supply
D
E
DUT
Power
supply
D
E
Vds
Id
_Id
Vds
Id
_Id
Pulldown + GND clamp + Power Clamp
Pullup + GND Clamp + Power clamp

## Slide 91: Model Creation Obtaining V-t tables
V_step at core edge rate
Without terminators
  If represented separately in the IBIS model
Four tables
  D=Low, V_fixture=Vlow
  D=Low, V_fixture=Vhigh
  D=Hi, V_fixture=Vlow
  D=Hi, V_fixture=Vhigh
DUT
Power
supply
D
E
Vstep
R_fixture
V_fixture
R_fixture
_______V_fixture

## Slide 92: LVDS Model Example
Ideal LVDS operation
400 mV differential mode
1.2 V common model
100  termination

## Slide 93: LVDS Model Example V-t tables
V-t tables needed for DC operating point
Timing between rising and falling edges
Timing relative to core data signal
Many ways to include differential terminator
  Termination current in I-V tables
  Termination current using [Series Current]
  Termination current using [Series MOSFET]
  Termination in package model

## Slide 94: LVDS Model Example
LVDS IBIS Models @ 1.25GHz
  Douglas Burns, SiSoft
  Used for next two slides
  Intentional time offset in plots
Capabilities and limitations of IBIS models
IBIS Summit http://www.eda.org/pub/ibis/summits/jun02
burns.zip: LVDS IBIS Models @ 1.25GHz (.ppt)
burns.pdf: Douglas Burns, Steven Coe, and Kevin Fisher, Signal Integrity Software (SiSoft)

## Slide 95: Accurate LVDS IBIS Model @ 1.25GHz SiSoft presentation (time shift to make it easier to see matching)
SPI4 interface: 1.25GHz, target pad, VDDQ=2.375

## Slide 96: Effects of Changing VDDQ SiSoft presentation (same time shift)
SPI4 interface: 1.25GHz, target pad, VDDQ=2.325,
Model generated w/VDDQ=2.375

## Slide 97: LVDS Model Example
Model made at one V_common
  Not valid if V_common changes
Implications
  Hard to select Min, Max conditions
  Submodels for different V_common
Reality is V_common changes with bit pattern
IBIS was never designed to handle this!

## Slide 98: LVDS Model Example The IBIS 4.1 solution
IBIS 4.1 approach
  SPICE 3f5, VHDL-AMS, Verilog-AMS
LVDS model in SPICE
  Requires both circuit and process data
  Multiple NDAs could be required
LVDS models in an AMS language
  Behavioral equations
  Use of both digital and analog information
    Such as medium-term value of V_common
  Can include effects not addressed in IBIS 4.0

## Slide 99: Overview
High-speed modeling techniques
Differential buffer models
On-die terminations
Interconnect Models

## Slide 100: On-die Terminators
High-speed differential termination
Inside the package and bond wire
Minimizes reflection effects at the receiver
Fixed or variable resistance

## Slide 101: Representing On-die Terminators Many ways to do this
Use “terminator” model type
Use [Series Current]
Use [Series MOSFET]
Include current in one of the clamp tables
Include in a SubModel
  Termination can be disabled
  Value can be changed

## Slide 102: Representing On-die Terminators Tradeoffs
Ease of model creation
Linear or non-linear load
Actual FET or pass-gate load
Support in a specific simulator

## Slide 103: Representing On-die Terminators Terminator in buffer method
Do this within the [Model]
To insert a resistor to GND
| variable R(typ) R(min) R(max)
[Rgnd] 100ohm 80ohm 120ohm
To insert a series resistor
| variable R(typ) R(min) R(max)
[R Series] 8ohm 6ohm 12ohm

## Slide 104: Representing On-die Terminators Series current between pins
Define series connection for component
[Series Pin Mapping] pin_2 model_name function_table_group
5 Rser1 | Series Resistor, always ON
Define (linear or non-linear) resistance using I-V table
[Series Current]
| Voltage I(typ) I(min) I(max)
-5.0V -3900.0m -3800.0m -4000.0m
-0.7V -80.0m -75.0m -85.0m
-0.6V -22.0m -20.0m -25.0m
-0.5V -2.4m -2.0m -2.9m
-0.4V 0.0m 0.0m 0.0m
5.0V 0.0m 0.0m 0.0m

## Slide 105: Overview
High-speed modeling techniques
Differential buffer models
On-die terminations
Interconnect Models

## Slide 106: Module and Board Models
EBD model
  Simple transmission lines (L/R/C per unit length)
  Lumped R, L, C elements
  IC pin attachment
PKG model
  Adds RLC matrices for coupled lines
ICM (connector and interconnect) model
  Supports S-parameters and multi-section RLGC matrices

## Slide 107: High-Speed Interconnect Models Tool support
EBD and PKG models
  Check with ibischk3 / ibischk4
IBIS Interconnect (ICM)
  Check with icmchk1
[External Circuit]
  New in IBIS 4.1
EDA tools connect package to component
  Pkg Pin == IC Pad == Buffer

## Slide 108: High-Speed Interconnect Models
IBIS lumped package
  R_pkg, L_pkg, C_pkg
  Parameters are required
  Values can be set to 0.0
  Can define Typ/Min/Max values
Real packages are transmission lines
  Impedance
  Delay
R_pkg L_pkg
C_pkg

## Slide 109: High-Speed Interconnect Models
Lumped parameters
  Only valid at slow edge rates
Use of default parameters
  Can override on a pin-by-pin basis
R_pkg 0.12 0.10 0.15
L_pkg 2n 1n 3n
C_pkg 3p 2p 5p
[Pin]
! Pin name Model Name R_pkg L_pkg C_pkg
D1 IO_1
DD1 IO_1 0.090 6n 7p

## Slide 110: High-Speed Interconnect Models
Package Override Order
[Package Model] > [Pin] values > *_pkg
R_pkg 0.12 0.10 0.15
L_pkg 2n 1n 3n
C_pkg 3p 2p 5p
[Pin]
! Pin name Model Name R_pkg L_pkg C_pkg
D1 IO_1
DD1 IO_1 0.090 6n 7p
[Package Model] pkg1

## Slide 111: High-Speed Interconnect Models
Package model location
In same file as IBIS file using [Package Model]
  *.ebd, *.pkg
In a separate file
  File name based on package model type
  *.ebd, *.pkg, *.icm
  Must be in same directory
If files are in different directories
  Move one of the files

## Slide 112: High-Speed Interconnect Models
Lumped vs. distributed parameters
  Using same parameters could result in different characteristics
  *_pkg are lumped parameters by definition
Distributed parameters
  Values of parameters change (do not use lumped parameters)
  Use EBD or Package or Interconnect
  Valid at both fast and slow edge rates
Bond wires must be included somewhere
  Usually in the package model parameters

## Slide 113: High-Speed Interconnect Models Comparison
 | EBD | PKG | ICM
Lumped | Yes | Yes | Yes
Coupled traces | No | Yes | Yes
Matrices | No | Yes | Yes
S-parameters | No | No | Yes
Y-connects and dangling connects | Yes | No | Yes

## Slide 114: High-Speed Interconnect Models
Characteristics of high-speed packages
  Lumped model is not adequate
  Crosstalk between package traces
EBD models for packages
  Does not model any coupling
PKG models for packages
  Transmission line models
  RLC matrices for coupling
ICM models for packages
  Both matrix and S-parameters (Touchstone format)

## Slide 115: High-Speed Interconnect Models EBD Example
[Path Description] IN0
Pin 1 | Edge of Module
Len=0 L=0.2n R=10m / | Lumped Connector trace
Len=2.1 L=2.0n C=12.0p / | Units in inches
Fork | A Tee-connection
Len=40 L=0.15n C=1.2p / | Units in mils
Len=0 L=0.6 R=0.02 / | Bond wire to U0 Pin2
Node U0.2
Endfork
Len = 0 C = 0.8p / | Socket to U1 Pin2
Len = 0 L = 3.7n / |
Len = 0 R = 90m / |
Node U1.2

## Slide 116: High-Speed Interconnect Models EBD Example
[Path Description] IN2
Pin 2
Len = 1.5 L=6.0n C=2.0p / | Trace on module
Len = 0 R=50 / | Series terminator
Len = 0.25 L=6.0n C=2.0p / | Trace between R and package
Node R2.1 | Series resistor pack
Node R2.2
Len = 0.25 L=6.0n C=2.0p / | Trace between R and package
Node U0.4
[Reference Designator Map]
| Ref Des File name Component name
U0 good1.ibs nonesuch
U1 good1.ibs nonesuch
R2 r10k.ibs A_10K_Pullup

## Slide 117: High-Speed Interconnect Models PKG Example
[Inductance Matrix] Full_matrix
[Row] 1
3.04859e-07 4.73185e-08 1.3428e-08 6.12191e-09
1.74022e-07 7.35469e-08 2.7321e-08 1.33807e-08
[Row] 2
3.04859e-07 4.73185e-08 1.3428e-08 7.35469e-08
1.74022e-07 7.35469e-08 2.7320e-08 1.74022e-07
[Capacitance Matrix] Sparse_matrix
[Row] 1
1 2.48227e-10
2 -1.56651e-11
[Row] 2
2 2.51798e-10

## Slide 118: High-Speed Interconnect Models ICM Model Using [Tree Path Description]
A B C
Port1 >----------< >-----------< >-----------< Port2
|stub1 |stub4
|stub2 |stub4
|stub1
Section Mult=1 A
Fork
Section Mult=1 stub1
Section Mult=1 stub2
Section Mult=1 stub1
Endfork
Section Mult=1 B
Fork
Section Mult=2 stub4
Endfork

## Slide 119: High-Speed Interconnect Models ICM Model Using [Nodal Path Description]
1 2 3 4 5 6 shell 6-pin male mini DIN (computer)
| | +-+ +-+ | | +---+
| | | | | | | | | | Section
2 | 3 | 4 | 6 | shell | 6-pin female DIN (keyboard)
2 3 4 6 shell 6-pin female DIN (mouse)
[Begin ICM Model] PS2_splitter
ICM_model_type MLM
|as found on http://www.hardwarebook.net/adapter/
| userinput/ ps2keyboardygateway.html
[Nodal Path Description]
Model_nodemap PS2_splitter_Computer_side
N_section (C1 C3 C4 C5 Cs C2 C3 C4 C6 Cs
K2 K3 K4 K6 Ks M2 M3 M4 M6 Ms) Mult=1 RLGC_matrix_10x10
Model_nodemap PS2_splitter_Keyboard_side
Model_nodemap PS2_splitter_Mouse_side

## Slide 120: High-Speed Interconnect Models ICM Model Using [ICM S-parameter]
S-parameters in Agilent’s Touchstone format
IBIS Touchstone draft
  http://www.eda.org/pub/ibis/connector/touchstone_spec11
[ICM S-parameter]
File_name sample.s4p | any name and extension Port_assignment
|Port Node
1 A1
2 B1
3 A2
4 B2

## Slide 121: Summary
Not all features are supported by all vendors
  IBIS 4.1 parser is not yet available
  Support is limited for IBIS 4.1 and ICM
  Check with your EDA vendor
IBIS 3.2 and critical IBIS 4.1 features are better supported
  Model validation
  SPICE-to-IBIS
  S-parameters
  IBIS with SPICE and VHDL/Verilog-AMS

## Slide 122: Summary
Creating a high-speed model is non-trivial
More than one way to do things
  On-die termination
  LVDS simulation
True differential drivers are hard to model
  IBIS 4.0 assumes no signal coupling between buffers
  IBIS 4.1 approach offers greater flexibility
Package models have become more important
  Critical designs will move to ICM models over time