## Slide 1: Basic SI and Timing Budgets for Common Clock Designs
Todd Westerhoff
toddw@cadence.com

## Slide 2: Common Clock Data Transfer
Hold
D0
D1
D2
D0
D1
D2
Clock
Driver
Driving
Receiving
Tco
Flight Time
Setup
1
2
3
4
Notes: This diagram shows the basic timing relationships for a bus that uses a common clock signal and transfers data on the rising edge of the clock. Data is sent out on the bus by the driving device on the first clock edge and latched into the receiving device on the subsequent clock edge. There are four items to consider for each data transfer cycle:
1) First, the clock edge that initiates the transfer of data. For simplicity’s sake, we’ll assume that this happens at time 0.
2) The delay between the time that the driving device sees the initial clock edge and when it puts valid data onto the bus. We’ll call this Tco, or the “Time from Clock to Output”.
3) The time it takes the data to travel the net and settle at the receiver’s input. This is called the flight time, and is always measured with respect to the driver’s delay into the standard load. We’ll expand on this later.
4) There are at least two timing criteria the signal must satisfy in order to not violate timing at the receiver’s input. First, it must not arrive sooner than the receiver’s hold time after the initial clock, or a hold time violation will occur. It must also not arrive later than the receiver’s setup time before the second clock edge, or a setup violation will occur.
These relationships give rise to the minimum and maximum permissible flight time for the net, as we will see in the following pages.

## Slide 3: Defining Tco
Din
Clock
Output Buffer
Internal Logic
RL = 50 
Clock
rises
t = 0
Vmeas
Tco
Load for Tco measurement
(from databook)
Tco = time from clock rise to Vmeas into test load
Notes: Tco is a datasheet parameter that specifies the overall device’s delay.
It is always specified into a given test loading condition; it would have
no meaning otherwise.
Because we will use Tco in determining the timing budget for data
transfer, it is imperative that the same loading condition be used for
buffer delay measurement in the SI tools.

## Slide 4: Components of Tco
Din
Clock
Output Buffer
Internal Logic
RL = 50 
Clock
rises
t = 0
Vmeas
Tco
Internal delay = from clock rise to the point where the
output begins to switch
External (buffer) delay = how long the buffer takes to drive the reference load to Vmeas
Notes: If we were able to break open the device and probe internally, we could
actually talk about two components of Tco. The first is the delay from
the clock trigger (Tco always specifies a reference point on the clock
input as t=0) to when the output buffer actually begins switching. This
is the internal delay of the device, and can be negligible or significant,
depending on the part. On devices with internal PLLs, the internal
delay can actually be negative, but that’s another story …
The external delay (also called the buffer delay, or Time to Vm) is the
length of time it takes the output buffer to drive the reference load to
the measurement voltage (commonly called Vmeas or Vm).

## Slide 5: For Signal Integrity Purposes ...
Output Buffer
Internal Logic not
modeled
RL = 50 
Buffer
switches
at t = 0
Vmeas
Buffer Delay
Load for Tco measurement
(from databook)
Notes: Here’s where it begins to get interesting. Signal integrity simulators
commonly only model the output stage of the device, and not the internal
logic delay. So, the output buffer begins switching at t=0, instead
of some time later (namely, the internal logic delay after t=0).

## Slide 6: It’s all in the Math ...
Driving
Receiving
Tco
Flight Time
1
2
3
4
???
t = 0
Notes: So now we’re faced with a dilemma. How do we get the right delays from
the clock input of the driving device to the data input of the receiving one?
The SI simulator switches the driver’s buffer at t=0, which will not give us the
correct overall delays at the receiver’s input.
We could calculate (but not physically measure) the driving device’s internal delay
as (Tco - buffer delay), and then add that to the receiver timings we observed in the
simulation waveform to get the corrected receiver input timings.
OR, We could define the “Flight Time” as the “difference between the simulated
delay and the buffer’s delay into the standard load”. This is actually the standard
practice. At first, this approach often seems counter-intuitive; after all, why not just
have the simulator display the correct timings?
The benefit to this approach is that it lets us use the Tco number in the timing
equations without adjusting it, and as we shall see, there are other factors that need
to be taken into account anyway.
How is the flight time measured by SI tools? The “buffer delay” is determined by
simulating the package device’s output into the reference load. The buffer delay is
then subtracted from the simulated data to arrive at the correct values for Flight Time.

## Slide 7: Clock Jitter
Clock
Driver
Cycle 1
Cycle 2
Clock Jitter occurs when the clock period varies from one period to the next
  Usually caused by PLL instability in the clock driver
Jitter increases / decreases the clock period, decreasing the effective clock cycle
Notes: One thing we need to factor somewhere in our system analysis (although
not necessarily in our SI analysis) is clock itter, both in terms of the clock
generator and any internal PLLs in the devices on the net.
Clock jitter is the variation in the clock period from cycle to cycle. It has
the effect of making the data transfer cycle appear longer or shorter,
depending on the cycle to cycle variations.

## Slide 8: Clock Skew
D0
D1
D2
Clock
Driver
D0
D1
D2
t = 0
t = 1
t = 2
Occurs when different devices see the clock transition at different times
Increases / decreases the apparent clock cycle. Depending on which devices are driving / receiving
Reduces the effective clock cycle
Notes: Another factor is clock skew, or the difference in time between when the
different clock inputs on the net detect the clock signal. This can make
the data transfer cycle appear longer or shorter, depending on which
device is driving and which is receiving.
Clock skew is the difference in time between when the clock inputs
detect the clock signal -- it is an electrical issue, not merely a physical
one. While differences in the driver to receiver net lengths will certainly
contribute to clock skew, differences in receiver thresholds, capacitive
loading, and poor signal quality will also contribute to the problem.

## Slide 9: Crosstalk
When traces are close together, a change in current flow in one trace will cause current to flow in an adjacent trace
Aggressor traces induce currents in adjacent victim traces
Changes in current flow only occur during the aggressor’s rising and falling edges
Crosstalk
No Crosstalk
Notes: … and then there’s crosstalk. This is an entire subject in and of itself,
but there are a few things we should point out here. First, crosstalk
only occurs when signals are changing state ...

## Slide 10: Impacts of Crosstalk
Crosstalk causes switching noise to appear on victim traces that would otherwise be quiet
Crosstalk degrades the system noise budget when it occurs between signals that are not part of the same signal group
Since crosstalk only occurs when drivers are switching, the magnitude of crosstalk between bus bits is usually not important
Aggressor
Victim
Crosstalk-induced noise
Notes: … and then we should point out that there are different aspects of crosstalk
that are important to consider.
First (and most commonly) if two signals are unrelated, then any noise that
one signal induces on another is probably undesirable, and must be accounted
for in terms of a noise budget. For instance, any noise that any signal
induces on the system clock is probably a bad thing.
But, if we’re talking about a bunch of bits that switch together on a bus, we
really don’t care how much noise they induce in each other while they’re
switching. We only care that the noise settles out before the signals are
sampled. The magnitude of switching noise between bus bits is often
irrelevant and possibly misleading.

## Slide 11: Crosstalk - Impact on Bus Timing
Crosstalk between adjacent bus bits affects edge speed (and therefore flight time)
Denser routing makes better use of board space, but at the expense of larger variations in flight time
Pre-layout crosstalk analysis helps the designer make the best tradeoff between routing density and signal integrity
Even Mode
Reference
Odd Mode
D0
D1
D2
D0
D1
D2
D0
D1
D2
D0
D1
D2
Notes: … but what we do care about is the fact that the timing of the bus bits will
actually shift depending on what the adjacent bits are doing. Consider the
diagram above. In the middle case (reference) the middle bit switches
while the adjacent bits are quiet. Then, depending on whether the adjacent
bits switch in the same (Even mode) or opposite (Odd mode) direction, the
middle bit will either switch faster or slower.
The reason for this is that a change in current in a conductor induces a
opposite change in current in an adjacent conductor. So, when the bits
switch in opposite directions, the magnetic fields actually reinforce each
other, and cause the bits to switch faster. When the bits all switch in
the same direction, the magnetic fields interfere with each other and
cause the bits to switch slower.
So we now have another factor to account for in bus timing - the timing
shift caused by crosstalk.

## Slide 12: Bus Clock Cycle Budgeting
For each Driver  Receiver path:
  Tflightmax < Clock Period - Driver(Tcomax) - Skew - Jitter - Crosstalk - Receiver(Setup)
  Tflightmin > Receiver(Hold) - Driver(Tcomin) + Skew + Crosstalk
Driver(Tcomax)
Tflightmax
+/- Jitter
+/- Skew
Receiver(Setup)
< Clock Period
Driver(Tcomin)
Tflightmin
+/- Skew
> Receiver (Hold)
+/- Crosstalk
+/- Crosstalk
Notes: … and in the end, it all comes down to equations. First, we should note that
the timing requirements for each driver to receiver path will be unique, because
of the unique combinations of driver delays and receiver requirements.
How do we determine the minimum and maximum flight times for each driver
to receiver path? Pretty simply, actually. We usually start be defining the
desired bus frequency (say, 100 MT/s), which yields a 10nS clock period.
We know that Tco(max) + FlightTime(max) + Clock Jitter + Clock Skew +
Crosstalk Shift + Receiver Setup must be less than the Clock Period (or the
receiver’s setup constraint would be violated). Then we solve the equation
for FlightTime(max)
We also know that Tco(min) + FlightTime(min) - Clock Skew -
Crosstalk shift must be greater than the receiver’s hold time (Remember
that Skew and Shift are defined as +/- numbers, so we add or subtract
them as appropriate to get the worst case condition). Note that Jitter is omitted from this equation, because both the driver and receiver are referencing the same clock edge, instead of subsequent edges. Then, as before, we solve the equation for FlightTime.
You can enhance these basic equations to incorporate additional factors
like timing margin (a good idea), timing shifts due to power fluctuations,
etc. … the big trick being knowing how to validate those budgets during design.

## Slide 13: Common Clock Bus Example
Intel Pentium-Pro reference design
Processor/Chipset Bus (GTL+, 66 MHz)
Intel GTL+ Design Guidelines
Notes: … so let’s walk through one quick example. This is based on information
we pulled from Intel’s WWW site and is not necessarily up to date, but
serves as a useful illustration.
In this case, we’ll look at the GTL+ timings between the Pentium Pro
processor and the 440FX chipset. The bus is targeted to run at
66 MT/s.

## Slide 14: Defining Device Timing
Timings taken from “AC (dynamic) Specifications” sections of Intel datasheets
Most datasheets available via WWW
Important parameters
  Clock  Data Valid for GTL+ Bus
  Setup / Hold requirements for GTL+ signals
  PLL Jitter (if spec’d)
Pentium Pro
440FX (timings from 440LX)
Notes: The first step is to go find Tcomin, Tcomax, setup, hold and any internal
PLL jitter data supplied for each chip. In this example we used the
440LX chipset timings for the 440FX, simply because Intel didn’t have
the 440FX data posted on the WWW (the chip isn’t new enough).

## Slide 15: Determining Flight Times
Tflightmax = 4.50 ns
Tflightmin = 0.45 ns
Notes: We combined the part data from the datasheet with our budgets for various
timing specifications. The initial budgets are either based on other
specifications (like the jitter of the clock generator) - or educated guesses,
which can be modified later if needed.
In any case, we picked the following budgets:
Clock period = 15.15 ns (66 MHz)
Clock Skew = 200ps
Clock Jitter = 400ps
Crosstalk Shift = 400ps
We then used Microsoft Excel (it’s really a CAD tool, Microsoft just doesn’t
promote it that way) to create the timing equations and embed them into this
presentation (really, we’re not kidding).
Finally, we decided to us the “worst case times” (biggest MinFlight, smallest
MaxFlight) for our budgets for simulation. You can also use the different
delays depending on the path, it’s a only matter of preference and
bookkeeping.

## Slide 16: A Few Words on Device Models
Quality problems are still common in SI models (unfortunately)
  Check & question model quality!
  Check buffer delay calculations
Different models support different purposes
  Pre-layout models (min / max package parasitics only)
  Post-layout models (detailed per-pin parasitic data)
“Lumped” parasitics are not accurate enough for some purposes
Data from IBIS model with per-pin lumped parasitics
Notes: … so now we’re back to where we started, which is models. Hopefully, we’ve
illustrated how basic timing equations are used to determine bus cycle timings,
and where buffer delays fit into the larger scheme of things.
Hopefully, we’ve also illustrated that without having the test load data
specified in your models, the chances of getting accurate timing information
from your SI analysis is [dramatically] reduced. It’s also worth double-
checking the buffer delay data supplied, just to be thorough.
Note that different SI models may be supplied for different purposes. Models
that have different parasitics on every pin represent the actual package
characteristics, while other models are meant to specify on the best and
worst case characteristics for each class of device pin.
Finally, it’s worth knowing the details of how your simulator calculates and
manages the buffer delay data. Some tools store this data as part of the
buffer model (which can be problematic if different pins with different
parasitics use the same buffer), while other tools store the buffer delay
data on a per-pin basis. Some tools will calculate the buffer delay for you,
others may not. In any event, understanding the details of how all the
terms in the timing equations are handled is key to successful system analysis.