## Slide 1: Matrix Parameters in Touchstone
Bob Ross, Teraspeed Labs, USA
bob@teraspeedlabs.com
Hybrid Asian IBIS Summit (Tokyo)
Tokyo, Japan
November 14, 2023

## Slide 2: Agenda
Goals
Touchstone V1.0, V1.1, V2.0, V2.1 differences
Reference Impedances (resistances)
n-Port matrices (S, Y, Z)
  Conversions and mathematics
2-port matrices (H, G)
  Conversions
Conclusion

## Slide 3: Goals
Show features for an upcoming Touchstone Version 2.1 document
Show conversion mathematics for different per-port reference impedances (resistances) for TSCHK2.1 parser development
Note, reference impedance will be designated as reference resistance since complex references are not supported

## Slide 4: Touchstone Version 2.1 Document
Touchstone V1.0 and V1.1 formats in the Version 2.1 Document
  No keywords, content based on strict formatting rules
  V1.0 supports a single port reference resistance in the option line beginning with # … R <r value> …
  V1.1 supports per-port reference resistances at the end of the option line with # … R <r1> <r2>… <rn> syntax
  S-parameter matrices are defined based on the option line resistance entries
  All other matrices are NORMALIZED regardless of option line entries. For example, if R = 50.0 W, then z1,1 = 1.0 in V1.0 when the measured value is z1,1 = 50.0 W
  Per-port reference resistances are already supported by several EDA tools (but they may have different formats)

## Slide 5: Touchstone Version 2.1 Document
Touchstone V2.0 and V2.1 rules in the Version 2.1 Document
  Keyword based and [Version] 2.0 or [Version] 2.1 is required
  V2.0 and V2.1 have identical matrix data
  S-parameter matrices remain unchanged from V1.0 or V1.1 and are based on the reference resistance entries
  Y-, Z-, H-, G-parameter matrices are UN-NORMALIZED (sensitive to reference resistor values) – as if measured directly in ohms or siemens (mhos)
  [Reference] keyword lists the reference resistors
    Values can wrap (unlike in V1.1 where all values are on a single options line)

## Slide 6: TSCHK2.0 Conversion Syntax Between V1.0 and V2.0
tschk2 –canonical
tschk2 -canonical <options> FILE Shortcut for -canonical-v2.
tschk2 –canonical –v2
tschk2 -canonical-v2 <options> FILE Checks the file, sending error and warning
information to stderr, and writes a valid file
to stdout in Touchstone v2 format.
tschk2 –canonical –v1
tschk2 -canonical-v1 <options> FILE Checks the file, sending error and warning
information to stderr, and writes a valid file
to stdout in Touchstone v1 format, if possible.
A tschk2.1 parser should support the V1.1 and V2.1 conversions

## Slide 7: Notation
Z (normalized), ZU (un-normalized)
Y (normalized), YU (un-normalized)
H (normalized), HU (un-normalized), 2-port only
G (normalized), GU (un-normalized), 2-port only
R <r1> <r2>… <rn> per-port reference resistors
R <r> for a single reference resistance

## Slide 8: General N-Port Z Matrix Conversion
José Schutt-Ainé, ECE 546, Lecture 13, Scattering Parameters, Slides 28-29, Spring 2022, http://emlab.illinois.edu/ece546/Lect_13.pdf
Formulas are restated using the notation in this presentation
k = diagonal , … , ] are based on power wave per-port normalization between incident and reflected waves (b = Sa)
Z = (I + S)(I – S)-1 (normalized to r = 1; I = unit matrix)
ZU = k (I + S)(I – S)-1 k = k Z k
Multiplication by the diagonal matrix k produces the terms =

## Slide 9: Illustrating zui,j Term Calculation
= = = =

## Slide 10: N-Port Matrix Conversions
ZU  Z Z  ZU
= = /
YU  Y Y  YU
= / =
In V1.0 and V2.0, R <r> is used if
V2.0 cannot be converted to V1.0 if

## Slide 11: 2-Port H-Parameter Conversions
HU  H
=
H  HU
=

## Slide 12: 2-Port G-Parameter Conversions
GU  G
=
G  GU
=

## Slide 13: Conclusion
Differences in Touchstone V1.0, V1.1, V2.0, V2.1 are shown
New V1.1 option line syntax is shown
Transformations between normalized and un-normalized matrix data are given for different per-port reference resistances
TSCHK2.1 parser developer should add the per-port reference matrix transformation capability