## Slide 1: IBIS/XML – One step further
Atul P. Agarwal
IBIS Summit
Jan 2002

## Slide 2: Outline
Why IBIS/XML
What has been demonstrated
What needs to be done
Issues

## Slide 3: Why IBIS/XML
Separation of content from presentation
More structured representation
New computing paradigms
  Web Services

## Slide 4: Presentation info in the IBIS spec
“A line of the file may have at most 80 characters”
“If RLC parameters are available for individual pins, they can be listed in columns 4-6 under keyword [Pin]. “
“The state line is terminated with the slash '/', even if it extends over several lines to fit within the 80 character column width restriction.”
Notes: These are examples of presentation related information intermingled with model related information in the IBIS spec. Of course, these are there to make the file more readable to humans which in turn makes it more difficult to be automatically processed by a program. Therefore, a clear separation between presentation and content is required.

## Slide 5: XML advantages
Simple
Standard
Structured
Textual
  The Fine print
    XML documents can be very large
    XML documents are difficult to read easily (need tools)
Notes: An XML representation is relatively simple. It comprises a set of nested begin end tags. XML is now a world standard. The current version being. XML representation is structured, it can be represented using a formal grammar and thus parsers can automatically validate the XML representation against the grammar. Finally, XML representation is textual so it is readable by humans, making it easier to debug if required.
However, the XML documents can become very large and occupy a lot of disk space. The are not easy to read and follow in a traditional text editor, need tools to read and process them.

## Slide 6: Web Services
a new breed of Web applications
self-contained, self-describing, modular applications
can be published, located, and invoked across the Web.
other applications (and other Web services) can discover and invoke the deployed service.
built on XML/HTTP

## Slide 7: Web Services Support Components
SOAP (remote invocation)
UDDI (trader, directory service)
WSDL (expression of service characteristics)
XLANG/XAML (transactional support for complex web transactions involving multiple web services)
XKMS (XML Key Management Specification) - ongoing work by Microsoft and Verisign to support authentication and registration

## Slide 8: Processing an XML Document
XML DOC
DTD
Style Sheet
Processing Agent
XML Parser
Parse Tree
Rendering Agent
3rd Party App
Display Device
Notes: The above figure shows a typical XML flow. The XML document file is parsed by an XML parser. The parser may check for well formedness (ie, it obeys the XML specific rules) or may be validating (verifies the document against a DTD). The parser internally builds up a Parse tree which can be processed by a third party application or rendered using XLST onto a display device.

## Slide 9: IBIS/XML Flow demonstrated
Text Ibis Model
Ibis C parser
IBIS XML
Model
Third party application
Validating Parser
IBIS DTD
Third party application
Transformed IBIS XML document
Parser/XSLT processor
Basic
XSLT
(Level1)
Presentation XSLT
(Level2)
IBIS model Presentation
XSLT processor
Notes: This is proposed IBIS/XML flow. The C parser acts like a gateway into the system such that IBIS/XML files are generated using it. This guarantees that the files have passed the basic checks. These XML files can then be processed by validating or non-validating parsers which now act as the front end to third party applications. XML files may also in turn be generated by third party applications. When it is required to render these files to a human readable form, the files are transformed by a two stage process. During the first stage, the IBIS/XML files are converted to an intermediate XML format appropriate for further rendition. In the second stage, the Intermediate file is rendered to the target device by an appropriate device specific XSLT transform.

## Slide 10: IBIS/XML for Pin
<Pin>
<Pin_name_section>
<Pin_name Max_len="5"> A11 </Pin_name>
</Pin_name_section>
<Signal_name_section>
<Signal_name Max_len="20" > wrn </Signal_name>
</Signal_name_section>
<Pin_model_name_section>
<Model_name Max_len="40"> BT2Z50CX </Model_name>
</Pin_model_name_section>
<Pin_package_info_section>
</Pin_package_info_section>
</Pin>
Notes: This is how an IBIS Pin may look like in XML. (The details of the Pin_package_info_section have not been shown to conserve space)

## Slide 11: XSL for Transformation 1
<xsl:template match = "Pin" >
<column width = "5" >
<xsl:value-of select = "Pin_name_section/Pin_name" />
</column>
<column width = "15" >
<xsl:value-of select = "Signal_name_section/Signal_name" />
</column>
<column width = "15" >
<xsl:apply-templates select = "Pin_model_name_section" />
</column>
<xsl:apply-templates select = "Pin_package_info_section" />
</xsl:template>
Notes: The above XSL is used to transform an IBIS/XML file to an intermediate format which organizes data in rows and columns (ie, tabular) as shown in the previous slide.

## Slide 12
java org.apache.xalan.xslt.Process
-IN Sample.xml
-XSL sampleformat.xsl
-OUT format.xml
Notes: The above command invokes the XALAN XML processor to transform the Sample.xml IBIS/XML file to an intermediate XML format (format.xml) appropriate for rendering in various formats after subsequent processing. It uses the sampleformat.xsl XSL file to do so.

## Slide 13: Presentation XML for a Pin
<rowdata>
<column width="5"> A14 </column>
<column width="15"> a[7] </column>
<column width="15"> BT2Z50CX_PU50K </column>
<column width="5"> 35m </column>
<column width="5"> 3.69nH </column>
<column width="5"> 0.48pF </column>
</rowdata>
Notes: This shows the same IBIS data in a format suitable for rendering on a device (text file, display, browser etc). This is more presentation oriented. This XML has been arrived at from the previous one by using XSLT.

## Slide 14: XSL for Transformation 2
<xsl:template match="rowdata“>
<xsl:for-each select="column">
  <xsl:choose>
  <xsl:when test="child::keyword">
  </xsl:when>
  <xsl:when test="child::comment">
  <xsl:apply-templates select="comment" />
  </xsl:when>
  <xsl:otherwise>
  <xsl:value-of select="text()" />
  <xsl:call-template name="do-the-padding">
  <xsl:with-param name="abc" select="text()" />
  <xsl:with-param name="width" select="@width" />
  </xsl:call-template>
  </xsl:otherwise>
  </xsl:choose>
  </xsl:for-each>
</xsl:template>
Notes: This complex looking XSL is used to convert the intermediate Presentation IBIS/XML to a standard IBIS text file. Notice the for-each ad choose constructs. What the above says is that if a “rowdata” tag is matched in the XML file, then for each tag called “column” if there is a child called “keyword” do something, if there is child called “comment” do something else, otherwise use the value of the “column” tag to invoke the template “do-the-padding”.

## Slide 15: Generating the Text Format
java org.apache.xalan.xslt.Process
-IN format.xml
-XSL ibistextformat.xsl
-OUT sample1.ibs
Notes: The above command invokes the XALAN XML processor to transform the format.xml file to a text format IBIS file (sample1.ibs). It uses the ibistextformat.xsl XSL file to do so.

## Slide 16: The IBIS text format
A12 a[0] BT2Z50CX_PU50K 32m 3.45nH 0.46pF

## Slide 17: XML for GND Clamp
<Gnd_clamp_section>
<Comment>
<Comment_char> | </Comment_char>
<Comment_line> voltage I(typ) I(min) I(max) </Comment_line>
</Comment>
<Gnd_clamp>
<voltage> <Number> -3.30000 </Number> </voltage>
<typ> <Number> -11.46380A </Number> </typ>
<min> <Number> -11.71150A </Number> </min>
<max> <Number> 11.40800A </Number> </max>
</Gnd_clamp>
</Gnd_clamp_section>

## Slide 18: Elements vs Attributes
<Gnd_clamp_section>
<Comment>
<Comment_char> | </Comment_char>
<Comment_line> voltage I(typ) I(min) I(max) </Comment_line>
</Comment>
<Gnd_clamp>
<Point> voltage= -3.30000
typ = -11.46380A
min = -11.71150A
max = 11.40800A
</Point>
</Gnd_clamp>
</Gnd_clamp_section>

## Slide 19: What next ?
Standardize on the IBIS XML tags
Standardize on the IBIS XML DTD/XSD
Standardize on an IBIS Presentation XML
Modify the Parser to generate XML

## Slide 20: Issues
XML is an evolving standard
XSLT is complex
DTD cannot capture the complete grammar
  Need XSD (XML schema definition)
Very few validating Parsers

## Slide 21: Useful Links
XML info
  www.w3.org
  www.xml.com
  www.xslt.com
EDA XML
  http://www.oasis-open.org/cover/xmlAndEDA.html
  http://www.zapthink.com/online/acronyms.htm#
In House Info
  http://www.eda.org/pub/ibis/xml/
  http://www.eda.org/pub/summits/jun00/labonte.zip

## Slide 22: Acknowledgments
Bob Ross
  For providing the sample IBIS models
Pallavi Ray & Hriday Ranjan Daga
  For doing all the hard work
Notes: I would like to thank Bob Ross for his help and support; and Pallavi and Hriday of my team for helping me with the research and development.